## Slide 1: Introduction to ATM Air Traffic Control as part of Air Transport System
Fedja Netjasov
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Air Traffic System
2

## Slide 3
Air Traffic means the flying of aircraft (air navigation) through the airspace between the origin and the destination airports, as well as the moving of aircraft on the manoeuvring areas of the airport (runways, taxiways, aprons).
A country or region’s Air Traffic System is complex and involves the following sub-systems:
  Airlines (national, regional, low-cost, charter, cargo, etc.),
  Airports (civil, military, hub, regional, sport, etc.),
  Air Navigation Service Providers (ANSP).
Air Traffic (1)

## Slide 4
Airlines provide a transport service to passengers and goods (cargo) between two airports.
Customers are passengers and goods.
Airports provide a handling service to passengers and goods (cargo), as well as to airlines.
Customers are passengers, goods and airlines.
Air Navigation Service Providers provide the traffic control service to airlines.
Customers are the airlines.
Air Traffic (2)

## Slide 5
Air Traffic (3)
Airport 1
Airport 2
Airport 3
Airport 4
Airline A
Airline A
Airline B
Airline C
Airline C
Airline D
Air Navigation Service Provider

## Slide 6
Air Traffic (4)
Statistical Summary of Commercial Jet Airplane Accidents Worldwide Operations 1959 – 2019, Boeing, 2020

## Slide 7
Air Traffic (5)

## Slide 8
Air Traffic (6)
Sept. 3, 2019
12:00 UTC
https://www.flightradar24.com/airport/beg

## Slide 9: Air Traffic System Elements
Human
Procedures
Equipment
Environment
Air Traffic is a -
Complex
  dynamic
  multi-agent
  - highly distributed
- Socio-technical
- Safety critical
system

## Slide 10: Air Traffic System Elements
Human includes the Air Traffic Controllers (ATCo) and Pilots: their roles and functions in the system (surveillance, communication, navigation), as well as the challenge they manage (workload, situational awareness, fatigue, errors, etc.);
Equipment includes all airborne-based and ground-based equipment and tools used for surveillance, communication and navigation purposes. Also, it includes equipment used for prediction, detection and resolution of conflict situations - ”Safety nets”, and other decision support tools;

## Slide 11: Air Traffic System Elements
Procedures include the set of rules which ATCo and pilots should follow (comply with), using available equipment in all meteorological and traffic situations; eg. aircraft separation rules, rules of communication between ATCo and pilots, etc.
Environment includes all influences on the system which are not controllable (eg. meteorological situation); or are controllable using certain measures (eg. air traffic demand).

## Slide 12: Air Navigation Services
12

## Slide 13: Air Navigation Services (1)
All states, members of ICAO (International Civil Aviation Organization), are obliged to determine, for territories for which they have sovereignty and/or jurisdiction, the airspace in which they will provide Air Navigation Services - ANS.
The states responsible for the provision of ANS in the relevant airspace are required to determine the appropriate body (service) responsible for provision of those services, so called Air Navigation Service Provider - ANSP.
This body could be a specific Agency or Civil Aviation Directorate.

## Slide 14: Air Navigation Services (2)
The main goals of Air Navigation Service provision are:
preventing collisions between aircraft in flight, and between aircraft and the terrain;
preventing collisions between aircraft on the airport manoeuvring areas and obstructions, vehicles and people in their vicinity;
handling of air traffic flows in a manner that allows a regular flow of air traffic;
providing advice and information necessary for safe and efficient flights;
notifying appropriate organisations regarding initiation of search and rescue operation and if, necessary, assisting these organisations.

## Slide 15: Air Navigation Services (3)
Area
Approach
Airport
  ATM - Air Traffic Management services;
  CNS - Communication, Navigation and Surveillance services;
  MET Meteorological services;
  AIS - Aeronautical Information services;
  SAR - Search and Rescue services.

## Slide 16: Air Navigation Services (4)
  ASM – Airspace Management;
  ATS – Air Traffic Service;
  ATFM – Air Traffic Flow Management.

## Slide 17
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com