## Slide 1: Introduction to ATM SESAR programme
Tatjana Bolić
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Outline
The SESAR project overview
SESAR 2020 research programme – approach to innovation cycle
SESAR 2020 research programme – concept and principles
Delivering SESAR Solutions
The future of SESAR?
Note:
  Some material herein adapted with thanks from previous presentations from SJU
2

## Slide 3: The SESAR project – overview

## Slide 4: THE ATM CHALLENGE
2030
2040
2010
2020
~ - 60%
4

## Slide 5: Single European Sky
Key Response
Delay
Traffic
1995
Central Flow Management
Unit
2004
Single European
Sky
2006
SESAR
2019
Airspace Architecture
Study
2009
SES2
2001
9/11
2008
Economic Recession
2010
Volcanic eruptions
2020
COVID-19
5

## Slide 6: SES pillars
The first pillar is based on regulating ANSP performance by means of performance monitoring and strengthening the network management function
The second pillar establishes a single safety framework through the European Aviation Safety Agency (EASA)
The third pillar provides new ATM technologies through the
SESAR project
by defining, developing, and deploying technologies and procedures needed to increase ATM performance
The fourth pillar addresses the management of airport capacity to keep it aligned with air transport capacity
The fifth pillar addresses the human dimension by ensuring that the changes are acceptable to operational staff

## Slide 7: Three phases of SESAR project
Council of the European Union. Council regulation (EC) No 219/2007 of 27 February 2007 on the establishment of a Joint Undertaking to develop the new generation European air traffic management system (SESAR). Strasbourg: Council of the European Union; 2007
The definition phase - was performed by the SESAR Consortium (2005–2008), with the goal of delivering a European ATM Master Plan (MP) by 2008. The purpose of this MP was to define a research, development, and deployment plan for ATM solutions in Europe, with the goal of achieving SES performance objectives
The development phase involves the research, development and validation of the needed ATM solutions, and is managed by the SESAR JU, a public-private partnership established by this regulation. This phase was originally intended to run from 2008 to 2013
In the deployment phase, the validated ATM solutions are to be produced and implemented on a large scale; this phase was planned to take place from 2014 to 2020

## Slide 8: SESAR Joint Undertaking (SJU)
Established in 2007
SESAR1 2008-2014

## Slide 9: The SESAR Joint Undertaking
• SESAR 2020
• 2014-2024
19 industry members
1 unique
public-private partnership
2 founding
members

## Slide 10: SESAR Deployment Manager (SDM)
Deployment phase
Established 2013
Commission implementing regulation (EU) No 409/2013 of 3 May 2013 on the definition of common projects, the establishment of governance and the identification of incentives supporting the implementation of the European air traffic management master plan (text with EEA relevance). Brussels: The European Commission; 2013
•
Manage the implementation of Pilot
Common Projects (PCP)
Commission implementing regulation (EU) No 716/2014 of 27 June 2014 on the establishment of the pilot common project supporting the implementation of the European air traffic management master plan (text with EEA relevance). Brussels: The European Commission; 2014

## Slide 11: SESAR project lifecycle
Vision towards 2035
SESAR 1: 2008-2016
SESAR 2020: 2016-2024
EU-wide deployment Common Projects and individual implementation projects

## Slide 12: THE NEED FOR PERFORMANCE

## Slide 13: SESAR 2020 research programme – approach to innovation cycle

## Slide 14: How does it work
1
2
3
4
5
6
Industrial programme management, with one design authority
All relevant stakeholders are working together
SJU prepares transition to deployment through Master Planning activities
Strong emphasis on demonstrating benefits and building compelling business cases
Validation as much as possible in real operating environments as a preparation for deployment
Airspace users are involved in every stage of the Program
<VGI: put picture of airbus without airline logo>

## Slide 15: SESAR Key Features
The future European ATM system relies on the full integration of airports as nodes into the network. This implies enhanced airport operations, ensuring a seamless process through collaborative decision-making (CDM).
The feature reflects this move towards automation with activities addressing enhanced arrivals and departures, separation management, enhanced air and ground safety nets and trajectory and performance-based free routing.
An optimised ATM network must be robust and resilient to disruptions, including weather. It also relies on having a dynamic, consistent and accurate plan that provides reference information to all planning and executing ATM actors.
The enhancements described in the first three Key Features will be underpinned by an advanced, integrated and rationalised aviation infrastructure, providing the required technical capabilities in a resource-efficient manner. This feature will rely on enhanced integration and interfacing between aircraft and ground systems, including ATC and other stakeholder systems.

## Slide 16: SESAR 2020 RESEARCH PROGRAMME
TRANSVERSAL ACTIVITIES
OPTIMISED ATM NETWORK SERVICES
ADVANCED AIR TRAFFIC SERVICES
HIGH PERFORMING
AIRPORT OPERATIONS
ENABLING AVIATION INFRASTRUCTURE

## Slide 17: SESAR Innovation pipeline
Increasing level of maturity
Three phases of research and development activity within the SESAR 2020 research programme

## Slide 18: SESAR Solution
SESAR Solution represents a change in the way air traffic management is performed
Solutions are new operational concepts, procedures and relevant technologies

## Slide 19
Innovation pipeline

## Slide 20: How to move through the pipeline?
TRL – Technology Readiness Level
V-phases of E-OCVM

## Slide 21: SESAR 2020 - Research Maturity
Exploratory Research
Very Large-scale Demonstrations
Open Calls
Open Calls
1
2
6
7
3
Technology Readiness Level (TRL)
4 5
Industrial Partnership
Fundamental Scientific Research – To TRL1
Thematic Approach
Establish the Science
Engage Universities
Reach outside of ATM
1
6
Application-Oriented Research – To TRL2
Structure aligned to Industrial Research for transition
Industrial Research & Validation – To TRL6
High Performance Airport Operations
Advanced Air Traffic Services
Optimised ATM Network Management
Enabling Aviation Infrastructure
Working in Partnership
6
VLD – From TRL6
High Capacity Airport Operations
Advanced Air Traffic Services
Optimised ATM Network Management
Enabling Aviation
Infrastructure
Engaging the wider Community
TRL6 (V3) Gate
7
2
4 5
3
TRL2 (V1) Gate TRL4 (V2) Gate
Industrial Research & Validation
MATURITY GATE aims at assessing:
the actual maturity of a SESAR Solution
ability to deliver the expected performance
validation approach for the next maturity phase

## Slide 22: SESAR Solution life cycle model
Exploratory Research
Industrial Research
Very Large Demonstration
Industrialisation & Deployment
R&D Topic
Delivered SESAR Solution
R&D Topic
Delivered SESAR Solution
R&D Topic
Delivered SESAR Solution
R&D Topic
Delivered SESAR Solution

## Slide 23: SESAR 2020 research programme – concept and principles

## Slide 24: Trajectory-based operations

## Slide 25: The SESAR Vision

## Slide 26: AUTOMATION SUPPORT
Controller working position tools
Traffic complexity detection and resolution enabling Free Route
Point Merge technics
Enhanced Conflict Alert
Automated surface movement planning and routing
Airport safety nets and routing guidance

## Slide 27: FLIGHT- AND FLOW-CENTRIC OPERATIONS
Flight and flow-centric operations with Initial 4D trajectories
Performance Based Navigation (PBN)
Air/ground Data Communication
User-preferred routing
Extended AMAN

## Slide 28: INTEGRATION OF ALL VEHICLES
Drones, small & large accommodated then integrated
Automated vehicle operations
Space plane & balloon operations
Urban passenger & freight services
Special missions by remotely managed & autonomous vehicles

## Slide 29: SHARING OF INFORMATION
SWIM – System- wide information management
Extended flight plan
Extended Projected Profile & 4D trajectory
MET Information Exchange
Air- ground communication

## Slide 30: INTEGRATED SYSTEMS
Integration of Airport and Network Operations Planning
Seamless Interoperability between European ATM ground systems and essential interoperability world- wide
Air vehicle system and ground system enhanced interoperability
Advanced Short-Term Air Traffic Flow Management measures & Advanced flow management including slot swapping

## Slide 31: VIRTUALISATION
Remote Tower technology & operations across multiple airports and for special purpose operations, including across national boundaries
Virtual centre capability to maintain air vehicle operations and services in exceptional or planned circumstances, including across national boundaries

## Slide 32: AVIATION INFRASTRUCTURE EVOLUTION

## Slide 33: TODAY’s AVIATION INFRASTRUCTURE
1980
1990
2000
2007
1G
64 kbps
10 kbps
2G
x 6
1 Mbps
3G
INTERNET
x 16
100 Mbps
4G
CLOUD
x 100
10 Gbps
5G
x 100
Throughput
Time
VDLM2
ACARS
2018

## Slide 34: INFRASTRUCTURE PRINCIPLES
Safe, Secure and
Resilient Infrastructure
Moving focus from physical assets to delivery of services
Performance Based
and Integrated CNS
Combined Satellite- based, Airborne and Ground-based CNS
Increased Civil-Military
Synergies and Dual Use
Efficient use and long- term availability of suitable radio spectrum
Rationalised
Infrastructure
Increased levels of Connectivity and
Automation

## Slide 35: ATM information sharing using SWIM
A/G Datalink Ground Management
AOC ATM
Airport Airside Operations
Aerodrome
ATC
Approach
ATC
Military
Meteo
Network Information Management
Aeronautical Information Management
Advanced Airspace Management
Air/Ground
Datalink
Ground/Ground
SWIM
En-route /
Data Exchanged
Demand & Capacity data
ATFCM scenario data
Meteo data
Aeronautical data
Flight data
Surveillance data
Sharing information via Providing / Consuming service(s)
Information Services Reference Model (ISRM)
Common data definition
ATM Information Reference Model (AIRM)
SWIM Technical infrastructure
Standards
Standards
Interoperability through standards
Standards

## Slide 36: SWIM definition
SWIM consists of standards, infrastructure and governance enabling the managementof ATM information and its exchange between qualified parties via interoperable services.
Qualified parties
SWIM Infrastructure
Service(s)
Service consumer(s)
Network infrastructure
Standards
Standards
Standards
Standards
SWIM
Enabled Applications
Qualified party
ATM
information
Qualified parties
ATM
information
SWIM
Governance

## Slide 37: WHAT ABOUT SECURITY? CYBERSECURITY IS A MUST!
TODAY
TOMORROW
Multi-stakeholder system of systems
Public networks
Increased use of COTS
Virtual infrastructure
High connectivity
Increased Automation
=
High exposure
High impact
Specific systems and networks
Point to point communication
Physical infrastructure
Low connectivity
Poor Automation
=
Low exposure Limited impact

## Slide 38: The securability of SESAR Solutions
V0
V1 V2 V3
ATM needs
Scope
Pre-industrial Feasibility development &
integration
Industrialization Deployment Operations
V4 V5 V6
V7
Decommissioning
Cyber resilient architecture
High level requirements for industrialization, deployment and operations
Aspects of cyber-resilience
Foresight - prediction, anticipation Robustness - ability to keep operating Resourcefulness - control damage, mitigate it Redundancy - substitutable
Rapid recovery
Adaptability - to changing environments

## Slide 39: Delivering SESAR Solutions

## Slide 40: SESAR Solutions Catalogue
SESAR Solutions refer to new or improved operational procedures or technologies that aim to contribute to the modernisation of the European and global ATM system.
63 SESAR Solutions delivered and 79
further in the pipeline
Many are already being deployed across Europe
www.sesarju.eu/index.php/activities-solutions
www.sesarju.eu/sites/default/files/documents/reports/SESAR_Solutions_Catalogue_2019_web.pdf
40

## Slide 41
Answer to Aviation Business Needs (e.g. punctuality)
Deliver Performance (e.g. save fuel, CO²)
Knowledge Transfer (e.g. technical datapack)
Infrastructure & standards (e.g. SWIM
ops-internet)
SESAR
Solution
41
Validated Operational Improvement (e.g. procedure)

## Slide 42: SESAR IMPLEMENTATION ACROSS EUROPE
Synchronised SESAR Deployment (PCP)
42

## Slide 43: Key local deployments of SESAR Solutions
Remote tower
Runway status lights

## Slide 44: SESAR Solutions: local deployments

## Slide 45: SESAR Solutions – remote tower services
Manage remotely the traffic situation in real time of one or more airports
Technology
Video cameras with zoom-in and infrared
Ground sensors
360 panoramic high resolution screen
Navigation aids
SESAR validation exercises: Cost Effectiveness
Able to operate for longer periods Lower staffing costs
Supporting Regional Economy
OUT-THE-WINDOW VIEW

## Slide 46: SESAR Solutions – Runway status lights (CDG, Paris)
Runway incursions are among the greatest risks in airport operations today.
By installing lights which automatically alert when it is unsafe to enter a runway, airports can provide runway users with an early warning of a potential hazard.
S TA K E H O LDE R S
ANSP
AO
AU
NM
BENEFITS
Enhanced runway safety
Increased situational awareness
Runway status lights (RWSL) are fully automatic and require no input from controllers, airport operators or flight crew
STATUS
Linking intelligence about airfield surface movements with airfield lighting enhances surface safety for aircraft and vehicle movements

## Slide 47: SESAR Solutions: Europe-wide deployment
Key Europe-wide deployments:
  Extended arrival management (E-AMAN)
  Time-based separation (TBS)

## Slide 48: SESAR Solutions – Extended arrival management (E-AMAN) horizon
BENEFITS
Improved operational efficiency by reducing holding times
Improved operational efficiency by reducing fuel burn and emissions
Efficiency in terms of air navigation service provision
Improved safety and quality of service
E-AMAN allows for the sequencing of arrival traffic much earlier than is currently the case, by extending the AMAN horizon from the airspace close to the airport to further upstream and so allowing more smooth traffic management.
In November 2015, the Solution entered into force in Heathrow Airport by NATS and sees controllers from the four countries working together to slow down aircraft when there are significant delays at the airport.
London-Heathrow has cut holding times in its arrival stacks by one minute, reducing noise emissions and saving airlines over EUR 2 million in fuel bills and 7 500 tonnes of carbon dioxide annually
S TA K E H O LDE R S
ANSP
AO
AU
NM
STATUS

## Slide 49: SESAR Solutions – Time-based separation
Today, aircraft making their final approach to land are obliged to maintain minimum separation distances. These distances are fixed whatever the wind conditions. When keeping to these distances in strong headwinds longer gaps of time develop between aircraft. This means fewer flights landing per hour (reduced airport capacity), leading to delays and increased holding at busy times, which results in increased fuel burn. SESAR’s time-based separation (TBS) replaces current distance separations with time intervals in order to adapt to weather conditions. It provides consistent time-based spacing between arriving aircraft in order to maintain runway approach capacity.
S TA K E H O LDE R S
ANSP
AO
AU
NM
BENEFITS
Improved airport capacity as a result of increased aircraft landing rates in strong headwind conditions
Reduction in holding times as well as stack entry to touchdown times
Increased situational awareness
Analysis has shown that there has been no increased risk to wake
turbulence encounters, and no increase in the number of go-arounds following introduction of time-based separation at London Heathrow
STATUS

## Slide 50: SESAR Solutions in a global context

## Slide 51: The future of SESAR?

## Slide 52: FUTURE CHALLENGES & OPPORTUNITIES FOR THE AVIATION “ECOSYSTEM”
52
New uses of the sky, pushed forward by new entrants from digital industry
New travelers and reinvention of mobility to access the sky and a call for inter-operability & sustainability
Seamless end-to-end personalised customer journey across transport modes with data shared more freely
Automation of piloting and controlling requiring shift in human role (new skills and talents)
European leadership challenged with implications on sovereignty and disruption in value chain (e.g. linked to control on data)
Internet of the Sky,
data sharing freely
Pilotless ‘connected’ airplanes
Automated Air Traffic control, decoupled from physical location
Urban air mobility
Reinvention of
airports
Supersonic flights / commercial
space travel (still exclusive)
New uses of
the sky
New players stepping in from consumer electronics industry

## Slide 53: THE NEED FOR ONGOING ATM R&D
Thousands of aircraft in the sky
Hundred of thousands of connected flying vehicles in the sky
Tomorrow, Digital Aviation infrastructure to enable all air operations
Connected airplanes and rotorcrafts, drones, urban air mobility and air taxi and services
Today, airspace is occupied mainly by traditional manned aviation
Traditional piloted fixed-wing and rotorcraft with limited connectivity
Adaptation of current system is not an option to continue the European aviation success story (from an industrial, innovation and sovereignty point of view)
Source: Pictures from Airbus, Uber

## Slide 54: Future Research Challenges
Connected and automated ATM
Air-ground integration and autonomy
Artificial Intelligence (AI) for aviation
Capacity-on-demand and dynamic airspace
U-space and urban air mobility
Virtualisation and cyber-secure data sharing
Aviation green deal
Civil/military interoperability and coordination
Multimodality and passenger experience:
Digital European Sky – Strategic Research and Innovation Agenda

## Slide 55: Additional information and resources

## Slide 56: References
https://www.sciencedirect.com/science/article/pii/S2095809921000503
Council of the European Union. Council regulation (EC) No 219/2007 of 27 February 2007 on the establishment of a Joint Undertaking to develop the new generation European air traffic management system (SESAR). Strasbourg: Council of the European Union; 2007
Commission implementing regulation (EU) No 409/2013 of 3 May 2013 on the definition of common projects, the establishment of governance and the identification of incentives supporting the implementation of the European air traffic management master plan (text with EEA relevance). Brussels: The European Commission; 2013
Commission implementing regulation (EU) No 716/2014 of 27 June 2014 on the establishment of the pilot common project supporting the implementation of the European air traffic management master plan (text with EEA relevance). Brussels: The European Commission; 2014
https://www.atmmasterplan.eu/
http://www.sesarju.eu/index.php/activities-solutions
https://ext.eurocontrol.int/ehp/?q=node/1570
https://www.sesarju.eu/sites/default/files/documents/reports/SESAR_Solutions_Catalogue
_2019_web.pdf
https://www.sesarju.eu/sites/default/files/2019-05/AAS_FINAL_0.pdf
https://www.sesarju.eu/sites/default/files/documents/reports/SRIA%20Final.pdf
56

## Slide 57: Acronyms
Acronym | Definition
4D | four dimensional
AI | artificial intelligence
ANS | air navigation services
ANSP | air navigation service provider
ATM | air traffic management
CDM | collaborative decisionmaking
CNS | communication, navigationand surveillance
E-AMAN | extended arrival manager
EASA | European Aviation Safety Agency
E-OCVM | European Operational Concept Validation Methodology
MET | aviationmeteorology
MP | European air traffic management master plan
OPS | operations
PBN | performance based navigation
PCP | pilot common project
R&D | research and development
RPAS | remotely piloted aircraft systems
RWSL | runway status light
SDM | SESAR Deployment Manager
SES | single European sky
SESAR | single European sky
SJU | SESAR Joint Undertaking
SRIA | strategic research andinnovation agenda
SWIM | system-wide information management
TBO | trajectory-based operations
TBS | time-based separation
TRL | technologyreadiness level
VLD | very large scale demonstrations
57

## Slide 58
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com