## Slide 1: Introduction to ATM Airspace Management (ASM)
Fedja Netjasov
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Airspace sectorisation problem
2

## Slide 3: Airspace Sectorisation (1)
Two problems exist:
How to divide airspace into a finite number of sectors?
  Shape of the sectors?
  Number of elementary sectors?
  Etc.
How to use already defined sectors within given airspace?
  When to split or merge sectors?
  How many sectors to use for a certain demand?
  Etc.
https://www.skybrary.aero/index.php/Sectorisation

## Slide 4: Airspace Sectorisation (2)
The process of sector definition comprises virtual division of airspace. Thus, the provision of air traffic services is decomposed, in the different sectors, into tasks with manageable workload.
The opening of a new sector does not guarantee the arithmetic sum of the capacities of the elementary sectors – the combined capacity is a complex combination of factors such as traffic flow direction, coordination procedures, in-sector flight times, etc.
Therefore, a capacity figure is calculated for every sector configuration.
https://www.skybrary.aero/index.php/Sectorisation

## Slide 5: Sectorisation Criteria (1)
The ATC sectorisation principles evolved over the years to a complex set of criteria that fit into global concepts.
Today, ATC sector definition is an important part of the broader process of airspace design.
https://www.skybrary.aero/index.php/Sectorisation

## Slide 6: Sectorisation Criteria (2)
A number of factors form the boundaries of a sector; many of them are ATS-oriented, others defined by international relations:
  State boundaries or bilateral agreements for provision of ATS;
  International agreements for provision of ATS over international waters;
  Location of areas of special use – danger, prohibited, temporary segregated;
  Geographical characteristics of the area, type of service that is to be provided, radio and radar coverage;
  Direction of main traffic flow, in-sector flight time, conflict point distribution, etc.
https://www.skybrary.aero/index.php/Sectorisation

## Slide 7: Meeting Capacity Demand (1)
Increased capacity demand is generally met by the provision of more sectors.
Usually, the demand is calculated as short-term operational predictions based on planned flights.
Opening/closing of sectors should closely monitor the demand to achieve efficient use of all available resources -
  For example, dynamic arrangements should be made to ensure the availability of the required air traffic controllers.
  Failure to provide the required sector configuration on time may lead to potential risks arising from sector overload, inter-sector miscommunication, etc.
https://www.skybrary.aero/index.php/Sectorisation

## Slide 8: Meeting Capacity Demand (2)
Demand (D)
Capacity (C)
D > C
D > C

## Slide 9: ATM Sector Management (1)
Declared capacity
A measure of the ability of the ATC system, or any of its subsystems, or operating positions to provide service to aircraft during normal activities.
It is expressed as the number of aircraft entering a specified portion of airspace in a given period of time, taking due account of weather, ATC unit configuration, staff and equipment available, and any other factors that may affect the workload of the controller responsible for the airspace.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 10: ATM Sector Management (2)
Declared capacities are given as the number of aircraft that can be served per hour.
The exact value is determined using a variety of methods (eg. simulation, expert assessment, etc.).
The calculation takes into account airspace size and structure, expected traffic flow, the equipment used, etc.
Declared capacities are to be periodically reviewed by the ANSPs.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 11: ATM Sector Management (3)
Over-delivery
An occurrence when the declared rate of the ATFM regulation is exceeded by the actual number of aircraft that enter a regulated sector during a particular period.
Overload
An occurrence when an air traffic controller reports that he/she has had to handle more traffic than they consider it was safe to do so. An overload could be caused by an inadequate flow management strategy, or by over-deliveries; or by both.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 12: ATM Sector Management (4)
There are several ways to respond to increased traffic demand:
  Introduction of new equipment that helps the controllers handle more traffic while preserving the attained levels of safety and efficiency,
  Imposition of flow control, ie. restricting the number of aircraft that can enter the sector airspace,
  Opening more ATM sectors so that the traffic (and workload) is split across more controllers.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 13: ATM Sector Management (5)
The purpose of ATM sector management is to ensure that optimal sector configurations are used at all times.
A sector configuration is to be considered optimal if no excess sectors are open and no sector is subject to over-delivery for a prolonged period of time.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 14: Benefits of ATM Sector Manag. (1)
Flexibility – different sector configurations can be used depending on expected traffic flow (eg. the sector can be divided horizontally or vertically, split into three or more sectors, etc.).
Optimal use of personnel – sectors can be merged after traffic levels have decreased. This gives the management options to handle the traffic with fewer controllers, as opposed to the strategy where all possible sectors are manned at all times; regardless of traffic levels.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 15: Benefits of ATM Sector Manag. (2)
Increase of overall efficiency – when looking at air traffic control from a global perspective, the widespread use of ATM sector management helps to better handle the “bottlenecks” of air traffic flow thus reducing delays, costs and emissions.
Safe ATS provision – appropriate sector configuration ensures optimal controller workload preventing overload and distraction caused by too low traffic levels.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 16: Restrictions of ATM Sector Manag.
Sectors cannot be split indefinitely – there is no strict rule about this, but a sector with less than eg. 5 minutes of flight time is considered inefficient with present day equipment.
ATM sector management is useful when there are peaks and drops in traffic flow. If the traffic distribution is uniform within the day other options should be used.
Splitting sectors reduces the traffic-related workload (there are fewer aircraft on the frequency), but also increases inter-sector coordination. This must be taken into account when choosing the sector configuration.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 17: SMATSA Examples (1a)
Sectorisation in SMATSA airspace (as of summer 2019):
• In the horizontal plane airspace is divided in following sectors:
E – EAST, N – NORTH, S – SOUTH and W – WEST;
• In the vertical plane airsace is divided into five layers (based on Division Flight Levels (DFL) - 325, 345, 365, 385):
L – LOWER: FL 125 or 205 / FL 325;
M – MIDDLE: FL 325 / FL 345;
Z – UPPER: FL 345 / FL 365;
Y – TOP UPPER: FL 365 / FL 385;
X – SUPER TOP UPPER: above FL 385.
That generates 20 elementary sectors in total :
LE, LN, LS, LW, ME, MN, MS, MW, ZE, ZN, ZS, ZW, YE, YN, YS, YW, XE, XN, XS, XW.

## Slide 18: SMATSA Examples (1b)

## Slide 19: SMATSA Examples (2)

## Slide 20: SMATSA Examples (3)

## Slide 25: Opening of More Sectors (1)
The opening of new sectors is based on local particularities. While there are no strict rules for this, some typical criteria are:
  Expected traffic is above a specified threshold, eg. 90% of the sector capacity;
  The number of expected aircraft on the frequency at the same time is greater than a specified threshold, eg. 20 aircraft on the frequency at the same time;
  Traffic complexity, eg. a lot of aircraft departing from/arriving at nearby aerodromes;
  Expected adverse weather, especially CB;
  Testing of ATS equipment, eg. a new ATS system;
  A combination of the above.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 26: Opening of More Sectors (2)
The typical opening procedure is as follows:
  The supervisor makes a decision to open a new sector based on local criteria;
  The controllers from the new sector:
    verify the operational status of the equipment;
    inform the adjacent sectors/units;
    perform a takeover/handover procedure (get informed about the situation – conflicts, coordinations, aircraft requests, weather, etc.) with the controllers of the affected sector(s);
    assume control of aircraft within their area of responsibility.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 27: Opening of More Sectors (3)
Risks associated with the opening of new sectors:
  The procedure starts too late – this can lead to controllers working under high workload in an unfamiliar environment;
  Too many frequency changes within a short period of time - this can easily lead to a blocked frequency, or an aircraft being transferred to a wrong frequency;
  Poor takeover/handover;
  Underestimation of traffic, leading to sectors not being open when they should have been;
  Overestimation of traffic, leading to sectors being open unnecessarily.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 28: Closing/Merging of Sectors (1)
The closing/merging of sectors is based on local particularities. While there are no strict rules for this some typical criteria are:
  Expected traffic is and is expected to remain below a specified threshold, eg. 90% of the merged sector capacity;
  The number of expected aircraft on the frequency at the same time is, and is expected to remain, less than a specified threshold;
  Traffic complexity, eg. few aircraft departing from/arriving at nearby aerodromes;
  Weather improvement;
  A combination of the above.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 29: Closing/Merging of Sectors (2)
The typical closing/merging procedure is as follows:
  The supervisor makes a decision for closing/merging sectors when traffic levels are low and most situations (conflicts) have been resolved;
  The controllers from the sector being closed inform the concerned sectors/units;
  The controllers from the united sector perform a takeover/handover procedure and assume control of all aircraft within their area of responsibility;
  The frequency of the closed sector is usually monitored for a period of time (eg. at least 30 minutes).
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 30: Closing/Merging of Sectors (3)
Risks, associated with the closing/merging of sectors:
  Premature closing/merging, resulting in the overload of the united sector; this can be avoided if correct timing for the procedure is used;
  Underestimation of traffic, leading to overload shortly after the sectors have been merged; this risk can be mitigated with adequate interpretation of traffic forecasts.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 31: Changing the Sector Config. (1)
Sometimes traffic flows shift in such a way that a different configuration with the same number of sectors is considered preferable to opening a new sector or merging existing sectors.
  For instance, a configuration of one upper and two lower sectors (which managed a high number of departing and arriving traffic) may need to be replaced by three vertically split sectors (lower, middle and upper) in order to cope with the expected increase of overflying aircraft.
As in the other cases, the decision for changing the sector configuration is made by the supervisor based on the traffic demand.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 32: Changing the Sector Config. (2)
The procedures to be followed are described in the ATSU manual of operations, and typically include:
  Informing the concerned sectors/units about the new frequencies;
  Coordination between the sectors as necessary (eg. for conflicting aircraft that are now in a different sector);
  Performing handover/takeover between the sectors as necessary.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 33: Changing the Sector Config. (3)
Risks associated with changing the sector configuration while preserving the number of sectors:
  At least some of the controllers will face a (completely) different situation (in terms of airspace, aircraft and procedures);
  Increased inter-sector coordination is to be expected in the transition period (aircraft within the sector group may have to change frequency);
  Some of the controllers will inevitably control (for a few minutes) aircraft that are well outside the boundaries of their new sector while, at the same time, their situational awareness will be reduced (due to eg. colour representation of the aircraft that are entering the airspace that is now controlled by a different sector).
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 34: The Importance of Good Timing (1)
The main benefits of ATM sector management are the optimal use of personnel and the ability to handle traffic peaks safely and efficiently.
These tasks can only be achieved with good timing, which means that:
  New sectors are usually to be opened 10-20 minutes before the increased traffic demand to allow controllers to safely perform the procedures;
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 35: The Importance of Good Timing (2)
  Sectors should be merged only when there is reasonable assurance that the same sectors will not have to be reopened within a reasonable period of time (at least 30-40 minutes). Too frequent opening/closing of sectors should be avoided as this may lead to:
    poor coordination with adjacent units;
    aircraft being transferred to wrong frequencies;
    overall increase of the controller workload associated with the procedure.
https://www.skybrary.aero/index.php/ATM_Sector_Management

## Slide 36
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com