## Slide 1: Introduction to ATM Air Traffic Service (ATS)
Fedja Netjasov
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Air Traffic Service ATS
2

## Slide 3: Types of Air Traffic Control System (procedural and radar systems)
3

## Slide 4
Procedural system:
  based on STRIP as main input for flight and pilot POSITION REPORTS;
  radio communication with pilots;
  temporal values for Smin (up to 15 min);
  small capacity.
Radar system:
  based on STRIP as main input for flight;
  radio communication with pilots;
  radar technology for air traffic monitoring/surveillance;
  spatial values for Smin (up to 20 NM);
  higher capacity.
ATC System Types (1)

## Slide 5
Procedural system:
ATC System Types (2)

## Slide 6
Radar system:
ATC System Types (3)

## Slide 7
ATC System Types (4)

## Slide 8
SRE

## Slide 9
SRE/SSR

## Slide 10: Air Traffic Controller (ATCo) decision making processes
10

## Slide 11: Decision-making process (1)
The ATCo process for making decisions and issuing clearances and instructions to pilots separately for each flight, has a goal to provide the necessary separation between aircraft during a flight through a given airspace with the most efficient utilisation of aircraft performance; satisfying traffic demand and ATC capacity.
The ATCo decision making process consists of mathematical and logical operations necessary to determine the types and schedule of both the ATCo’s and the pilots’ actions (based on available input data), as well as numerical values of certain elements of those actions (decisions).

## Slide 12: Decision-making process (2)
For example – monitoring the flights of two aircraft, the ATCo will look at whether they are on the same FL, or not (logical operation). If they are at the same FL, the ATCo will calculate their separation at the trajectory crossing point (mathematical operations) and if separation is potentially violated, th eATCo will consider a change of FL, speed or heading for one, or both aircraft (decision on type of action) and its schedule (first change of heading for aircraft 1, then change of speed for aircraft 2 - decision on schedule). Finally, the ATCo will decide upon the required change of heading (degrees) and speed (knots) (decision on numerical values).

## Slide 13: Decision-making process (3)
The Decision-making process contains the following activities:
  Presentation of input data to the ATCo for the airspace for which he/she has jurisdiction;
  Analysis of input data using mathematical and logical operations;
  Choice of appropriate action and determination of numerical values for elements of those actions (decisions);
  Decision and output data:
    For pilots in the form of - clearances, instructions and information;
    For adjacent ATCo in form of - transfer elements.

## Slide 14
Input
data
Analysis
Choice of
appropriate
action and
determination of
numerical values
Decision
and
output data
Mathematical and logical
operations
and analysis of data
Types of actions
Flight plans
Meteorological data
AIP/NOTAM
Aircraft position
Data for aircraft transfer

## Slide 15: Decision-making process phases (1)
Traffic situation influences ATCo physical and mental activities.
Conflict is every situation in which safe aircraft separation could be violated.
Conflict could occur:
  Between two or more aircraft;
  Between aircraft trajectory and terrain or closed airspace;
  Due to traffic demand and capacity imbalance.

## Slide 16: Decision-making process phases (2)
Decision-making phases:
  Planning: based on current and predicted aircraft positions, the ATCo decides which aircraft will reroute; which aircraft will change speed or FL, etc. and coordinate this information with the adjacent ATCo; all with the aim to enable safe aircraft separation quickly.

## Slide 17: Decision-making process phases (3)
  Implementation: using the radio frequency or “data link”, the ATCo provides instructions to pilots and transfers aircraft to adjacent ATCos;
  Monitoring: ATCo monitors the traffic situation and checks whether traffic status is in accordance with the plan (checking the compatibility between the plan and reality);
  Validation: determine how effective the decision was.

## Slide 18
Monitoring
Validation
Planning
Implementation
Actions
Result of
action on
a system
Observations
Compatibility
between the plan and
realisation
Mental activities
Physical activity

## Slide 19: Data necessary for ATCo work – flight plan, meteo data, messages
19

## Slide 20
Data about aircraft (flight) intentions (flight plan);
Data about origin and destination airports;
Data about meteorological situations;
Data about airspace;
Data about current location of the aircraft in the airspace.
Data necessary for ATCo work
(1)

## Slide 21
Flight plan is the document which serves as the information source for ATCo about flight intentions.
The Flight plan is a kind of “contract” between the airline and ANSP by which:
  the pilot is obliged to follow procedures, clearances, instructions and information given by the ATCo and will strictly follow elements filed in the flight plan, and -
  ATCo is obliged to be fully responsible for flight safety and to separate the flight from rest of the traffic.
Data necessary for ATCo work
(2)

## Slide 22
Filed by ATCo
Filed by pilot
Should be sent to all ANSPs through whose airspace aircraft have to pass
Should be sent only in case of emergency events to the ANSP that starts the search and rescue activity.

## Slide 23: ATCo activities
23

## Slide 24
Directly:
  with ATCo on the same working place
Indirectly:
  with pilots;
  with neighbouring ATCos (domestic);
  with neighbouring ATCos (international).
ATCo communication (1)

## Slide 25
Aircraft
Crew
ATCo
domestic
interphone
ATCo international
telephone
Procedural
ATCo
direct
Radio frequency
ATCo communication (2)

## Slide 26
ATCo Activities

## Slide 27: Pilot related activities (1)
ATCo activities related to pilots could be divided into three basic types:
  Conformance Management – type of activity which includes monitoring aircraft trajectories and correction of aircraft guidance deviations from approved trajectory in 2D, 3D and 4D:
    Conformance Monitoring;
    Conformance Resolution.

## Slide 28: Pilot related activities (2)
  Separation Assurance:
    Conflict Management takes place at the strategic level; only applies to planned flight trajectories; and includes Conflict Detection and Conflict Resolution activities;
    Hazard Management takes place at the tactical level and applies to both planned flight trajectories, as well as previous aircraft positions; and includes Hazard Detection and Hazard Resolution activities.

## Slide 29: Pilot related activities (3)
  Congestion Management:
    Assignment - process of assigning specific routes to certain flights in order to manage traffic flows;
    Sequencing - process of defining a sequence of flights in order to manage traffic flows;
    Scheduling - process of defining a specific time window for flight arrival or passing through certain airspace in order to manage traffic flows.

## Slide 30: Pilot related activities (4)
Specific general activities through which previous activities are realised are:
  Identification of Aircraft
  Clearance Delivery;
  Providing Information; and
  Providing Instruction.

## Slide 31: Pilot related activities (5)
Identification of aircraft should be done before the ATCo commences surveillance/monitoring of aircraft.
Identification should be maintained during the flight until the aircraft leaves certain airspace.
When identification is made, or if it is lost during the flight, the ATCo should immediately inform pilots, and should issue appropriate instructions.

## Slide 32: Pilot related activities (6)
Clearances are giving permission to pilots to act according to conditions specified by the ATCos or conditions required by pilots.
Pilots should reply (read back) to ATCo parts of the clearances relating to safety and instructions provided by voice communication.

## Slide 33: Pilot related activities (7)
Providing information includes:
  Informing pilots about aircraft positions;
  Informing pilots about Essential Traffic;
  Other information as required.

## Slide 34: Pilot related activities (8)
Instructions ATCo’s requirements for pilots to perform certain actions, such as:
  Instruction for heading changes (vectoring procedure) – procedure for guiding aircraft by giving pilot a set of headings in order to maintain given trajectory (route);
  Instruction for speed changes (both horizontal and vertical);
  Other instructions.

## Slide 35: ATCo related activities (1)
During a flight, aircraft pass from one airspace to another, i.e. from the jurisdiction of one, to the jurisdiction of another ATC service/unit.
Passing into the jurisdiction of another ATC service/unit, means the responsibility for safe, regular and expeditious flight is transferred to another ATC service/unit.
The transmission of jurisdiction and responsibility is called a transfer between ATC services/units; and the transfer is preceded by a process of coordination between the aforementioned services/units.

## Slide 36: ATCo related activities (2)
The objective of the coordination between ATC services/units is to reach an agreement in a timely manner about the transfer elements in order to be assured that the aircraft passes safely from the jurisdiction of one ATC service/unit to another, according to agreed conditions and with consent of both ATC services/units.
ATC services/units should establish and apply standard coordination and transfer procedures with the aim to reduce the necessity for voice communication.
Those procedures should be harmonized with ICAO procedures and specified in Letters of Agreement – LoA.

## Slide 37: ATCo related activities (3)
Letter of agreement is a written agreement between appropriate ATC services/units which determines a coordination procedure between those services/units, as well as the content of the flight data being exchanged (mandatory and additional data).
The LoA also specifies how much time in advance - before the aircraft arrives at the transfer point – the flight data should be exchanged between ATC services/units.

## Slide 38: ATCo related activities (4)
Mandatory data are:
  Aircraft call sign;
  Name of transfer point as well as arrival time;
  Flight level or altitude;
  SSR code.
Additional data are:
  Aircraft type,
  Destination airport,
  Flight route,
  Purpose of flight, etc.

## Slide 39: ATCo related activities (5)
Coordination:
  LoA defines how much time in advance coordination begins;
  It is agreed by Planning ATCos,
  Radio connection could be established with adjacent ATCo before airspace boundary/corridor (Transfer of Communication Point, see next slide).
Transfer:
  Made on airspace boundary/corridor (Transfer of Control Point, see next slide),
  Pilots have an obligation to establish radio connection with adjacent ATCo as soon as possible, and also to send a position report.

## Slide 40: ATCo related activities (6)

## Slide 41: Air Traffic Control - ATC Flight Information Service - FIS Alerting Service - AS
41

## Slide 42
ATS provide the following services in real-time:
  Air Traffic Control Service – ATC ;
  Flight Information Service – FIS;
  Alerting Service – AS.
ATS

## Slide 43
Area of ATC jurisdiction:
Control of traffic of civilian and military aircraft;
Complete airspace of one country or region (over ground or water surface up to certain height).
Main ATC goals are to enable safe, regular and efficient air traffic.
Air Traffic Control (1)

## Slide 44
SAFE: air traffic without conflicts between any aircraft and terrain, obstacles or other aircraft.
REGULAR: air traffic with minimal possible flight delay.
EFFICIENT: ATC capacity is always greater than air traffic demand.
Air Traffic Control (2)

## Slide 45
Origin
airport
Climbing
Descending
Phases of Flight (1)
Take-off
Destination
airport
Landing
Cruising

## Slide 46: Air Traffic Control Units – airport, approach, en-route
46

## Slide 47
Airport control unit (tower);
Approach control unit;
En-route control unit.
Air Traffic Control Units

## Slide 48
Origin
airport
Climbing
Descending
Airport control unit (1a)
Take-off
Destination
airport
Landing
Cruising

## Slide 49
The Airport Control Unit (TOWER) is responsible for the provision of ATC services to airport traffic, i.e. all traffic on the manoeuvring surfaces of the airport, as well as all aircraft flying near the airport, i.e. in CTRs in VMC conditions.
In IMC, it is responsible for traffic control until traffic enters the runway (prior to take-off), or from leaving the runway (after landing); and according to the agreement reached between the TMA Control Unit and TOWER.
TOWER require visual contact with the outside (airport).
Airport control unit (1b)

## Slide 50
Airport control unit (2)

## Slide 51
Airport control unit (3)

## Slide 52
Origin
airport
Climbing
Descending
Approach control unit (1a)
Take-off
Destination
airport
Landing
Cruising

## Slide 53
The Approach control service (APP) is responsible for all controlled arrivals and departures from one or more airports within the Terminal controlled area (TMA).
APP do not require visual contact, but use surveillance systems that allow ATCos to monitor the traffic flow on a separate screen.
Approach control unit (1b)

## Slide 54
TMA control unit (2)

## Slide 56
Origin
airport
Climbing
Descending
En-route control unit (1a)
Take-off
Destination
airport
Landing
Cruising

## Slide 57
The En-route (area) control service (ACC) is responsible for all controlled flights within CTA/UTA, separated in layers and sectors.
A team of controllers (usually two) works on each sector:
  An executive ATCo who maintains radio communications with aircraft, monitors and vectors aircraft to prevent collisions and update strips, and
  A planning ATCo who coordinates with neighbouring controllers and highlights possible aircraft pair conflicts to executive controller.
En-route control unit (1b)

## Slide 58
En-route control unit (2)

## Slide 59
En-route control unit (3)

## Slide 60
En-route control unit (4)

## Slide 61
Flight Information Services (FIS) provide flight information services, i.e. advice and information necessary for the safe and efficient operation of flights.
These services are provided to all aircraft to whom ATC services are provided, as well as other aircraft to whom ATC services are not provided but are otherwise known to the Flight Information Service.
Information provided through FIS includes meteorological information, traffic information, information related to state of infrastructure of airports, and any other information which could affect safety.
Flight Information Service

## Slide 62
Alerting Service (AS) informs the appropriate organisations regarding the initiation of search and rescue operations for an aircraft and, where appropriate, assists those organisations.
These services are provided to all aircraft to whom ATC services are provided, as well as to other aircraft to whom ATC services are not provided but are otherwise known to the Flight Information Service, or to whom they have submitted flight plans; but also to any other aircraft for which it is known, or it is believed, is the object of a hijack.
Alerting Service

## Slide 63
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com