## Slide 1: Introduction to ATM Air Traffic Flow Management (ATFM)
Graham Tanner
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Introduction to flight planning and messaging

## Slide 3: Introduction
Flight plan
  Purpose
  Information required
  Worked example
Messaging
  Distribution within Europe
  Network Manager & centralised systems
  Filing
  Slot management
  A look ahead to the extended flight plan
Note
  European focus, key role of EUROCONTROL
  Civilian, commercial use

## Slide 4: Introduction
What is a flight plan?
  Document providing specified information to air traffic service units relative to an intended flight, or portion of a flight of an aircraft
    Completed by the aircraft operator (AO)
    Usually submitted by the aircraft operator
  Information and format prescribed by ICAO rules, adapted regionally (e.g. navigation specifications; air traffic flow management)
    Doc 4444 Procedures for Air Navigation Services – Air Traffic Management (‘PANS-ATM’), 16th Edition 2016
    Doc 7030 Regional Supplementary Procedures, 5th Edition 2008
  Infrequent changes
    Last update made in 2012 (announced in 2009) – minor changes
    Planning in progress for extended flight plan (EFPL) – major changes

## Slide 5: ICAO flight plan form

## Slide 6: ICAO flight plan form
ICAO model flight plan form
  ICAO Doc 4444 (‘PANS-ATM’) Appendix 2
Also known as
  FAA Form 7233-4 International Flight Plan
  CAA CA48/RAF 2919 FPL Form
  and so on...

## Slide 7: Flight plan information
Message fields are known as ‘items’
Coded inputs required, in general
  All clock times in UTC
  All other times in hours/minutes
  All text capitalised
  ICAO codes used
Low resolution (hence need for EFPL)
File before departure (with exceptions)
  Departure = EOBT (should be a realistic time!)
  No earlier than 120 hours before
  No later than 3 hours before (else ‘late filing’)
Filed flight plan = FPL

## Slide 8: Flight plan information
Submission details
Address data (FPL will be sent to listed ATS units)
Filing date/time (DDHHMM)
Originator indicator (address of FPL source)
Item 3 message type (FPL = standard ICAO ATS message type)
Air traffic services (ATS) units – generic term (e.g. air traffic control unit, flight information centre)
Other ICAO ATS message types – CHG, DEP, ARR, ..

## Slide 9: Flight plan information
Content
Item 7 aircraft identification (operator code & flight identifier = unique KEY FIELD#1)
Item 8 flight rules & type of flight (IFR/VFR/mixture, scheduled/non-sched./ military/general/other)
KEY FIELD – containing flight plan information that cannot be changed once filed
IFR flights – aircraft properly equipped to operate in instrument meteorological conditions (IMC)
VFR flights – fly aircraft solely by reference to outside visual cues

## Slide 10: Flight plan information
Content
Item 9 aircraft number, type and wake turbulence (if >1, ICAO aircraft type & corresponding WTC)
Item 10/10a equipment on board aircraft (radio communication, navigation & approach aid equipment – some also appear in item 18)
WTC – Light, Medium, Heavy and J Super Heavy

## Slide 11: Flight plan information
Content
Item 13 departure airport & EOBT (ICAO airport code & estimated time aircraft will depart KEY FIELD#2)
KEY FIELD – containing flight plan information that cannot be changed once filed

## Slide 12: Flight plan information
Content
Item 15 route (initial cruising speed, initial cruising level & route description)
Speed – kNots, Kph, Mach number
Level – Flight level, Standard metric level, Altitude in hundreds of feet or tens of Metres

## Slide 13: Flight plan information
Content
Item 16 destination airport KEY FIELD#3, elapsed time & alternative airport(s) (ICAO airport code, total estimated flight time HHMM & up to 2 alternative destination airports – in case of diversion)
KEY FIELD – containing flight plan information that cannot be changed once filed

## Slide 14: Flight plan information
Content
Item 18 other information (relevant to flight, >20 sub-fields available, e.g. elapsed times at points en-route, aircraft tail number, equipment cross-referenced with other items, etc.; however date of flight is KEY FIELD#4)
KEY FIELD – containing flight plan information that cannot be changed once filed
Equipment – if item 10 includes ‘R’ (approved for basic area navigation), then item 18 lists appropriate capability (e.g. ‘B1’ Basic Area Navigation/RNAV 5 all permitted sensors)

## Slide 15: Flight plan information
Content
Item 19 supplementary information (not normally filed, but available from operator if an ATS unit should request it; eg. pax + crew on-board, name of pilot, total fuel endurance, survival equipment – in case of search & rescue)

## Slide 16: Flight plan information
ICAO flight plan form appropriate for…
  VFR private flight 
  IFR commercial flight 

## Slide 17: Preparing a flight plan

## Slide 18: Flight plan example
Preparing a flight plan
  IFR flight between Heathrow – Frankfurt, dep. 1500 (08APR19), using real data
  Examples of the types of aeronautical information available (route)
  ICAO format, for electronic filing (same information as paper form)
    Machine-readable
(FPL-KTN153-IS
-A319/M-SDE3FGIKRWXY/S
-EGLL1500
-N0454F330 DET1J DVR UL9 KONAN UL607 SPI UT180 PESOV T180
UNOKO UNOKO2L
-EDDF0101 EDFH
-EET/EGTT0010 EBUR0022 EDVV0045 EDUU0046 EDGG0050 REG/GGJGD
SEL/MITJ OPR/ENGAGE AIRWAYS DOF/190408 RMK/TCAS PBN/A1B1D1O1S2)

## Slide 19: Flight plan example
Flight plan items
(FPL-KTN153-IS
-A319/M-SDE3FGIKRWXY/S
-EGLL1500
-N0454F330 DET1J DVR UL9 KONAN UL607 SPI UT180 PESOV T180
UNOKO UNOKO2L
-EDDF0101 EDFH
-EET/EGTT0010 EBUR0022 EDVV0045 EDUU0046 EDGG0050 REG/GGJGD
SEL/MITJ OPR/ENGAGE AIRWAYS DOF/190408 RMK/TCAS PBN/A1B1D1O1S2)
Aircraft operator
Heathrow – Frankfurt
Day of departure
IFR scheduled flight

## Slide 20: Flight plan example
(FPL-KTN153-IS
-A319/M-SDE3FGIKRWXY/S
-EGLL1500
-N0454F330 DET1J DVR UL9 KONAN UL607 SPI UT180 PESOV T180
UNOKO UNOKO2L
-EDDF0101 EDFH
-EET/EGTT0010 EBUR0022 EDVV0045 EDUU0046 EDGG0050 REG/GGJGD
SEL/MITJ OPR/ENGAGE AIRWAYS DOF/190408 RMK/TCAS PBN/A1B1D1O1S2)
Flight plan items
Airbus A319 medium WTC
S standard radio comm, nav & approach aid equipment
D distance measurement equipment
E3 PDC ACARS (datalink)
F automatic direction finder
:
/S Transponder-Mode S
Performance-based navigation level
Tail number

## Slide 21: Flight plan example
(FPL-KTN153-IS
-A319/M-SDE3FGIKRWXY/S
-EGLL1500
-N0454F330 DET1J DVR UL9 KONAN UL607 SPI UT180 PESOV T180
UNOKO UNOKO2L
-EDDF0101 EDFH
-EET/EGTT0010 EBUR0022 EDVV0045 EDUU0046 EDGG0050 REG/GGJGD
SEL/MITJ OPR/ENGAGE AIRWAYS DOF/190408 RMK/TCAS PBN/A1B1D1O1S2)
Flight plan items
Route:
N0454F330 at top of climb, cruising at FL 330, 454 knots (TAS)
DET1J Standard Instrument Departure (SID) from Heathrow
DVR ‘DOVER’, SPI ‘SPRIMONT’ navaids
UL9, UL607, UT180, T180 airways (upper/lower airspace)
KONAN, PESOV, UNOKO waypoints
UNOKO2L Standard Instrument Arrival (STAR) at Frankfurt

## Slide 22: Flight plan example – route
Flight plan items – route information:
  SID – a designated IFR departure route linking airport/runway with a significant point on an airway
  STAR – vice versa, linking airway to airport instrument approach procedure
  No need to file intermediate waypoints along same airway – only specify when/where change occurs (i.e. point1 > airway1 > point2 > airway2 > point3)
  Simplest route is a direct (DCT) route between entry/exit points (incl. Free Route Airspace)
  Note that some states require certain units to be used (e.g. Russian Federation requires metric speed/altitude)

## Slide 23: Flight plan example – route
Sources of aeronautical information available:
  Aeronautical Information Publication (AIP) – strategic
  Network Operations Portal (NOP Portal) – strategic, pre-tactical, tactical
  Route Availability Document (RAD) – strategic
  UK & Ireland Standard Route Document (SRD) – strategic
  Accessing Flexible Use of Airspace (FUA) – pre-tactical, tactical
  Network Operations Plan (NOP) – strategic
examples follow...
Notes: Example flight plan – the route
Sources of information for planning the route – these will be outlined using the worked example flight plan; all sources are available via the Network Operations Portal

## Slide 24: Flight plan example – route
Sources of aeronautical information available (examples):
  Aeronautical Information Publication (AIP) – standardised information published by each state (covering general, en-route & airports)
    AIRAC cycle synchronises changes every 28 days (08APR19 was within ‘AIRAC 1904’)
    AIP also updated by Amendments, Supplements (long-term temp. changes), NOTAMs & Pre-flight Info. Bulletins for short-term announcements (e.g. RWY closures)
    Available from states & European AIS Database (EAD) – “one-stop shop”
(NATS) www.nats-uk.ead-it.com
(EUROCONTROL EAD) www.ead.eurocontrol.int

## Slide 25: Flight plan example – route
Sources of aeronautical information available (examples):
  Network Operations Portal (NOP Portal) gateway that brings together all operational information in one place
  Two versions: protected and public
  Information by strategic, pre-tactical, tactical phase (+ post-operations):
    Scenarios (optimisation of capacity)
    ATFCM Daily Plan (D-1 only), a set of tactical ATFM measures on next day (via ANM & INP)
    European Airspace Use Plan (EAUP/EUUP)
    News & updates
    Weather
    NOP Portal examples…
www.public.nm.eurocontrol.int/PUBPORTAL/gateway/spec/

## Slide 26: Flight plan example – route
ATFCM Notification Message (ANM) filtered by ‘EG’
Initial Network Plan (INP) map showing areas predicted to have a significant impact on network
ATFCM Daily Plan:
Notes: All examples for D-1

## Slide 27: Flight plan example – route
Weather assessment
ATFCM Measures (scenario list)
Notes: All examples for D-1

## Slide 28: Flight plan example – route
Sources of aeronautical information available (examples):
  Route Availability Document (RAD) – common reference document for route & traffic orientation; organises traffic into specific flows to make the best use of available capacity
  RAD restrictions are requested by states/FABs (collaborative process):
    Geographic location combined with flight level/time conditions/parameters
  Flight planning via ‘restricted object’
    Three main types of restrictions: forbidden/allowed/only option
    Logical AND/OR/NOT operators
    Examples:
restricted objects
AND
AND
(Geneva)
(Toulouse)
(Paris CDG)
(significant points)
OR
OR
(Paris Orly)
NOT

## Slide 29: Flight plan example – route
Sources of aeronautical information available (examples):
  Route Availability Document (RAD) – huge document with 5 appendices:
    Appendix 2 Area Definitions (defines airports/areas into groups, e.g. London Group)
    Appendix 3 City pair Level Capping (applies between O/D airports)
    Appendix 4 En-route DCTs / General limits (direct limitations, incl. Free Route Airspace)
    Appendix 5 Airport Connectivity (direct connections between airports, without SIDs/STARs or with SIDs/STARs which certain aircraft cannot comply with)
    Appendix 6 Flight Profile Restrictions (vertical profile restrictions between ATS units)
    Appendix 7 FUA Restrictions (airspace restrictions)
www.nm.eurocontrol.int/RAD
Appendix 3
city pairs (restricted objects)
Heathrow,
Gatwick,
etc.
Frankfurt,
Cologne Bonn,
etc.

## Slide 30: Flight plan example – route
Sources of aeronautical information available (examples):
  Route Availability Document (RAD) – although deals with restrictions:
    facilitates flight planning while improving ATFM
  Example in response to expected capacity and staffing shortfalls:
    Enhanced network measures developed for summer 2019 (‘eNM/S2019’)
    Aim to reduce en-route delay from over 4 min to below 2.5 min per flight
    To be achieved via the RAD, moving 1100+ flights/day out of capacity constrained ACCs through the use of level caps and lateral rerouteings
    Measures became effective on AIRAC 1905 (from 25APR19):
    Impact on airlines cf. network benefits

## Slide 31: Flight plan example – route
Sources of aeronautical information available (examples):
  UK & Ireland Standard Route Document (SRD) – assists in constructing UK/Irish portions of flight plannable routes (find ‘preferred’ routeings by airports/points)
  SRD also available via RAD portal
www.nats-uk.ead-it.com/aip/current/srd/SRD_Spreadsheet.xls

## Slide 32: Flight plan example – route
Sources of aeronautical information available (examples):
  Flexible Use of Airspace (FUA) – concept for increasing airspace capacity & improving efficiency/flexibility of aircraft operations
    Airspace no longer designated as either ‘military’ or ‘civil’ but considered as a continuum & used flexibly on a day-to-day basis (civil/mil. coordination)
  European Airspace(/Updated) Use Plan (EAUP/EUUP) publishes 24H (Conditional Routes (CDR), Restricted Airspace (RSA) allocations & FUA restrictions), eg.
    CDR1 route may be available for flight planning during times published in the relevant AIP; permanently plannable unless EAUP/EUUP notifies of closure
    CDR2 route may not be available for flight planning; permanently unplannable unless EAUP/EUUP publishes availability conditions
    CDR3 route shall not be available for flight planning at all; ATC may issue tactical clearances

## Slide 33: Flight plan example – route
www.public.nm.eurocontrol.int/PUBPORTAL/gateway/spec/
EAUP/EUUP message: CDR1 closures
EAUP/EUUP message: CDR2 available

## Slide 34: Flight plan example – route
Network Operations Report 2018 (Draft)

## Slide 35: Flight plan example – route
Sources of aeronautical information available (examples):
  Network Operations Plan (NOP) – short to medium-term outlook of how the ATM Network will operate, including expected performance at network and local level
  Updated annually; seasonal part is hosted in the Network Operations Portal
  NOP includes:
    Network planning
    Overview of current forecasts
    Identify potential bottlenecks & mitigation solutions
https://www.eurocontrol.int/publications/european-network-operations-plan

## Slide 36: Flight plan example
(FPL-KTN153-IS
-A319/M-SDE3FGIKRWXY/S
-EGLL1500
-N0454F330 DET1J DVR UL9 KONAN UL607 SPI UT180 PESOV T180
UNOKO UNOKO2L
-EDDF0101 EDFH
-EET/EGTT0010 EBUR0022 EDVV0045 EDUU0046 EDGG0050 REG/GGJGD
SEL/MITJ OPR/ENGAGE AIRWAYS DOF/190408 RMK/TCAS PBN/A1B1D1O1S2)
Flight plan items summary
  Time consuming to prepare manually
    Multiple sources (e.g. AIP, RAD, ..)
    Daily messages (e.g. CDR availability)
    Route constraints restrict choice (e.g. level capping)
  Thankfully flight planning tools are available!

## Slide 37: Flight planning tools
Commercial IFR passenger flight planning tools available
  Variety of tools available to serve the requirements of
    Single aircraft operators (VFR/IFR)
    Business aviation operators (IFR)
    Large commercial carriers (i.e. operating hundreds of IFR flights per day)
  Basic filing tools (e.g. on-line)
  EUROCONTROL provides access to free tools (CHMI and NOP protected) so that airlines can manage their flights within Europe
  Flight planning suites with access to up-to-date weather & aeronautical information. Examples include:
Other tools are available!

## Slide 38: Flight planning tools
Flight planning suites
  Generate internal operational flight plans
    With more detail than needs to be filed as flight plan (i.e. only the required information items are submitted)
    Generate alternative valid flight plans for dispatchers (e.g. predicted fuel burn compared with flight time, routes & associated en-route charges)
    File flight plan and then receive, process and automatically act upon ATFM messages (i.e. integrate with slot allocation process)
    Communicate with the flight crew whilst airborne via datalink

## Slide 39: Flight planning tools
Example of typical airline flight planning behaviour
  Computer-based flight planning is now the norm
    Tools permit flight plans to be prepared and submitted without human intervention (e.g. cheapest option filed) – dispatchers often only need to deal with exceptions
  File first / original flight plan 10-16H before scheduled departure time
  As information comes available (e.g. network disruption, latest weather forecast, CDR availability, runway/SID/STAR usage, aircraft change) updated flight plans are submitted
    No later than 3 hours before (else ‘late filing’)
    If disruption, flight plan could be updated 30 minutes before EOBT (eg. new route)
  OFP example follows…

## Slide 40: Flight planning tools
standard flight plan items
route (choice)
additional detail
fuel
weights
fuel/
time
deviation
tankering
route/weather
alternate airports
wind
Notes: Comparison showing the additional detail available (green) to the AO compared with information required to be filed (red)

## Slide 41: Flight planning tools
Repetitive flight plans (RPLs)
  An alternative mechanism of filing IFR flight plans
  Suitable for flights operated regularly, e.g.
    Same flight every day
    Same flight every Tuesday
  Batch of repetitive flights are submitted in advance for the season (‘summer’ or ‘winter’); two versions can be submitted:
    new lists (NLST)
    revised lists (RLST)
  ACK sent to airline; RPLs are processed/reprocessed each AIRAC cycle; invalid RPLs are corrected by EUROCONTROL (feedback sent to airline)

## Slide 42: Flight planning tools
Repetitive flight plans (RPLs)
  Advantage: reduced workload for the aircraft operator (‘file-and-forget’)
  Disadvantage: unable to adjust for daily conditions (e.g. weather, temporary availability of shorter routes – Conditional Routes)
  But change is coming – RPLs will be phased out in Europe from 29MAR20
    Advance notice given, so that operators have time to update their systems

## Slide 43: Distribution of messages in Europe

## Slide 44: Network Manager
How is the flight plan filed and distributed between ATS units?
  Europe has a centralised flight plan processing and distribution service: EUROCONTROL Network Manager (NM)
  Background:
    Aircraft operators used to file flight plans individually to all concerned ATS units
    1980s European Transport Ministers agreed to implement ICAO concept of a “Centralised Traffic Management Organisation”
    1990s EUROCONTROL established the Central Flow Management Unit (CFMU), adding ATFM and FPL functions, adding geographical coverage (e.g. UK traffic flow added in 1995)
    1996 CFMU fully operational – all flight plans in the CFMU Area collected & redistributed to ATS units by IFPS
    2011 EC nominated EUROCONTROL as the Network Manager, as defined by Single European Sky II (SES) legislation
    CFMU became the Network Manager Operations Centre (NMOC)

## Slide 45: Network Manager Operations Centre
Summary of NMOC core operational services:
  Flow & Capacity Management
  ATM Access Gateway & Flight Planning Operations
  Information Management Domain
  Crisis and Contingency Management
  Post-operations analysis and reporting
Integrated Initial Flight Plan Processing System (IFPS):
  Single source for distribution of IFR flight plan messaging in Europe
  Covers ICAO EUR Region known as the IFPS Zone (IFPZ or FPM DIST) – over 40 states
  Neighbouring airspace also receives copies – FPM COPY & ATFM ADJ (differing reasons)
  NM AREA covers all NM operations (incl. charging zone, RAD)

## Slide 46: Integrated Initial Flight Plan Processing System
IFPS
  IFPS receives, checks (e.g. with RAD) and processes FPL content
  Current software version ‘NM 23.0’ (usually two releases each year)
  2 units (FP1 in Belgium, FP2 in France) share workload
  4D profile is estimated for each flight within IFPZ
  Delivers IFR flight plans to ATS units within IFPZ and the flow management system (ETFMS)
  Daily workload:
    >30k flights
    >90% FPLs are processed automatically; <10% manual intervention (i.e. NM workload)
    >60k messages

## Slide 47: Filing
Filing of flight plan to IFPS (i.e. from AO to NM)
  Filing a flight plan = a request for a slot (exempted flights: HEAD/SAR/MEDEVAC/..)
FPL – file from flight planning tool (-120H to -3H before EOBT)
  2 closed networks: AFTN (Aeronautical Fixed Telecommunications Network) & SITA (originally Société Internationale de Télécommunications Aéronautiques)
  Network Operations Portal (protected version)
  IP/VPN web service
  In each case, originator has unique address indicator
    IFPS response: ACK (success), REJ (unfixable errors), MAN (errors, then ACK or REJ)
RPL – file by e-mail (pre-season possible) – RPLs will be phased out in Europe in 2020
  Pre-formatted documents (IFPS RPL format)
    IFPS response: ACK (i.e. processed later)

## Slide 48: Filing
IFPS processing (i.e. flight plan accepted)
Conversion to ADEXP format (if submitted in ICAO format)
  ADEXP – ATS Data Exchange Presentation format for ATS message exchange between IFPS, aircraft operators & ATS units
RPL transfer to IFPS for processing -20H before EOBT
(FPL-KTN153-IS
-A319/M-SDE3FGIKRWXY/S
-EGLL1500
-N0454F330 DET1J DVR UL9 KONAN UL607 SPI UT180 PESOV T180
UNOKO UNOKO2L
-EDDF0101 EDFH
-EET/EGTT0010 EBUR0022 EDVV0045 EDUU0046 EDGG0050 REG/GGJGD
SEL/MITJ OPR/ENGAGE AIRWAYS DOF/190408 RMK/TCAS PBN/A1B1D1O1S2)
-TITLE IFPL
-BEGIN ADDR
-FAC CFMUTACT
-FAC EGTTZGZP
:
-FAC EDDXYIYR
-END ADDR
-ADEP EGLL
-ADES EDDF
-ARCID KTN153
-ARCTYP A319
-CEQPT SDE3FGIKRWXY
-EOBD 190408
-EOBT 1500
-FILTIM 070421
-IFPLID AA99990000
-ORGNID EGLLXUOW
-ORIGIN
-NETWORKTYPE AFTN
-FAC EGLLUOWH
-SEQPT LB1
-WKTRC M
:

## Slide 49: Enhanced Traffic Flow Management System
ETFMS
  4D flight plans received from IFPS – i.e. planned information
  Data received from other sources e.g. departure/arrival times (airports, AOs), radar data (ANSPs), position reports (AOs) and meteorological data – i.e. real-time or near real-time information to refine 4D flight profiles
  ETFMS calculates traffic demand in every sector & airport in NM AREA
  Computed Assisted Slot Allocation (CASA) – calculates & allocates slots
2 main functions

## Slide 50: Enhanced Traffic Flow Management System
ETFMS
  Contingency!
  03APR18 – live flight data deleted (instead of test environment data):
    1026 outage occurred
    1226 contingency plan started
    1300 cause of the technical failure was identified
    Deleted FPLs resubmitted by airspace users
    1800 ETFMS returned to operational status
Network capacity
-10%

## Slide 51: Slot management
Heathrow – Frankfurt example: two congested airports, so regulation not unusual
  At time of ACK message, EOBT 1500, so with taxi-out time ETOT 1515 (EOBT remains unchanged unless flight is regulated)
  IFPS must be notified of any change to EOBT of more than 15 minutes
    Later EOBT – AO to send DLA (Delay) or CHG (Change) message
    Earlier EOBT – AO to send CNL (Cancel) message, receive ACK message back from IFPS, AO then submits a new flight plan with new EOBT
    Filed EOBT should always reflect the off-block time wanted by AO
Note: generic slot messaging shown. Slightly different slot
messaging is used at A-CDM airports such as LHR and FRA.

## Slide 52: Slot management
Heathrow – Frankfurt example, two congested airports, so regulation not unusual
  Slot Issue Time (SIT1) -2H before EOBT
  If slot issued, Slot Allocation Message (SAM) sent to AO & ATC (dep airport)
    SAM example – regulation due to weather (REGCAUSE ..) at Frankfurt (REGUL ..)
    ETOT 1515 becomes CTOT 1540 (take-off between -5 min & +10 min)
    Target Time Over (TTO KONAN 1603) is recent addition – a step towards EFPL
-TITLE SAM
-ARCID KTN153
-IFPLID AA99990000
-ADEP EGLL
-ADES EDDF
-EOBD 190408
-EOBT 1500
-CTOT 1540
-REGUL EDDFA09
-TTO -PTID KONAN -TO 1603 -FL F249
-TAXITIME 0015
-REGCAUSE WA 84
Note: generic slot messaging shown. Slightly different slot
messaging is used at A-CDM airports such as LHR and FRA.

## Slide 53: Slot management
AO response to slot allocation for a flight includes (other than comply with CTOT):
  Slot Missed Message (SMM)
    SAM cannot be achieved & new EOBT unknown (NM: CTOT cancelled; suspend flight)
  Modification message (CHG)
    SAM cannot be achieved & new EOBT is known
  ETFMS default – all flights Ready/Request For (direct) Improvement (RFI), however AO can change to Slot Improvement Proposal Wanted status with a SIP message
    Subsequent improvements then need to be accepted or rejected by AO (i.e. no longer automatic acceptance)
  If aircraft doors are closed & ready to depart, AO can request local ATC to send a Ready message (REA)
    AO unable to send such messages
AO can also consider re-routing options
Simplified!
Note: generic slot messaging shown. Slightly different slot
messaging is used at A-CDM airports such as LHR and FRA.

## Slide 54: Slot management
Further messages from ETFMS relating to slot allocation for a flight include:
  Slot Requirement Cancellation message (SLC)
    Flight no longer regulated (good news!)
  Slot Revision Message (SRM)
    Changing the CTOT
  Re-routing Proposal message (RRP)
    A new route is offered that changes EOBT, or removes regulation
  (If applicable) Slot Improvement Proposal message (SIP)
    If SIP status requested by AO – AO must accept or reject new CTOT
Note: generic slot messaging shown. Slightly different slot
messaging is used at A-CDM airports such as LHR and FRA.

## Slide 55: Slot management
ATFM statistics 2018:
  Total flights: 11.0m
  Regulated flights: 2.4m
Year | 2014 | 2015 | 2016 | 2017 | 2018
Regulated flights | 8.6% | 11.0% | 13.8% | 15.5% | 21.8%

## Slide 56: Extended flight plan

## Slide 57: Extended flight plan
A look ahead to the extended flight plan (EFPL)
  Limitations with current flight plan:
    Low resolution due to minimum requirements cf. AO operational flight plan (OFP)
    As with 2012 changes, revisions to flight plan have seen information added to item 18 (other information)
  SESAR solution = extended flight plan (by end of 2021?)
    Will include planned 4D trajectory as calculated by AO (increased accuracy)
    4D trajectory information will include flight-specific performance data, e.g.
      aircraft speed & mass for each point
      climb/descent capabilities of individual aircraft
OFP

## Slide 58: Extended flight plan
A look ahead to the extended flight plan (EFPL)
  EFPL expected benefits:
    Executed trajectory closer to AO’s preference
    Flight crew & ATM using same 4D profile, supplied by AO’s Flight Operations Centre
    Improved traffic predictions for flow management – improved 4D accuracy (+safety)
    Reduced NM workload – fewer filing rejections; fewer manual interventions
    Reduced ATCO workload – improved 4D accuracy helping conflict detection/resolution & Arrival Manager (AMAN) operations
  SESAR trials / eventual ICAO standardisation
    Note: EFPL message will be longer than current FPL – message distribution system improvements are required (AFTN/SITA/new web service?)

## Slide 59: Suggested reading
Latest editions
  EUROCONTROL ATFCM USERS MANUAL
    Ed.23.0 (MAY19)
  EUROCONTROL IFPS USERS MANUAL
    Ed.23.0 (MAY19)
  ICAO Doc 4444 Procedures for Air Navigation Services – Air Traffic Management (‘PANS-ATM’)
    16th Ed. (2016)

## Slide 60
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com