## Slide 1: Introduction to ATM Air Traffic Flow Management (ATFM)
Luis Delgado
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Measures for capacity and demand regulations

## Slide 3
ANS
AS
FIS
ATC
ASM
ATFM
ATS
AIP
NOTAM
CIRC
CNS
MET
S&R
AIS
ATM
ANS: Air Navigation Services
CNS: Communications, Navigation and Surveillance
ATM: Air Traffic Management
S&R: Search and Rescue
AIS: Air Information Services
MET: Meteorological Services
ASM: AirSpace Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services
AIP: Aeronautical Information Publications
NOTAM: Notices to Airmen
CIRC: Circulars
AS: Alert Services
FIS: Flight Information Services
ATC: Air Traffic Control

## Slide 4: Introduction – Airspace Management
ANS
AS
FIS
ATC
ASM
ATFM
ATS
AIP
NOTAM
CIRC
CNS
MET
S&R
AIS
ATM
ANS: Air Navigation Services
CNS: Communications, Navigation and Surveillance
ATM: Air Traffic Management
S&R: Search and Rescue
AIS: Air Information Services
MET: Meteorological Services
ASM: AirSpace Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services
AIP: Aeronautical Information Publications
NOTAM: Notices to Airmen
CIRC: Circulars
AS: Alert Services
FIS: Flight Information Services
ATC: Air Traffic Control

## Slide 5: Introduction – Airspace Management
Bill Larkins

## Slide 6: Introduction – Airspace Management
Bill Larkins

## Slide 7: Introduction – Airspace Management

## Slide 8: Introduction – Airspace Management

## Slide 9: Introduction – Airspace Management

## Slide 10: Introduction – Airspace Management

## Slide 11: Introduction – Airspace Traffic Services
ANS
AS
FIS
ATC
ASM
ATFM
ATS
AIP
NOTAM
CIRC
CNS
MET
S&R
AIS
ATM
ANS: Air Navigation Services
CNS: Communications, Navigation and Surveillance
ATM: Air Traffic Management
S&R: Search and Rescue
AIS: Air Information Services
MET: Meteorological Services
ASM: AirSpace Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services
AIP: Aeronautical Information Publications
NOTAM: Notices to Airmen
CIRC: Circulars
AS: Alert Services
FIS: Flight Information Services
ATC: Air Traffic Control

## Slide 12: Introduction – Airspace Traffic Services
Air Traffic Services Objectives
  Prevent collision between aircraft (air and ground)
  Expedite and maintain an orderly flow of air traffic
  Provide advice and information useful for the safe and efficient conduct of flights
  Notify appropriate organisations regarding aircraft in need of search and rescue aid, and assist such organisations as required
ICAO Annex 11: Air Traffic Services
ICAO Doc. 4444: Procedures for Air Navigation Services: Air Traffic Management.
ATC
FIS
AS

## Slide 13: Introduction – Air Traffic Flow Management
ANS
AS
FIS
ATC
ASM
ATFM
ATS
AIP
NOTAM
CIRC
CNS
MET
S&R
AIS
ATM
ANS: Air Navigation Services
CNS: Communications, Navigation and Surveillance
ATM: Air Traffic Management
S&R: Search and Rescue
AIS: Air Information Services
MET: Meteorological Services
ASM: AirSpace Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services
AIP: Aeronautical Information Publications
NOTAM: Notices to Airmen
CIRC: Circulars
AS: Alert Services
FIS: Flight Information Services
ATC: Air Traffic Control

## Slide 14: Introduction – Air Traffic Flow Management
ATFM: Air Traffic Flow Management
  Additional service to ATS aiming at improving safety, throughput and efficiency
ATFCM: Air Traffic Flow and Capacity Management
  ATFM + aiming at using as much as possible ATS capacity
  Keep forecast demand1 below estimated capacity at airports and airspace sectors
  1 Due to their easier predictability, for ATFM purposes, only IFR flights are considered when computing demand forecasts

## Slide 15: Introduction – Air Traffic Flow Management
Additional objectives
  Management of network systems infrastructure
  Monitoring of network operations
  Keep the Network Operations Plan updated
  Network capacity optimisation
  Maximise use of available resources and coordination (CDM)

## Slide 16: Introduction – Air Traffic Management
ASM
ATFM
ATS
ATM
ATM: Air Traffic Management
ASM: Air Space Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services
ATFM
Airspace/Route Availability
ATC
ASM
Traffic Demand
ATC Capacity

## Slide 17: Introduction – Air Traffic Management
ASM
ATFM
ATS
ATM
ATM: Air Traffic Management
ASM: Air Space Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services

## Slide 18: Capacity and demand problem

## Slide 19: Capacity and demand problem
Capacity problem – Airport
Capacity problem – Airspace

## Slide 20: Capacity problem – Airspace
Top of Climb (TOC, T/C)
Top of Descent (TOD, T/D)
Climb
Descent
Cruise

## Slide 21: Capacity problem – Airspace
Flight Information Regions (FIR) / Upper Information Regions (UIR)

## Slide 22: Capacity problem – Airspace
Air Traffic Control
  Volume of airspace under the responsibility of one controller (usually helped by one or two extra controllers)
  A radio communications frequency is assigned to each different sector
  “Hand off” and “Hand over”: Transfer of aircraft responsibility between controllers of adjacent sectors
S3
S2
S1

## Slide 23: Capacity problem – Airspace
Controller workload: principal constraint on airspace capacity
Capacity might be reduced significantly in presence of severe weather
Controller workload is difficult to compute:
  Capacity defined as number of aircraft simultaneously in sector, or number of aircraft crossing sector per unit of time
S3
S2
S1

## Slide 24: Capacity problem – Airspace

## Slide 25: Capacity problem – Airspace

## Slide 26: Capacity problem – Airspace

## Slide 27: Capacity problem – Airspace
altitude

## Slide 28: Capacity problem – Airspace

## Slide 29: Capacity problem – Airspace
altitude

## Slide 30: Capacity problem – Airspace
Numerous factors affect complexity of controllers’ task
  Airspace factors
  Traffic factors
  Operational constraints

## Slide 31: Capacity problem – Airspace
Airspace constraints typically have a less severe effect on airline operations than airport constraints (especially true in US)
 a capacity-constrained en-route sector can often be by-passed at limited cost by selecting an alternative route, whereas a flight has no choice but to eventually end up at its destination airport

## Slide 32
R1
R2
R3
1 – F1R3
2 – F2R1
1
2
3
4
5
6

## Slide 33
R1
R2
R3
1 – F1R1
2 – F2R3
3 – F3R2
4 – F4R1
5 – F5R3
6 – F6R3
7 – F7R2

## Slide 34
R1
R2
R3
R1
R2
R3
R1
R2
R3
R1
R2
R3
R1
R2
R3
R1
R2
R3
R1
R2
R3
R1
R2
R3
R1
R2
R3
1
2
3
4
5
6
7
8
9

## Slide 35
S1
R1
R2
R3
S1
S2
R1
R2
R3
S2
S3
S1
R1
R2
R3
S1
S2
R1
R2
R3
2A
1A
3A
2B
C1
C2
C1
C4
C2
C2
C3
C2

## Slide 36
S1
R1
R2
R3
S1
S2
R1
R2
R3
S2
S3
S1
R1
R2
R3
S1
S2
R1
R2
R3
2A
1A
3A
2B
C1
C2
C1
C4
C2
C2
C3
C2

## Slide 37
1
2
3
4
5
1
2
3
4
5
6
7
8
9
S1
1A
S1
S1
S1
S1
S1
S1
S1
S1

## Slide 38
1
2
3
4
5
1
2
3
4
5
6
7
8
9
S2
S1
2A

## Slide 39
S1
R1
R2
R3
S1
S2
R1
R2
R3
S2
S3
S1
R1
R2
R3
S1
S2
R1
R2
R3
2A
1A
3A
2B
C1
C2
C1
C4
C2
C2
C3
C2

## Slide 40
1
2
3
4
5
1
2
3
4
5
6
7
8
9
S2
S1
S1
S1
S1
S2
2A

## Slide 41
1
2
3
4
5
1
2
3
4
5
6
7
8
9
S2
S1
S2
2B
S2

## Slide 42
1
2
3
4
5
1
2
3
4
5
6
7
8
9
S2
S1
3A
S1
S2

## Slide 43
1A
2A
2B
3A
1
2
3
4
5
6
7
8
9
Opening scheme

## Slide 44
1A
2A
2B
3A
1
2
3
4
5
6
7
8
9
S1
S2
S2
S1
S1
S1
S2
S1
S1
S1
S1
S1
S1
S1
S1
Opening scheme

## Slide 45
1A
2A
2B
3A
1
2
3
4
5
6
7
8
9
Opening scheme

## Slide 46
1A
2A
2B
3A
1
2
3
4
5
6
7
8
9
Opening scheme
4 controllers available

## Slide 47
1A
2A
2B
3A
1
2
3
4
5
6
7
8
9
S2
S2
S1
S1
S1
S2
S1
S1
S1
S1
S1
S1
S1
S1
Opening scheme

## Slide 48
1A
2A
2B
3A
1
2
3
4
5
6
7
8
9
S2
S2
S1
S1
S1
S2
S1
S1
S1
S1
S1
S1
S1
S1
Opening scheme
ATFM
Regulation
Due to staffing issues
Due to capacity issues

## Slide 49
If demand exceeds capacity
  Try to change sector/airport configuration, or increase open sectors (increase capacity)
  Manage Flows: apply an ATFM initiative (regulation)
Ground delays are “cheaper” than air delays (re-routing or air holding)!!
Some flights might be exempted from ATFM measures

## Slide 50: Air Traffic Flow Management – Increase capacity
Airspace sectorisation: Barcelona FIR example

## Slide 51: Air Traffic Flow Management – Increase capacity
Airspace sectorisation: Barcelona FIR example

## Slide 52: Air Traffic Flow Management
Airport capacity-demand imbalance
  Regulations affect aircraft inbound to the congested airport
Airspace capacity-demand imbalance
  Regulations affect aircraft flying into the congested airspace sector (number of aircraft in sector, number departures/arrivals in TMA,…) or airway (flow in a given waypoint/airway,…)

## Slide 53: Air Traffic Flow Management – ATFM initiatives
Ground Stop (GS)
Ground delay Programs (GDP)
Airspace Flow Programs (AFP)
Collaborative Trajectory Options Programs (CTOP)
Severe Weather Avoidance Programs (SWAP)
Voluntary required re-routing
Miles in Trail (MIT)
Minutes in Trail (MINIT)
Minimum Departure Interval (MDI)
Metering (Time Based Metering (TBM))
Departure/en-route/arrival spacing (DSP, ESP, ASP)
Longitudinal, lateral and vertical tactical measures used by ATC
FL capping (FL)
Re-routings (RR)
Alternative routing scenarios (AR)
EU Restrictions
ATFM regulations

## Slide 54: Air Traffic Flow Management – ATFM initiatives
Ground Stop (GS)
Ground delay Programs (GDP)
Airspace Flow Programs (AFP)
Collaborative Trajectory Options Programs (CTOP)
Severe Weather Avoidance Programs (SWAP)
Voluntary required re-routing
Miles in Trail (MIT)
Minutes in Trail (MINIT)
Minimum Departure Interval (MDI)
Metering (Time Based Metering (TBM))
Departure/en-route/arrival spacing (DSP, ESP, ASP)
Longitudinal, lateral and vertical tactical measures used by ATC
FL capping (FL)
Re-routings (RR)
Alternative routing scenarios (AR)
EU Restrictions
Delay TMI
TMI – L2 (ATFM)
TMI – L3
TMI – L4

## Slide 55: Air Traffic Flow Management – ATFM slot
Delay assignment (Europe/AFP/GDP)
B. Manley and L. Sherry, “The Impact of Ground Delay Program (GDP) Rationing Rules on Passenger and Airline Equity”, 3rd International Conference on Research in Air Transportation, ICRAT 2008, Fairfax, VA, June 01-04, 2008

## Slide 56: Air Traffic Flow Management – ATFM slot
Delay assignment (Europe/AFP/GDP)
If there is an imbalance between capacity and demand:
  Delay is needed
If nothing is done, the delay will be in the air
  Re-routing to avoid congested areas
  Holding at destination
   High fuel consumption
   Ground delay is a better approach

## Slide 57: Air Traffic Management – ATFM slot
EOBT: Estimated Off-Block Time
ETOT: Estimated Take-Off Time
ETO: Estimated Time Over
TT: Taxi Time
Trip Time
ETOT
ETO
TT
EOBT
Expected Delay

## Slide 58: Air Traffic Management – ATFM slot
EOBT: Estimated Off-Block Time
ETOT: Estimated Take-Off Time
ETO: Estimated Time Over
TT: Taxi Time
Trip Time
ETOT
ETO
TT
EOBT
COBT: Calculated Off-Block Time
CTOT: Calculated Take-Off Time
CTO: Calculated Time Over
Trip Time
CTOT
Ground Delay
EOBT
TT
COBT
CTO
Actual take-off time between [CTOT-5 min, CTOT + 10 min]
TWR controllers will enforce take-off within the limits

## Slide 59: Air Traffic Management – Delay assignment
Computed Assisted Slot Allocation (CASA)
  Slot allocation algorithm (example)
Flight | ETO
F1 | 10:00
F2 | 10:06
F3 | 10:07
F4 | 10:10
F5 | 10:12
F6 | 10:18
Slot 1
Slot 2
Slot 3
Slot 4
Slot 5
Slot 6
Slot 7
10:05
10:10
10:15
10:20
10:25
10:30
10:00
Regulated Sector
ETO computed based on flight schedule
ETO: Estimated Time Over

## Slide 60
Air Traffic Management - ATFM
Slot 1  F1
Slot 2
Slot 3
Slot 4
Slot 5
Slot 6
Slot 7
Flight | ETO
F1 | 10:00
F2 | 10:06
F3 | 10:07
F4 | 10:10
F5 | 10:12
F6 | 10:18
10:00
10:05
10:10
10:15
10:20
10:25
10:30
ETO: Estimated Time Over
Regulated Sector
Computer Assisted Slot Allocation
Slot Allocation Algorithm (example)

## Slide 61
Air Traffic Management - ATFM
Flight | ETO
F1 | 10:00
F2 | 10:06
F3 | 10:07
F4 | 10:10
F5 | 10:12
F6 | 10:18
Slot 1  F1
Slot 2  F2
Slot 3
Slot 4
Slot 5
Slot 6
Slot 7
10:00
10:05
10:10
10:15
10:20
10:25
10:30
Regulated Sector
Computer Assisted Slot Allocation
Slot Allocation Algorithm (example)
ETO: Estimated Time Over

## Slide 62
Air Traffic Management - ATFM
Flight | ETO
F1 | 10:00
F2 | 10:06
F3 | 10:07
F4 | 10:10
F5 | 10:12
F6 | 10:18
Slot 1  F1
Slot 2  F2
Slot 3
Slot 4
Slot 5
Slot 6
Slot 7
10:00
10:05
10:10
10:15
10:20
10:25
10:30
Regulated Sector
Computer Assisted Slot Allocation
Slot Allocation Algorithm (example)
ETO: Estimated Time Over

## Slide 63
Air Traffic Management - ATFM
Flight | ETO
F1 | 10:00
F2 | 10:06
F3 | 10:07
F4 | 10:10
F5 | 10:12
F6 | 10:18
Slot 1  F1
Slot 2  F2
Slot 3  F3
Slot 4
Slot 5
Slot 6
Slot 7
10:00
10:05
10:10
10:15
10:20
10:25
10:30
Regulated Sector
Computer Assisted Slot Allocation
Slot Allocation Algorithm (example)
ETO: Estimated Time Over

## Slide 64
Air Traffic Management - ATFM
Flight | ETO | Delay
F1 | 10:00 | 0 min
F2 | 10:06 | 0 min
F3 | 10:07 | 3 min
F4 | 10:10 | 5 min
F5 | 10:12 | 8 min
F6 | 10:18 | 7 min
Slot 1  F1
Slot 2  F2
Slot 3  F3
Slot 4  F4
Slot 5  F5
Slot 6  F6
Slot 7
10:00
10:05
10:10
10:15
10:20
10:25
10:30
Regulated Sector
Computer Assisted Slot Allocation
Slot Allocation Algorithm (example)
ETO: Estimated Time Over

## Slide 65: Air Traffic Flow Management – ATFM initiatives
CAPACITY
ROUTING
ATC STAFFING
AIRPORT CAPACITY
MILITARY ACTIVITY
OTHER
ALL
WEATHER

## Slide 66: Air Traffic Flow Management – ATFM initiatives

## Slide 67: Air Traffic Flow Management – ATFM initiatives
Network Manager Operations Centre
ACC
FMP
ACC
FMP
ACC
FMP
ACC
FMP
Network
Manager
ACC: Area Control Centre
FMP: Flow Management Position

## Slide 68: Air Traffic Flow Management – ATFM initiatives
Network Manager Operations Centre

## Slide 69: Air Traffic Management – Phases
ATFM Phases
Strategic Phase Matches long-term demand and needed ATC capacity
Pre-tactical Phase Balances flights next day with available ATC Capacity
Tactical Phase Manage current flights with existing ATC capacity
The capacity commitments of every operational stakeholder in the network are reflected in a common planning document: the Network Operations Plan (NOP)
Daily Plan of ATFCM measures on the NOP Portal
Tactical updates in the NOP Portal

## Slide 70: Air Traffic Management – ATFM
Network Operations Portal
http://www.public.nm.eurocontrol.int/PUBPORTAL/gateway/spec/index.html

## Slide 71: Air Traffic Management
ASM
ATFM
ATS
ATM
ATM: Air Traffic Management
ASM: Air Space Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services

## Slide 72: Capacity problem – Airport

## Slide 73: Capacity problem – Airport
Top of Climb (TOC, T/C)
Top of Descent (TOD, T/D)
Climb
Descent
Cruise

## Slide 74: Capacity problem – Airport
Airport as a system of systems:
  Runways
  Taxiways
  Apron stands
  Passenger and cargo terminals
  Ground access complexes

## Slide 75: Capacity problem – Airport
Airport as a system of systems:
  Runways
  Taxiways
  Apron stands
  Passenger and cargo terminals
  Ground access complexes

## Slide 76: Capacity problem – Airport
Airport as a system of systems:
  Runways
  Taxiways
  Apron stands
  Passenger and cargo terminals
  Ground access complexes
Each one has its own capacity limitations
Capacity at airport limited by most limiting subsystem
BUT, at major airports:
  Capacity of system of runways = most restricting element
While it is usually possible to increase capacity of the other airport elements, adding a new runway (+ associated taxiways) is very expensive and takes a very long time to complete

## Slide 77: Capacity problem – Airport
Runway capacity: principal cause of most extreme instances of delays that lead to widespread schedule disruptions, flight cancellations and missed connections
Runway capacity: varies greatly from day-to-day and changes are difficult to predict (even a few hours in advance)
This creates an unstable operating environment

## Slide 78: Capacity problem – Airport
Difference between
  Strategic airport capacity
  Pre-tactical airport capacity
  Tactical airport capacity

## Slide 79: Capacity problem – Airport
Difference between
  Strategic airport capacity (scheduling at airports)
    Three levels of airports
      Level 1: Non-coordinated airport (capacity/demand ok)
      Level 2: Schedules facilitated airport (capacity/demand imbalance at time periods)
      Level 3: Coordinated airport (must have allocated slot to operate)
US | Europe
2 airports Level 3 (JFK and EWR) 4 airports Level 2 (ORD, LAX, MCO, SFO) Use of Special Traffic Management Programs | 100 airports Level 3 70 airports Level 2

## Slide 80: Capacity problem – Airport
Difference between
  Strategic airport capacity
  Pre-tactical airport capacity
B. Manley and L. Sherry, “The Impact of Ground Delay Program (GDP) Rationing Rules on Passenger and Airline Equity”, 3rd International Conference on Research in Air Transportation, ICRAT 2008, Fairfax, VA, June 01-04, 2008

## Slide 81: Capacity problem – Airport
Difference between
  Strategic airport capacity
  Pre-tactical airport capacity
  Tactical airport capacity
P.B. Liu, M. Hansen and A. Mukherjee, “Scenario-based air traffic flow management: From theory to practice”, Transportation research Part B, Vol. 42, 2008, p.p. 685-702.

## Slide 82: Additional material

## Slide 83: Examples of capacity factors at airports
Factors affecting airport capacity of a single runway
Capacity of a single runway depends on many factors, most importantly:
Mix of aircraft classes using airport
Separation requirements imposed by the ATM system
Type (high speed or conventional) and location of exits from the runway
Mix of movements on each runway (arrivals only, departures only, or mixed) and sequencing of movements
Weather conditions, namely visibility, cloud ceiling and precipitation
Technological state and overall performance of the ATM system

## Slide 84: Examples of capacity factors at airports
Mix of aircraft classes using airport
Classification of aircraft into classes for terminal area ATC purposes based on maximum take-off weight (MTOW)
  heavy class: all wide-body jets
  medium/large class: narrow-body commercial jets + some of larger commercial turbo-props
  small class: most general aviation airplanes, most types of private jets, + smaller commercial turboprops and regional jets
Aircraft mix indicates composition of aircraft fleet using any particular runway (eg., 25% S, 60% L, and 15% H)

## Slide 85: Examples of capacity factors at airports
Separation requirements imposed by the ATM system
Wing tip vortices

## Slide 86: Examples of capacity factors at airports
Separation requirements imposed by the ATM system

## Slide 87: Capacity problem – Airport
Type (high speed or conventional) and location of exits from runway

## Slide 88: Examples of capacity factors at airports
Type (high speed or conventional) and location of exits from runway
trailing aircraft of any pair can not touch down on the runway before leading aircraft is clear of the runway  “single occupancy”
more restrictive of the two requirements: “airborne separation” & “single occupancy” applies for each pair of aircraft
high-speed runway exits + well-placed runway exits: reduce runway occupancy times for arriving aircraft  increasing runway capacity
high-speed exits also useful when runway used for both arrivals and departures: if landing aircraft can exit a runway quickly, ATC may be able to “release” a following take-off sooner

## Slide 89: Examples of capacity factors at airports
Mix of movements on each runway and the sequencing of the movements
Separation requirements: specified for all combinations of consecutive operations
      A-A, A-D, D-A and D-D
Separation requirements for each combination are different:
  Capacity of runway during any given time period depends on mix of arrivals and departures during that period
  Trade-off between maximum arrival and departure rates that an airport can achieve

## Slide 90: Examples of capacity factors at airports
Weather conditions
P.B. Liu, M. Hansen and A. Mukherjee, “Scenario-based air traffic flow management: From theory to practice”, Transportation research Part B, Vol. 42, 2008, p.p. 685-702.

## Slide 91: Examples of capacity factors at airports
Technological state and overall performance of the ATM system

## Slide 92: Examples of capacity factors at airports
For multiple runways we also need to take into account:
lateral separation, especially in bad weather, between aircraft approaching the same airport on parallel runways
sequencing and separation of departing and landing aircraft on runways that intersect (eg., at LaGuardia)
sequencing of aircraft approaching airports located in close proximity to one another where 1 aircraft must cross the path of another aircraft landing at a nearby airport (eg., Chicago, Los Angeles and New York)
direction and strength of winds
noise-related and other environmental considerations and constraints

## Slide 93: Examples of capacity factors at airports
Lateral separation

## Slide 94: Examples of capacity factors at airports
Sequencing and separation of departing and landing aircraft on runways that intersect

## Slide 95: Examples of capacity factors at airports
Airports in close proximity (+8)
Passenger volume: 66,790,996 [FAA 2011]

## Slide 96: Examples of capacity factors at airports
Airports in close proximity (+8)
Passenger volume: 18,883,170 [FAA, 2011]

## Slide 97: Examples of capacity factors at airports
Airports in close proximity (+8)
25 miles driving (<1h by car)

## Slide 98: Examples of capacity factors at airports
direction and strength of winds
Aircraft departing and landing towards wind

## Slide 99: Examples of capacity factors at airports
noise-related and other environmental considerations and constraints

## Slide 100: Examples of capacity factors at airports
noise-related and other environmental considerations and constraints

## Slide 101: Examples of capacity factors at airports
noise-related and other environmental considerations and constraints

## Slide 102: Examples of capacity factors at airports
noise-related and other environmental considerations and constraints

## Slide 103: Examples of capacity factors at airports
noise-related and other environmental considerations and constraints

## Slide 104: Capacity problem – Airport
Airport capacity curve: can be obtained from historical airport performances
Set of points obtained over a long period of time (e.g. 1 month or +)
Capacity curve obtained by piece-wise linear convex curve
Curve 1: extreme points occur at least once
Curve 2: extreme points occur at least twice
Curve 3: extreme points occur at least 3 times  + robust

## Slide 105: Capacity problem – Airport
Airport capacity curve: can be obtained from historical airport performances
Set of points obtained over a long period of time (e.g. 1 month or +)
Capacity curve obtained by piece-wise linear convex curve
arrival
departure

## Slide 106: Capacity problem – Airport
Airport capacity curve: departure arrival trade-offs
“free-departures” point
equal number of departures and arrivals through A-D-A-D-A… sequence
departure only
arrival only
V. Butler, Increasing Airport Capacity Without Increasing Airport Size, 2008

## Slide 107
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com