## Slide 1: Introduction to ATM Performance measurement in ATM
Andrew Cook
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Performance measurement in ATM Overview
Background
Major frameworks impacting Europe
Current performance
Challenges ahead
Notes
Notes: There is a selection of additional information and resources at the end.
Note also that throughout the slides there are hyperlinks and references to websites, and selected further material in the slides at the end of the presentation.

## Slide 3: Background

## Slide 4: Background Why measure?
Lord Kelvin
(Sir William Thomson)
1824 – 1907
When you can measure what you are speaking about, and express it in numbers, you know something about it, when you cannot express it in numbers, your knowledge is of a meagre and unsatisfactory kind.
Some day, no doubt, some one will invent a flying machine that one will be able to navigate without having to have a balloon attachment.

## Slide 5: Background An overview
EUROCONTROL
Early 2000s, bad delays
Single European Sky (SES)
Performance Review Body
(regulation)
SESAR
(technology)


SES
Performance Scheme
SESAR
Performance Framework
ICAO
Notes: This slide introduces the two key players of the presentation: the SES Performance Scheme and the SESAR Performance Framework.
We will learn about them as we go along, and, at the end, compare and contrast their key properties.
Where did they come from? As a result of bad delays in the eary 2000s, the Single European Sky inititative was launched by the Europrean Commission.
It is founded on four original pillars.
We will look at its objectives and pillars in the next two slides.
EUROCONTROL, ICAO and the Performance Review Body are key actors in this context. We will meet the PRB in a moment.
Interoperability is a key factor. ICAO is at the core of this, e.g. with its Global Air Navigation Plan (GANP) – see also the ‘selected ICAO documents and alignment’ additional slides at the end of the presentation.
The role of EUROCONTROL is ubiquitous, from supporting the Performance Review Body, to leading research across the SESAR programme, and managing the ATM network as the ‘Network Manager’.

## Slide 6: Background The Single European Sky (SES)
Launched by the European Commission in 2004, to:
  reform the architecture of European ATM
  address issues at a European, rather than local, level
  legislative approach to meet future capacity and safety needs
Key objectives, to:
  “restructure European airspace as a function of air traffic flows”
  “create additional capacity”
  “increase the overall efficiency of the ATM system”
High-level, ambitious goals (“political targets”), aka SES ‘2005 vision’* for 2020:
  x3 increase in capacity (reducing delays)
  x10 improvement in safety
  10% reduction of flights’ impact on environment
  ≥ 50% reduction in costs of ATM services to airspace users
* EC, Nov. 2005. Announced during public announcement of SESAR Definition Phase contract, by EC Vice-President Jacques Barrot.
through
SES pillars
+ ‘indirect’ effects
Notes: These four high-level goals are important, and you should remember them.

## Slide 7: Background The SES pillars
First pillar: regulating performance; three measures:
  establish an independent performance review body (PRB)
  functional airspace blocks: targeted by end of 2012*
  strengthening the network management function (e.g. slot coordination)
Second pillar: single safety framework
  extend role of European Aviation Safety Agency (EASA)
Third pillar: new technologies – SESAR:
  define, develop & deploy that which needed to increase ATM performance
Fourth pillar: managing capacity on the ground
  investment in airport capacity to remain aligned with air transport capacity
Fifth pillar: human factors (e.g. ensuring changes are acceptable to operational staff)
* Slow progress re. original planning evolved into emphasis on virtualisation (e.g. remote centres) and cooperation irrespective of borders
Notes: There are further slides on the PRB in the additional information and resources slides at the end.
You will have already appreciated during these lectures the fundamental importance of SESAR. You will hear a lot more about it as we go along.
The fifth pillar was added later (SES II) and does not appear in quite a lot of the documentation.

## Slide 8: Major frameworks impacting Europe

## Slide 9: Major frameworks impacting Europe ICAO Manual on global performance (‘Doc 9883’)
Objective of Doc 9883
To support harmonised terminologies in ‘performance-based’ assessment: focus on desired results, with decision-making driven by results and data
Useful definitions
(Key) Performance indicator ((K)PI)
  quantitatively expresses current/past/expected performance
  since indicators support objectives, they should be defined having progress towards a specific performance objective in mind
  indicators are not often directly measured; they are calculated from supporting metrics according to clearly defined formulas
    e.g. cost-per-flight indicator = ∑ (costs) / ∑ (flights)
Key performance area (KPA)
  a way of categorising performance subjects related to high-level ambitions and expectations; ICAO has defined 11 KPAs, e.g. ‘safety’
Performance framework
  set of definitions & terminology describing the building blocks used by a group of ATM community members to collaborate on performance management
cf. SES(AR): KPI => target
Notes: You should be able to define a KPI, a KPA and a performance framework,
This slide gives the background definitions made by ICAO.
Note that in the SES and SESAR context, a KPI usually has an associated target. This was not part of the ICAO definition.

## Slide 10: Major frameworks impacting Europe What makes a good indicator?
Desirable qualities
Intelligible
  preferably to the point of being simple
Pertinent
  accurately reflect the aspect of performance being measured
Stable
  can’t refine them from one period to another without losing comparability
Some challenges
indicators often limited by data availability
may be difficult to respond to new data or methods, and maintain stability
if (too) simple, may not afford the best understanding of system dynamics
trade-offs between these desirable properties often necessary
avoiding proliferation – adding new indicators only where added value is clear
For further discussion, see:
Cook A, Tanner G and Zanin M, 2013. Towards superior air transport performance metrics – imperatives and methods.
Journal of Aerospace Operations, 2, 3–19.
Notes: Why not try first thinking about desirable qualities of an indicator, and then look back at this slide afterwards?

## Slide 11: Major frameworks impacting Europe ICAO Global ATM operational concept (‘Doc 9854’)
KPA | Name | Meaning
1 | Access and equity | 
2 | Capacity | 
3 | Cost effectiveness | 
4 | Efficiency | 
5 | Environment | 
6 | Flexibility | 
7 | Global interoperability | 
8 | Participation | 
9 | Predictability | 
10 | Safety | 
11 | Security | 
Notes: Why not try first thinking about what these KPAs might refer to, before looking at the next slide. Is any area missing? (It should not be.)
What do we mean by a KPA trade-off? Can you think of examples of areas that cannot be improved at the same time?
There is currently particularly high international interest in global interoperability and predictability.

## Slide 12: Major frameworks impacting Europe ICAO Global ATM operational concept (‘Doc 9854’)
KPA | Name | Meaning
1 | Access and equity | “all airspace users have right of access to the ATM resources needed to meet their specific operational requirements [...] shared use of airspace by different users”
2 | Capacity | “meet airspace user demands at peak times and locations while minimizing restrictions on traffic flow [...] resilient to service disruption”
3 | Cost effectiveness | “cost of service [...] should always be considered when evaluating any proposal to improve ATM”
4 | Efficiency | “airspace users want to depart and arrive at the times they select and fly the trajectory they determine to be optimum”
5 | Environment | “contribute to the protection of the environment by considering noise, gaseous emissions and other environmental issues”
6 | Flexibility | “ability of all airspace users to modify flight trajectories dynamically and adjust dep. & arr. times”
7 | Global interoperability | “uniform principles [...] non-discriminatory global and regional traffic flows”
8 | Participation | “ATM community [...] continuous involvement in the planning, implementation and operation”
9 | Predictability | “ATM service providers to provide consistent & dependable levels of performance”
10 | Safety | “highest priority [...] uniform safety standards [...] applied systematically”
11 | Security | “protection against [...] intentional acts (e.g. terrorism) or unintentional acts (e.g. human error, natural disaster) ”
Notes: How did you do?
Regarding trade-offs, did you think of examples of areas that cannot be improved at the same time? A common example cited is capacity and environment. As more and more capacity is offered, it is challenging to reduce the environmental impact.
Note that we refer to the provision of capacity during peak times. Providing it off-peak, when demand is low, is rather easier! ‘Resilience’ is becoming a key word in ATM.

## Slide 13: Major frameworks impacting Europe SESAR: European ATM Master Plan (1/5)
European ATM Master Plan, Edition 2020:
https://www.atmmasterplan.eu/ SESAR (2019)
Main planning for ATM modernisation in Europe; major updates every few years
Defines development and deployment priorities for delivering SESAR
Sits within framework of Single European Sky, and EU Aviation Strategy
More capacity needed to reduce delays; integration of drones a challenge (‘U-space’); scalable systems, digitalisation (with better automation and connectivity) and trajectory-based operations are core elements, whilst maintaining safety and mitigating ENV impact
Notes: These slides are to offer a flavour of the content of the ATM Master Plan. You are strongly encouraged to have a look through it.

## Slide 14: Major frameworks impacting Europe SESAR: European ATM Master Plan (2/5)
Main chapters of the Master Plan
The SESAR vision
  Offering improvements across ATM
  Embracing the digital transformation of aviation
  Delivering a digital European sky in four phases
Performance view
  Delivering a fully scalable system that is even safer than today’s
  Confirming the 2035 Performance Ambitions for controlled airspace & airports
Operational view
  SESAR target concept
  Essential operational changes
  Delivering the digital European sky (phase D)
  Link to the global context*
  The role of the human
  Cybersecurity in a safety-oriented industry
Notes: The SESAR vision expands on the four-phase approach.
We will look at the performance view in a few slides’ time.
“The target concept envisages the integration of all aerial vehicles, with higher levels of automation and digital connectivity, coupled with more automated support for the management of air traffic. In this new paradigm, aircraft will fly their optimum trajectories, relying on improved data sharing between aircraft and the ground infrastructure using mobile, terrestrial and satellite-based communication links.” (Master Plan, Edition 2020.)
Note that the operation view includes ‘essential operational changes’ and discusses the global context (e.g. the link to ICAO).
The EOCs ... are the nine essential ‘game changers’ triggering structural evolutions of European ATM. They are required to deliver the SESAR vision up to and including Phase C, the defragmentation of European skies through virtualisation. The EOCs, listed below, are not independent of each other.
CNS infrastructure and services
ATM interconnected network
Digital AIM and MET services
U-space services
Virtualisation of service provision
Airport and TMA performance
Fully dynamic and optimised airspace
Trajectory-based operations
Multimodal mobility and integration of all airspace users

## Slide 15: Major frameworks impacting Europe SESAR: European ATM Master Plan (3/5)
Main chapters of the Master Plan (cont’d)
Deployment view
  How and when the SESAR vision should be deployed
  Deployment scenarios
  Stakeholder roadmaps supporting essential operational changes
  Infrastructure evolution in relation to CNS and spectrum
  Standardisation and the regulatory view
Business view
  Holistic view of SESAR net benefits for manned aviation
  Holistic view of SESAR net benefits for drones
  Incentivisation strategy
A four phase approach is also described (see slide notes)
Through SESAR Solutions
airport roadmap
essential operational changes
time
Notes: The key thing to note here is that most of the delivery in SESAR is through the SESAR Solutions.
“SESAR Solutions are the main output of the SESAR development activities. They are new or improved operational procedures or technologies that aim to contribute to the modernisation of the European and global ATM systems. These solutions address all parts of the ATM value chain, integrating operations on the ground and in the air, as well as the underlying system architecture and technological enablers, which are validated in real day-to-day operations. When a SESAR Solution reaches maturity and is ready for implementation, it is delivered to the aviation community for industrialisation and subsequent deployment. This deployment can be voluntary or mandated, local or coordinated across the network under EU regulatory frameworks, and may be supported by EU funding. Coordinated deployment may be opted for where the implementation of a change is critical to the performance of the European network. The first wave of Europe-wide coordinated deployment started in 2014 and was supported by a regulatory framework and funding from the EU; this deployment work was carried out primarily through the Pilot Common Project (PCP) and the associated deployment programme.” (Master Plan, Edition 2020.)
--------------------------------------------------------------------------------------------------------------------
Deployment scenarios relate to changes that are in the pipeline towards deployment and that are associated with EOCs. They are based on mature SESAR Solutions proposed for deployment, and Solutions approaching maturity. For each deployment scenario, the operating environment(s) in which performance gains can be realised are indicated, with a roll-out time and contribution to performance.
The business view in the Master Plan describes the monetised benefits and investment costs associated with the deployment of the full Master Plan vision for phases A to D. The last sub-section covers the topic of incentives: current and future.
Note
The Deployment Manager was established by the European Commission as a SES instrument, in 2014. It works closely with the SJU. It is responsible for the Management Level of the SESAR deployment governance, for the coordination of the implementation of the most essential SESAR operational improvements through the concept of ‘Common Projects’. The SESAR Deployment Alliance is the organisation selected by the Commission to perform the DM function until 31 December 2020. The SDA is a not-for-profit international association, composed of leading airlines, airports and air navigation service providers. A Common Project is an extraction from the European ATM Master Plan, based on mature SESAR Solutions to be deployed in a synchronised and timely manner across Europe, translated into European law. Whilst the European ATM Master Plan is indicative, a Common Project binds the Member States of the European Union and their operational stakeholders. The first Common Project is known as the Pilot Common Project (PCP).
--------------------------------------------------------------------------------------------------------------------
The SESAR vision is being realised in four progressive, overlapping phases. The phased approach takes into account that aviation is digitalising rapidly and that the supporting infrastructure needs to evolve based on shorter innovation cycles than previously. The descriptions below are extracts from the Master Plan, Edition 2020:
Phase A: address known critical network performance deficiencies by delivering solutions that enhance collaboration between stakeholders, including across state borders and with aircraft, implementing initial system-wide information management, and introducing network capacity and demand balancing measures.
Phase B: efficient services and infrastructure delivery through the launch of first ATM data services, the introduction of cross-border free-route operations, and the integration of advanced airport performance management into the network and the provision of initial U-space services.
Phase C: defragmentation European skies through virtualisation and dynamic airspace configuration, supported by the gradual introduction of higher levels of automation support, the full integration of airports into ATM at network level and the management of routine drone operations.
Phase D: digital European sky through the delivery of a fully scalable system for manned and unmanned aviation supported by a digital ecosystem, full air-ground system integration, distributed data services, and high levels of automation and connectivity.

## Slide 16: Major frameworks impacting Europe SESAR: European ATM Master Plan (4/5)
Notes: This a key table in the ATM Master Plan. It presents the “Performance Ambitions” of SESAR on the right-hand side of the table. The target year is 2035. The baseline is 2012, from an earlier edition of the Master Plan.
These “Performance Ambitions” are not binding (cf. the targets of the SES Performance Scheme, that we will meet later). They may be adapted, e.g. if traffic levels change significantly from forecast levels, noting that the look-ahead time (2035) is a lot further than the SES PS. Contributions from beyond SESAR are included and exogenous effects (e.g. increasing aircraft sizes and average flight times) are also taken into account.
A prominent Performance Ambition example is the reduction in delay, with a target improvement of 1-3 minutes per departure. We will investigate this further in the next slide.
On the left are shown the SES high-level goals that we met earlier, so that the reader can compare the goals and Ambitions across the rows, where applicable. An example is the 50% reduction in the unit costs (e.g. en-route charges) paid by the airlines. Their baseline year is 2005.
The Master Plan talks of SESAR contributing to ‘eliminating environmental inefficiencies’. The upper bound of the reduction (10%) corresponds to the SES target on the left.
The safety Ambition has been increased relative to the previous MP, now expressed as zero accidents with direct ATM contribution.
The Master Plan explains that: “Repeated contact and coordination with the Performance Review Body resulted in coordination of efforts between the technology and performance pillars of the SES to ensure the readability of the SESAR Performance Ambitions by the SES performance scheme. Efforts were also made to make more visible and explicit the link between the Master Plan’s priorities and key objectives and the EU’s aviation strategy.”

## Slide 17: Major frameworks impacting Europe SESAR: European ATM Master Plan (5/5)
SESAR 2035 Ambition: reduce total dep delay/flight by 1-3 mins
  2012: avg dep delay/flight = 9.5 mins
    of which, (in)directly due ATM & weather = 3.7 mins (appx.)
    these are the 3.7 mins that are thus being targeted
  assumes: 15.2 million flights by 2035†; delay growth α traffic
Main contribution to reduction expected from reactionary* delay
  i.e. knock-on* delay in the network
Reactionary reduction esp. associated with increased arrivals predictability by:
  reference business trajectories (agreed prior to push-back, as move to TBO)
  sharing airport operating plans between airports and Network Manager
† Appx. 60% cf. 2012. This will have to be revisited following the Covid-19 pandemic.

## Slide 18
EUROCONTROL
Early 2000s, bad delays
Single European Sky (SES)
Performance Review Body
(regulation)
SESAR
(technology)


SES
Performance Scheme
SESAR
Performance Framework
ICAO
Remember this?!
Notes: We started off with this slide earlier.
We have examined the SESAR technologies.
Let’s now focus on the SES Performance Scheme and the SESAR Performance Framework, the former first.

## Slide 19: Major frameworks impacting Europe SES Performance Scheme: basis
‘Natural monopoly’ – single supplier may offer lower prices than group of competitors
  often pertains with infrastructure industries / network services / utilities
  moot point: some ATM elements (e.g. tower services) cheaper if competitive?
  need regulation (incentives, sanctions) to stop abuse of market power
  ICAO (Doc 9082) gives States oversight and stresses performance delivered
Four main approaches to regulate prices (in a monopolistic situation):
  cost of service / rate of return (‘reasonable’) RoR, based on e.g. cost of capital and asset base
  price caps can usually retain profit within the cap
  revenue caps (also applied in SES PS)
  benchmarking / targets (binding performance targets are set in SES PS)
SES Performance Scheme and Charging Scheme at centre of SES policy, together designed to produce market conditions (lower charges) in monopoly context
Targets set in context of reliable forecasts, within envelopes (but cf. Covid-19)
  Performance Plans reviewed by Performance Review Body for Commission
    some elements of (1)-(4) above, but mostly (1) and (4)
    incentive schemes: too easily trigger bonuses, penalties too light (says PRB)
Notes: The SES Performance Scheme essentially sets out to overcome a potential downside (higher prices) of a market comprised of a series of monopolies (State service providers).
Of the four main approaches to protect against monopolies, (1) and (4) are the strongest elements of the SES Performance Scheme.
National performance plans are assessed by the Performance Review Body.

## Slide 20: Major frameworks impacting Europe SES Performance Scheme: past, current, future
RP | Effective | EU-wide binding KPIs (NB. Other PIs and monitoring are in place) |  |  | 
 |  | Safety | Environment | Capacity | Cost efficiency
1 | 2012-2014 (en-route focus) | N/A |  Average horizontal en-route flight efficiency re. last-filed flight plan (“KEP”) ... | Minutes of en-route ATFM delay: 0.5 min/flight (& national KPIs for airport ATFM arrival delay) | Average determined unit cost for e/r ANS  3.2% p/a (“original” target; 2009-2014)
2 | 2015-2019 (extended to gate-to-gate; safety added) |  Effectiveness of safety management (EoSM) & applying severity classification scheme, 2017 onwards | ... & actual trajectory (“KEA”) |  | Average determined unit cost for e/r ANS
3 | 2020-2024 (pre-Covid-19 plans shown; see notes) | Continued application of EoSM “levels”; a “counterbalance” w.r.t. capacity and cost efficiency | ... KEA falling to 2.40%, for 2022-24 (KEP now downgraded to indicator, from KPI, so no targets. It was a KPI only in 2019.) | Relaxed to 0.9 min/flight in 2020, falling to 0.5 by 2023 |  1.9% 2.7% p/a
(& national KPIs for ANS terminal cost efficiency)
New method with
better baseline
Split into reference periods
Notes: The SES Performance Scheme is slpit into ‘reference periods’. This allows each period to adapt to and build on the previous one.
Having relatively shorter blocks avoids setting distant targets (e.g. for 2035) that may need to change as a function of the traffic.
National performance plans refer to each reference period.
Unlike the SESAR Ambitions, the SES Performance Scheme KPIs are legally binding on the States. They face (small) penalties if they are not met.
Note two things. Cost efficiency is progressively improving. In 2018, EU-wide actual unit costs were below the ‘determined’ unit costs (targets).
We measure capacity through average en-route ATFM, although it is not really the best measure of capacity (cf. ‘pertinence’ quality, flagged earlier).
Since actual delay performance was not very good (as we’ll see later), the target for 2020 was relaxed pre-Covid-19. However, the SES PS risk-sharing mechanisms cannot effectively deal with the collapse of air travel during Covid-19, and the cessation of the assumed underlying flow of revenue into the system (ultimately from passengers). It is difficult for ANSPs to scale operations to actual demand (their greatest costs are staff costs). In November 2020, the Commission and States adopted an exceptional measures Regulation, whereby airlines will have to cover the revenue gap of 2020-21, delayed to 2023 and spread over 7-5 years. RP3 is currently out to consultation. Member States should revise their PPs and submit them by October 2021.
The PRB recommends that safety targets should remain the same, whilst environmental targets should be more ambitious during reduced traffic. ANSPs need flexibility in terms of capacity to restructure their business: revised capacity targets reflect lower traffic for 2021 and, with gradually increasing traffic, the system-wide cost optimum of 0.5 mins delay/flight applies for 2023 and 2024. The targets will allow ANSPs to implement technological changes, responding to changes in demand. The PRB new proposed (and current) targets (en-route ATFM mins/flight) are: 2020, 0.9 (0.9); 2021, 0.35 (0.9); 2022, 0.5 (0.7); 2023-4, 0.5 (0.5).
Regarding cost efficiency, ANSPs reported 2020 costs only 1% less than 2019 actual costs. However, only a limited number of ANSPs reported needing additional finance from third parties (e.g. the States, or banks) for 2020 and 2021: most were able to finance all or part of the revenue gap by their own means. Airlines will have to contribute to covering this gap starting in 2023. The PRB proposes targets also requiring cost containment measures for ANSPs, such that airlines do not have to cover the whole shortfall.
For further RP3 details, see: Advice on the revision of performance targets for RP3 (Performance Review Body, March 2021).

## Slide 21: Major frameworks impacting Europe SESAR Performance Framework (1/2)
Methodology is a combination of:
    Top-down to apportion from Performance Ambitions and baselines
    Bottom-up to identify Solutions per KPI; applying weights
Validation targets set per Solution (and per SubOE†, i.e. not per Deployment Scenario*)
  gap analysis thus performed at Solution level
Targets are directly related to Performance Ambitions
    no Performance Ambition (in a KPA) => no validation target (still consolidation of results for this KPA when available, but no gap analysis, since there is no Performance Ambition to compare with)
KPIs: with associated validation targets: directly related to Performance Ambitions
PIs: complementary indicators to illustrate the benefits of one or more Solutions
  might map to a KPI; mandatory or non-mandatory; no associated targets
Metrics: indicators not in SPF but allowed to further complement benefits
† sub-operating environment, e.g. ‘large airports‘ * package of Solutions and their planned deployment
see next slide
From Master Plan
Notes: Now we turn to the SESAR Performance Framework, the second of the two European mechanisms that this presentation describes.
The main thing to note here is that the so-called ‘validation targets’ in the SESAR Performance Framework are allocated top-down and bottom-up.
They refer back to the Performance Ambitions of the ATM Master Plan and are allocated across the SESAR Solutions.
This process is essentially a mixture of allocation and negotiation, based on what the R&D for each Solution suggests that it can deliver.

## Slide 22: Major frameworks impacting Europe SESAR Performance Framework (2/2)
Slide courtesy of: Jose Manuel Cordero, PJ19.04 Lead, ENAIRE
SESAR 3?
Notes: This is what the allocation looks like across the SESAR Solutions.
You do not need to know any of these numbers.

## Slide 23: Major frameworks impacting Europe SESAR Perf. Framework cf. SES Perf. Scheme (1/2)
Actual, ‘real world’ measurements | Validation models (SESAR Solutions); supports R&D
Aligned with 2005 high-level goals | E.g. maps contributions to 2005 high-level goals
Baseline: 2005 (Established: 2010) | Baseline: 2012 (previous MP edition); Established: 2006 (‘D2’)
‘Target’ year: was 2020, now 2035 (no doubling of traffic by 2020, but still ambitious targets) | ‘Target’ year: 2035
Reference periods: blocks / iterations | Deployment scenarios and roadmaps
Focus of delivery through regulation | Focus of delivery through technology (SESAR Solutions)
Some indicators binding, some for monitoring allocated through negotiated national performance plans | Performance Ambitions (aspirational) (+ other (K)PIs) MP Ambitions allocated across Solutions top down & bottom up
Safety, environment, capacity, cost-efficiency* | Nine of the ICAO KPAs are currently included†
More focus on ANSPs but with dependencies on other stakeholders, e.g. airlines, who are consulted re. performance plans | All stakeholders
ANSP regulations have ‘risk sharing’ mechanism to balance (e.g. low) ‘traffic’ v. (high) ‘cost’ risks | Traffic adjusted for forecasts & changing capacity needs
* “Cost efficiency” is SES terminology; ICAO refers to “cost effectiveness”.
† Through various KPIs and PIs, except for ‘global interoperability’ & ‘participation’, which are crucial but not similarly included. Resilience KPIs are included under ‘capacity’; punctuality under ‘predictability’.
SES Performance Scheme
SESAR Performance Framework
Notes: This is one of the most important slides in the presentation.
It summarises the key facts relating to the SES Performance Scheme and the SESAR Performance Framework, comparing and contrasting their key properties.

## Slide 24: Major frameworks impacting Europe SESAR Perf. Framework cf. SES Perf. Scheme (2/2)
SESAR Performance Framework cf. SES Performance Scheme have different:
  provenances
  implementations
  ... focuses (which is perfectly reasonable)
They need to continue to work together
  Performance Scheme taking account of SESAR deployment, and vice versa
  SESAR deployment contributions are subject to on-going research & validation for SESAR Solutions

## Slide 25: Current performance

## Slide 26: Current performance European punctuality performance up to 2019
Highest-ever traffic levels in 2019 (2016 ≈ back to 2008)
Six years of growth (from 2014 incl.)
Lower growth in 2019 (0.9% cf. 2018)
2018: fifth consecutive annual fall
2019: improved
2020: improved (but exceptional)
Average daily traffic
Source: Network operations report 2019 (EUROCONTROL, 2020)
Source: PRR 2019 (PRC, 2020)
Notes: It took until 2016 to recover to the pre-downturn traffic levels of 2008;
growth in 2019 slowed down cf. 2018.
2020 was exceptional, due to Covid-19, as we will see later.
We’ll see in the next slide why punctuality (arrivals within 15 minutes of schedule) improved somewhat in 2019.

## Slide 27: Current performance European punctuality performance up to 2019 (cont’d)
Average en-route ATFM delay, some recovery in 2019: 1.57 mins/flight cf. RP2 target: 0.50 (2015-19)
  total ATFM delay split about 70% en-route, 30% airport
  en-route: capacity is main cause; followed by staffing and weather
Reactionary (‘knock-on’) delay 44% (45-46% previous five years) – fairly stable ratio
Some delay improvements in 2019 due to re-routing measures (e.g. with longer routes)
SESAR ambition for 2035: average dep. delay: 6.5-8.5 mins/flight (cf. top of bars)
Average departure delay (mins/flight)
Source: Network operations report 2019
(EUROCONTROL, 2020)
0.73 0.86 0.88 1.73 1.57
14.4 (PRR 2019)
12.8 (PRR 2019)
Notes: The main message here is that actual European performance was well below both the SES Performance Scheme delay target (2015-2019) and the SESAR Performance Ambition (for 2035).
Note also that a huge part of the delay in the system is reactionary delay, which is quite stable (at over 40%), albeit with some reduction in 2019.
We’ve already learned that ATFM delay in Europe is a flow management, tactical ‘slot’ delay resulting from capacity restrictions at the destination airport, or in the en-route airspace.
“En-route ATFM delay improved in 2019 to 1.57 min/flt ... this was due to fewer disruptions and less weather impact while [EUROCONTROL] measures* helped reducing demand of the constrained ACCs ... leading to some 24 million minutes of avoided delays. The set of measures reduced traffic in ACCs such as Maastricht and Karlsruhe, mitigating capacity constraints in much of the core area.
The average flight-planned distance increased when compared to 2018, resulting in additional 5.8 million nautical miles flown over the whole year. This means an average daily increase of more than 15 000 nautical miles. ... negative impacts were ... recorded for the last filed flight plan and the actual trajectory as a result of the capacity problems in the network, industrial actions and crisis situations that led to reduced capacities and re-routings to avoid capacity constrained and avoided/closed areas due to crisis situation.”
Source: Network operations report 2019 (EUROCONTROL, 2020)
* See also the lecture ‘An introduction to flight planning and ATM messaging’:
Enhanced network measures developed for summer 2019 (‘eNM/S2019’)
Aim was to reduce en-route delay from over 4 min to below 2.5 min per flight
To be achieved via the RAD, moving 1100+ flights/day out of capacity constrained ACCs through the use of level caps and lateral re-routeings

## Slide 28: Current performance SES Performance Scheme – RP2 dashboard
Note 1. Various FAB performance plans have different planned contributions to the EU target.
Note 2. PRB calculated that the economic optimum for delay was appx 0.35 min/flight (2010).
*
* Functional Airspace Block Europe Central: Belgium, France, Germany, Luxembourg, the Netherlands and Switzerland.
Notes: For interest, you can see (and download) on-going performance data for the SES Performance Scheme in the on-line dashboard (see link).
The economic optimum for delay, calculated at appx 0.35 min/flight, uses University of Westminster calculations.
More on this will be presented in the ‘Delays in European aviation: trends and costs’ lecture.

## Slide 29: Current performance SES Performance Scheme – RP3 dashboard (accessed March 2020)
Note. 2020-21 is an exceptional period, due to Covid-19: low traffic and low delays.

## Slide 30: Challenges ahead
NB. Some overlaps between these

## Slide 31: Challenges ahead SESAR Perf. Framework and SES Perf. Scheme
Different focuses – more work on alignment, e.g. quantifying how Master Plan (deployment) contributes to SES Performance Scheme
External volatility – traffic variations (2016 ≈ recovery to 2008; Covid-19 re-think)
Trade-offs: lower user costs, more capacity, less CO2 ... and lower delay (getting worse)
Indicators too heavily focused at network level and on ANSPs
  many States argue that ‘one size fits all’ does not work for SES PS
  why not include airlines and airports in the SES PS?
Suitability of purpose, e.g. although average ATFM delay is established as a leading indicator, TMA arrival sequencing & taxi-out times show far greater time contributions
More guidance is needed on the interpretation of small changes (e.g. 30 x 1 min delays avoided => actual benefit = ?), statistical sampling errors, and significance testing
  coupled with a greater focus in SESAR Solutions on larger delay changes (e.g. 1 x 30 mins => more meaningful delay improvement)
Notes: These challenges focus on some examples relating to the SES Performance Scheme and the SESAR Performance Framework.
Further work is required to integrate them, and this will be achieved further and further through subsequent editions of the ATM Master Plan.
Adapting these plans in the immediate, medium and longer terms with regard to fluctuating traffic is challenging.
Challenges re. providing lower user (airline) costs, at the same time as increasing capacity and reducing the environmental impact of aviation and ATM are apparent.
There is arguably room for better adaptation to individual States in the SES Performance Scheme, and to include airlines and airports (not just ANSPs).

## Slide 32: Challenges ahead Door-to-door (D2D) context
Flightpath 2050 (ACARE, 2011)
  “highly ambitious goals” (x5)
  “90% of travellers within Europe are able to complete their journey, door-to-door within 4 hours”
Trade-offs: flight-centric cf. pax-centric metrics (and sub-types)
  pax delay, driving airline costs (& behaviour)
  x1.6 – x1.7 (US); x1.3 – x1.9 (Europe)
  can’t always detect changes with flight-centric metrics
How measure progress without the right metrics? (Currently gate-to-gate focus)
Impacts of intermodal factors (e.g. integrated ticketing) on, e.g.:
  Essential operational changes, such as flight prioritisation (e.g. UDPP)
  ATM technology changes, such as collaboration at airports (e.g. A-CDM)
Is faster better? What should we measure? – ‘slow’ & ‘green’ travel paradigms
More work launched in 2020 as part of the SESAR ER4 projects Modus (and BEACON)
Notes: Flightpath 2050 establishes a number of ambitious goals for European aviation,
including that 90% of travellers within Europe be able to complete their journey,
door-to-door within 4 hours, when such journeys include air as one of the modes.
The average delay of a delayed passenger is 1.3 – 1.9 times higher than the average delay of a delayed flight.
We generally focus rather heavily on flight-centric metrics in ATM, rather than passenger-centric metrics, although passenger delay drives a large part of airlines’ delay costs.
This will be demonstrated in the ‘Delays in European aviation: trends and costs’ lecture.
We need to use the right metrics to measure the right effects.
This will be demonstrated in the lecture: ‘Domino: a novel platform to assess the coupling of ATM systems from a flight and passenger perspective’.

## Slide 33: Challenges ahead Scope and trade-offs
Scope
Trade-offs: network scale cf. community scale cf. local/routes (macro, meso, micro)
Stakeholder inclusion (e.g. SES PS focus on ANSPs)
Restricted metrics (some examples only):
  resilience (capacity KPA, various PIs): absorptive, adaptive, restorative
  no KPIs yet for flexibility KPA (UDPP examples) or access and equity KPA
  with respect to cost of: delay, resilience, flexibility/uncertainty
Lack of forward-scoping indicators (in addition to pax and door-to-door requirements):
  automation; cybersecurity; utility (speed paradigm, previous slide); NOx
(Other) trade-offs
Quantitative relationships between KPIs still generally poorly understood
  may well worsen as we extend their scope (e.g. above)
  safety as a “counterbalance” w.r.t. capacity & cost efficiency
Need s/holder tools to explore KPIs (e.g. ANSP national performance plans)
  and for SESAR Solutions to extrapolate local models to network level
(buffer, re-sector, rebook)
Domino
Notes: We currently focus on network-level metrics, more than local-level investigations.
More advanced state-of-the-art examples will be presented in the lecture: ‘Domino: a novel platform to assess the coupling of ATM systems from a flight and passenger perspective’.
We are also still missing several groups of metrics, e.g. for resilience, flexibility and equity, and especially how these relate to (delay) costs.

## Slide 34: Performance measurement in ATM Key sources (in addition to 2020 Master Plan)
Performance Review Reports (PRRs) (EUROCONTROL)
  annual, June (draft in April)
www.eurocontrol.int/library
SESAR Solutions Catalogue (SESAR)
  Third edition, 2019 (ad hoc)
  www.sesarju.eu
Strategic Research and Innovation Agenda (SESAR)
  ‘Final’ edition, 2020 (first such)
www.sesarju.eu

## Slide 35: Additional information and resources
Notes: These additional resources are for wider and deeper context, and further reference only

## Slide 36: Selected timeline

## Slide 37: Selected timeline Potted history (1/3)
1998
2004
Single European Sky (SES) launched by EC in response to increasing delays
SESAR (SES ATM research project) launched – ‘technological pillar’ of SES
2005
Four SES high-level goals set by Commission for 2020 (originally)
Performance Review Commission (PRC) established by EUROCONTROL
ICAO: global ATM operational concept (‘Doc 9854’)
2006
2007
SESAR Joint Undertaking established (PPP founded by EU & EUROCONTROL):
maintain Master Plan: e.g. review SESAR contribution to SES high-level goals
2008
Global economic crisis:
SESAR: Performance target (‘D2’), SESAR ‘definition phase’, therein:
SESAR Performance Framework established, range of targets set out
traffic downturn – previous forecasts, CBAs etc less valid / invalid

## Slide 38: Selected timeline Potted history (2/3)
2009
2010
SES Performance Scheme established (NB. after SESAR Performance Framework)
big change: ends automatic full cost recovery principle (since 1981)
2012
Master Plan (2nd ed.) quantifies SES goal contributions
Master Plan (1st ed.), sets out contributions to SES goals, evolving doc
reflects: 2008+, ICAO docs 9883, 9854, 9750 (global interoperability)
ICAO: manual on global performance (‘Doc 9883’)
2013
2014
PRC designated 1st Performance Review Body of SES PS (until end 2016)
Reference Period 1 (RP1) of SES Performance Scheme closes (2012-2014)
2015
Master Plan (3rd ed., “Edition 2015”)
ICAO: 2013–2028 global air navigation plan (‘Doc 9750’) (4th ed.)
in coordination with SESAR and NextGen (US)
SES Performance Scheme RP2 starts (2015-2019)

## Slide 39: Selected timeline Potted history (3/3)
2016
2017
2nd Performance Review Body of SES PS appointed (until end 2024)
2019
Master Plan (‘Edition 2020’)
Traffic back to 2008 levels
ICAO: 2016–2030 global air navigation plan (‘Doc 9750’) (5th ed.)
ICAO: global air navigation plan (‘Doc 9750’) (6th ed.)
2020
2035
SESAR Performance Ambition ‘target’ year
2050
Flightpath 2050 – Europe’s Vision for Aviation – 4-hour D2D target (Advisory Council for Aviation Research and Innovation in Europe – ACARE)
SES Performance Scheme RP3 starts (2020-2024)
Original SES high-level goals ‘target’ year was 2020
Covid-19 pandemic – multiple impacts

## Slide 40: Selected ICAO documents and alignment

## Slide 41: Major frameworks impacting Europe ICAO Global ATM Operational Concept (‘Doc 9854’)
ICAO (2005). Global Air Traffic Management Operational Concept (Doc 9854), Ed. 1, International Civil Aviation Organization, Montréal.
(Not updated with second edition.)
https://store.icao.int/publications.html
(appx. USD 90)
A key objective
Presents ICAO vision of an integrated, harmonised and globally interoperable ATM system – agreed levels of safety, optimum economic ops, environmentally sustainable (horizon: up to and beyond 2025)

## Slide 42: Major frameworks impacting Europe ICAO Manual on global performance (‘Doc 9883’)
ICAO (2009). Manual on global performance of the air navigation system (Doc 9883), Ed. 1, International Civil Aviation Organization, Montréal.
(Not updated with second edition.)
https://store.icao.int/publications.html
(appx. USD 180)
A key objective
To support harmonised terminologies in ‘performance-based’ assessment = focus on desired results, with decision-making driven by results and data

## Slide 43: Mapping SESAR changes to ICAO framework Source: ATM Master Plan, Edition 2020

## Slide 44: Mapping SESAR changes to ICAO framework (Cont’d)
Mapping between the SESAR deployment scenarios and the ICAO Aviation System Block Upgrades (ASBU) Elements. The ICAO framework of 2019 shows a finer granularity than its predecessor.

## Slide 45: Comparing Europe, US and China

## Slide 46: Current performance, wider context Comparing Europe, US and China
Data level by region | Europe | US | China
Focus on arrival or departure delay | departure | arrival | departure
Delay threshold | ≥ 5 mins | ≥ 15 mins | > │5 mins│*
Main delay causes reported | airline weather ATFM, weather ATFM, airports ATFM, en‐route reactionary | airline weather ATFM reactionary security | airline weather ATFM military
* Classified as on-time if any departure delay is zero, or less, on arrival.
Being replaced with a 15-min arrival delay threshold.

## Slide 47: Current performance, wider context Comparing Europe, US and China
(2014)

## Slide 48: Current performance, wider context Comparing Europe, US and China
http://authors.elsevier.com/sd/article/S1000936117300237
Cook A, Belkoura S and Zanin M, 2017. ATM performance measurement in Europe, the US and China.
Chinese Journal of Aeronautics, 30 (2), 479-490. ISSN 1000-9361

## Slide 49: Current performance, wider context Comparing Europe, US and China
* SES Performance Scheme targets shown.
Delay reduction within capacity KPA, target relative to 2012. En-route target for RP2.
*

## Slide 50: Current performance, wider context Comparing Europe, US and China
Cook A, Belkoura S and Zanin M, 2017. ATM performance measurement in Europe, the US and China.
Chinese Journal of Aeronautics, 30 (2), 479-490. ISSN 1000-9361
 | Europe | US | China
ATFM service provision | 41 States (EUROCONTROL) 63 en-route centres | Federal Aviation Administration 20 air route traffic ctrl centres | Air Traffic Management Bureau (CAAC) 8 upper air ctrl areas
Default management | at-gate | airborne | mix
MIT | very limited | yes (->TBM) | yes
Special use airspace | core | coast | core
ATFM / AO/ airport CDM | yes | yes | yes
http://authors.elsevier.com/sd/article/S1000936117300237

## Slide 51: Further material on the SES Performance Scheme

## Slide 52: SES Performance Scheme Charging Scheme: principles
Full cost recovery replaced by ‘determined costs’ – paradigm shift
Incentives in regs for ANSPs to balance ‘traffic’ v. ‘cost’ risks (‘risk sharing’ mechanism)
  actual traffic high: some revenues over ‘dead band’ go to AUs
  actual costs high: ANSP bears costs (incentive to off-set by reducing costs)
  alert thresholds established at both EU and local level to enable a revision of targets when underlying assumptions (e.g. traffic) change significantly (but cf. Covid-19!)
Overall: stronger incentives on reducing costs, weaker incentives on improving capacity
  assumptions in some performance plans made to game system
  financial incentives currently mandatory for capacity KPA (all KPIs); optional for environment KPA – should they be mandatory for all KPAs?
    only the UK had an ENV incentive in its pre-Covid-19 RP3 performance plan
    better to incentivise capability (technological functionality)?
2018: cost of ATFM delay to AUs €2009 1.7bn, cf. ANSP delay penalties €2009 4m (Source: PRB)
Is overall 50% unit cost reduction realistic without associated forecast traffic growth?
  in 2018, EU-wide actual unit costs were below determined unit costs (target)
    partly driven by under-investment in capacity
  some support for price cap, instead of tying cost efficiency KPI to traffic

## Slide 53: SES Performance Scheme Charging Scheme: en-route surpluses in 2018
Top two bars (above, left): ATSPs are net winners in both situations – actual costs overall lower cf. PPs (but mixed pictures across ATSPs); traffic higher than planned (grows across RP2, esp. for larger ATSPs). Bonuses/penalties set relative to agreed performance targets in performance plans: but note the small effects.
NB. ATSP = Air traffic service provider, main provider in the State concerned (typically same as ANSPs).

## Slide 54: Major frameworks impacting Europe SES Performance Scheme: data
Decreasing ENV performance (longer routes flown) as a result of capacity problems in the network, industrial actions and crisis situations. (Note that from JAN20 (RP3), route charging is based on actual (not planned) routes.)

## Slide 55: SES Performance Scheme Charging Scheme: en-route return on equity (RoE)
RoE is a profitability measure, relative to the equity, i.e. net assets (assets minus liabilities). ‘Good’ rates depend on the industry, but >15% generally considered so. The estimated surplus at the EU level represents 9.5% of 2018 en-route revenues: higher than the 4.9% planned in the PPs. This corresponds to a (weighted average) ex-post actual RoE of 13.0% (cf. 7.2% planned in the PPs). Cf. NATS en-route: 14.3% in 2018. The estimated surplus includes some costs exempt from cost-sharing for main ATSPs in 2018. The EC-allowed amounts to be reimbursed to airspace users will be eligible for carry-over to the following RP(s).

## Slide 56: Major frameworks impacting Europe Performance Review Body (PRB) and RP3 update
2014: EUROCONTROL’s Performance Review Commission (with support from its Performance Review Unit), was designated as first PRB until end of 2016
2017: second PRB appointed in June (supported by: Ernst & Young; Helios, Integra)
Key roles (working closely with National Supervisory Authorities (e.g. CAA in UK)):
  advise Commission on revisions to SES PS and Charging Scheme
  advise Commission on ATM Master Plan in context of the two schemes
  consult on / assess the Performance Plans
  monitor performance in current Reference Period
    https://www.eurocontrol.int/prudata/dashboard/vis/
  consult on following RP, propose binding targets to Commission
Most States asked to revise their RP3 plans even pre-Covid-19, with PRB citing:
  “managing the major [safety] risks well”; but not meeting ENV targets
  lack of fundamental structural change & cross-border cooperation
  infrastructure investment without direct impact on performance
Further, additional challenges due to Covid-19 and very large fall in traffic
  States should revise their plans and submit them by October 2021

## Slide 57: Major frameworks impacting Europe The context for NATS
Commercialised in 2001 into a public-private partnership: NATS Holdings Ltd
  49% Secretary of State for Transport (gives Govt vetoes and special voting rights)
  42% The Airline Group Ltd
  5% NATS staff
  4% LHR Airports Ltd
ATC services over UK, eastern North Atlantic (Shanwick Oceanic), and 13 UK airports
  also provides other ATC and related services in UK and overseas
Regulatory / economic oversight by CAA
Price caps on en-route charges: RPI – [efficiency factor]
  one factor for European e/r and London Approach, one for Shanwick Oceanic
  they consider: traffic, performance (e.g. delays, ENV), costs
  possible adjustment in following periods for pension adjustments
Reporting on SES perf. dashboard both for UK-Ireland FAB, and UK alone
  FAB covers e/r airspace and large TMAs, but excludes Shanwick Oceanic

## Slide 58: Further material on the SESAR Performance Framework

## Slide 59: Major frameworks impacting Europe SESAR Performance Framework
D4.1 – 2017 release
  https://ec.europa.eu/research/
D4.7 – 2019 release
  currently in force
  not currently publicly available
  reference for first part of Wave 2 (mid Wave 2, further release planned)
Note
PJ.19: content integration; 27 partners; lead: EUROCONTROL
PJ.19-04: performance management; lead: ENAIRE

## Slide 60: Major frameworks impacting Europe SESAR Performance Framework
Slide courtesy of: Jose Manuel Cordero, PJ19.04 Lead, ENAIRE
Progressive Performance Assessment refinement
Validation Results
Estimations
SOL
SOL
SOL
SOL
SOL
SOL
SOL
SOL
SOL
SOL
SOL
Performance Assessment
Release (PAGAR) #1
Performance Assessment
Release (PAGAR) #2
Performance Assessment
Release (PAGAR) #n
VALIDATION TARGETS
Gap Analysis
Gap Analysis
Gap Analysis
Three, yearly assessment cycles for SESAR 2020 IR Wave 1: 2017, 2018 and 2019; similar in IR Wave 2
PERFORMANCE FRAMEWORK

## Slide 61
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com