## Slide 1: Introduction to ATM Essential data sources in aviation and ATM
Graham Tanner
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Introduction

## Slide 3: Introduction
Overview of a range of useful aviation/ATM data sources
  Traffic (flights)
  Passenger (‘pax’)
  Other useful data (e.g. enablers, calibration)
Note
  European focus
  Comprehensive, but non-exhaustive list
  Official sources (unofficial/open data sources also exist)
  From perspective of a university researcher with limited budget!
Notes: Lecture will provide an overview of suitable data sources: focus is on flights and passengers, with other useful ‘enabler’ data sources
Note European perspective and other data sources are available, including a growing supply of open source data; commercial datasets are usually expensive
(MET/weather data and financials not covered)

## Slide 4: General observations
Data requirements
  Define and specify the data required
  Consider time periods (affected by disruption/incidents?)
  Consider coverage (e.g. top 200 airports ≥ 95% pax; ≥ 90% movements)
Different sources
  Often multiple data sources are required
  Differences between the ‘same’ data (collection/cleaning/assumptions)
Restrictions
  NDA, export control, cost (increases with the level of disaggregation)
  Depends on usage (academic research, commercial, publication)
Notes: Some general observations (particularly relevant when planning dissertations)
Before rushing out to request or even purchase data, work out your data requirements (a more limited, easier-to-acquire dataset may be suitable)
Check the time period as it may turn out to have been affected by disruption – weather/strikes (e.g. affecting a particular airline, a particular airport, a particular country or the network); impact of COVID-19 on aviation; if time period is too recent the data may not be available yet (i.e. time lag)
A carefully selected data extract may be sufficient, rather than complete coverage
Multiple sources may be required
Flights and passengers are from different sources
There may be differences between the ‘same’ data sourced from different suppliers (e.g. due to different collection methods or assumptions made); if a choice, consider favouring one source to ensure consistency
Usage restrictions
- Will apply for data from commercial suppliers or data acquired under a licence agreement

## Slide 5: General observations
Using the data
  Understand the data before using; sufficiently defined? (e.g. ‘arrival time’? – could mean touchdown, scheduled/actual at-gate) – request and test samples to check, calibrate with other data
  Data cleaning and preparation for usage
  Estimate, derive, impute missing data
  Consider having a data management WP for projects?
Watch out for…
Notes: Usage
Make sure you understand what the data fields contain; if available, refer to the data description or data dictionary, e.g. arrival time may not be at airport gate
Data preparation may be required before a dataset is usable; usually cleaning/recoding to fit research requirements
Data gaps need to be filled somehow

## Slide 6: General observations
…two passenger data examples
LCC!
Jetstar Asia Airways ticket summary for three routes (NOV11)
Heathrow?
CAA Table 12.2 Domestic Air Passenger Traffic To and From Reporting Airports for 2014
Notes: Usage – check your data before using, e.g.
Jetstar Asia is a LCC so there shouldn’t be any first class fares
To avoid double-counting passenger numbers, the UK’s CAA reports domestic passenger traffic under the London airports, so if you are interested in passengers travelling to/from Aberdeen you might overlook the Heathrow route (since all Aberdeen-Heathrow/Heathrow-Aberdeen pax are reported under Heathrow)

## Slide 7: General observations
…traffic data example – how many flights in one day? Easy answer surely!
Reported flights on Friday 23AUG13 (EUROCONTROL sources)
  Statistics & Forecast Service (STATFOR): 31 656
  Network Manager (NM): 31 759
  Demand Data Repository (DDR): 32 790
  Why different?
Difference due to
  Varying purposes (e.g. DDR airspace load accuracy leads to flights counted twice in consecutive days)
  Varying geographic coverage
Notes: Usage – example reveals that the number of flights on 23AUG13 varies because these datasets are intended for different purposes, or different areas are covered

## Slide 8: Geographic scope
Number of flights in Europe – depends on what’s meant by ‘Europe’
  Membership of: EU (27) EU + EFTA (31) EUROCONTROL (41) ECAC (44)
Reporting areas
  SES Performance Scheme (RP2Region) 30 states/zones
  EUROCONTROL STATFOR Forecasts (ESRA08) 34 traffic zones
  EUROCONTROL en-route charging (CRCO16) 39 zones
  Network Manager Area (NM Area) 42 states
incl. UK!
Notes: Usage – be aware of what’s being reported (e.g. European Union compared with ECAC (European Civil Aviation Conference)
Graphic pre-dates UK exit from the EU (i.e. EU-28)
(EFTA = European Free Trade Association; Iceland, Liechtenstein, Norway, Switzerland)

## Slide 9: Some of the key data sources

## Slide 10: Key data sources (global, regional, national)
Other sources are available too…
Notes: Examples of some of the key data sources

## Slide 11: Traffic data

## Slide 12: Traffic data – introduction
What do we mean?
  Flights, flown rather than scheduled
  Instrument flight rules (IFR), commercial
Data granularity
  Aggregated overview, coarse
  Individual flights with tail number
Month (SEP10) / ECAC
  894 140 flights
Day (10SEP10) / ECAC
  32 231 flights
Day (10SEP10) / LHR
  684 departures
Day (10SEP10) / LHR-FRA
  17 departures (BA+LH)
Day (10SEP10) / LHR-FRA
  BA904 1040 (scheduled dep.) 1046 (actual dep.) A319 (G-EUPM) 131 seats …
Examples follow
Notes: Traffic data
Flights flown rather than the schedule
Interested in commercial passenger flights (IFR), i.e. fare-paying pax onboard
Level of detail required? Aggregate data or detailed data per flight

## Slide 13: Traffic data
Summary data
  ICAO Data+ summaries based on air transport statistic data collected by ICAO Member States from airlines & airports
Subscription
required
ICAO Data+: ‘Air Carrier Traffic’
Notes: Traffic data
Example of ICAO Data+ summaries
Example of a nice clean dataset – full data each year and each month; can usually find similar data in airline annual reporting (though maybe not aircraft hours)

## Slide 14: Traffic data
Summary data
  ACI EUROPE summaries based on statistic data collected from airport members, e.g. Airport Traffic Report (monthly/annual movements [arr. + dep. = 2] as well as pax/freight)
Published
ACI EUROPE: Airport Traffic Report
Notes: Traffic data
Example of ACI EUROPE airport summary data

## Slide 15: Traffic data
Route data
  Eurostat offer a selection of datasets collected by EU Member States – high level summaries down to the number of flights per route, e.g. main airports within the EU
Published
Eurostat: ‘avia_par_de’ table
Notes: Traffic data
Example of Eurostat summary (free access; very useful), e.g. per O/D

## Slide 16: Traffic data
Route data
  Eurostat offer a selection of datasets collected by EU Member States – high level summaries down to the number of flights per route, e.g. main airports outside the EU
Published
Dataset downloaded in SEP19 - 4 month time lag
Eurostat:
‘avia_paexac’ table
Notes: Traffic data
Example of Eurostat summary revealing time lag before data available (4 months is pretty good); data will be updated as states report their figures

## Slide 17: Traffic data
Route data
  EUROCONTROL units produce a vast amount of traffic data, though access varies; agreements sometimes required
  CODA (Central Office for Delay Analysis) database – supports flight delay analysis, but useful for other purposes
Registration
required
TTF: Total Operated Flights
Notes: Traffic data
Example of EUROCONTROL CODA delay data, e.g. total operated flights can be extracted per O/D

## Slide 18: Traffic data
Flow data
  EUROCONTROL units produce a vast amount of traffic data, though access varies; agreements sometimes required
  STATFOR Interactive Dashboard (SID) – ECAC statistics and forecasts*
Registration
required
* historical data also available
STATFOR:
‘Traffic Per Flow’ avg. daily flights (AUG19)
Notes: Traffic data
Example of EUROCONTROL STATFOR flow data (forecasts and historical)

## Slide 19: Traffic data
Per flight data
  EUROCONTROL PRISME data service provides data for various purposes:
    Operational/protected users via ‘Demand Data Repository’ (DDR)
    Researchers/academia via ‘R&D data archive’
Data | DDR | R&D data archive
access | restricted | registration required
since | JUL11 | MAR15
temporal | daily | MAR, JUN, SEP, DEC each year
released | next day | two years later
coverage | 4D trajectories with details of route, timing points, airspace structure, aircraft | limited information of route, timing points, airspace structure, aircraft
www.eurocontrol.int/dashboard/rnd-data-archive
Notes: Traffic data
EUROCONTROL PRISME data covers all filed and flown flights, an enormous amount of data though limits on what can be made available; research access to the DDR service was withdrawn in 2019 – new R&D data archive launched as a replacement, but reduced number of data fields and temporal coverage
DDR data contains historic and forecast data
DDR and R&D data archive consist of a range of files for different purposes

## Slide 20: Traffic data
Per flight data
  EUROCONTROL data cont.
  Depending on access and the file, three types of data available per flight
  Flight model:
    Model 1 (‘M1’) / Filed Tactical Flight Model (FTFM) filed flight profile from the last filed flight plan from the airline
    Model 2 (‘M2’) / Regulated Tactical Flight Model (RTFM) calculated flight profile (M1 with ATFM measures applied)
    Model 3 (‘M3’) / Current Tactical Flight Model (CTFM) actual 4D trajectory flown (updated with radar data); closest estimate available of “actual” flown
Also…
Model 0 (‘M0’) / original filed flight plan
Notes: Traffic data
EUROCONTROL data: M1 = last filed data; M2 = M1 with regulations applied; M3 = flown data
We also refer to M0 to describe first flied data (AO original flight intention)

## Slide 21: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14
    Traffic demand between airport pairs with flight information (no trajectories) – selected fields shown (≈100 fields)
EOBT
AOBT
Licence
required
ETOT
DDR: ‘exp2’ file
Notes: Traffic data
Example of EUROCONTROL summary data (from DDR ‘exp2’ file) – intended to describe traffic demand, but gives a useful summary per flight, with equipment, key times, operator, service type, etc.

## Slide 22: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14
    Flight in more detail
  IB 3163 schedule
    LHR dep 0910 [UTC+1]
    MAD arr 1240 [UTC+2]
Notes: Traffic data
Example of EUROCONTROL summary data – drill down into this flight (IB 3163), with further details from other sources
Note times in UTC, i.e. EOBT 0810 is 0910 in schedule

## Slide 23: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14 (IB 3163)
    Planned 4D flight trajectory using last filed flight plan (M1) – selected fields
Licence
required
772.66 NM
0 = Climb,
2 = Cruise,
1 = Descent
ETOT
COMPTON
DDR: M1 ‘so6’ file
Notes: Traffic data
Example of EUROCONTROL summary data (from DDR ‘so6’ file) – still focusing on IB 3163
Planned trajectory (M1) data per point – entry/exit times, flight level, coordinates, distance
Note planned route from Heathrow is via COMPTON SID

## Slide 24: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14 (IB 3163)
    Actual 4D flight trajectory, updated with radar data (M3) – selected fields
Licence
required
ATOT
741.45 NM
0 = Climb,
2 = Cruise,
1 = Descent
OCKHAM
DDR: M3 ‘so6’ file
Notes: Traffic data
Example of EUROCONTROL summary data (from DDR ‘so6’ file) – still focusing on IB 3163
Actual trajectory (M3) data per point – entry/exit times, flight level, coordinates, distance
Note flown route from Heathrow is via OCKHAM on GASGU SID

## Slide 25: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14 (IB 3163)
    view of M1/M3 trajectories in NEST tool
    no change of route; dep/arr time changes
    but was M1 the airline’s original intention?
Licence
required
M1
M3
M1
M3
Distance: 772.66 NM
T/O - T/D: 01:56:50
Distance: 741.45 NM
T/O - T/D: 01:59:39
Notes: Traffic data
Example of EUROCONTROL summary data – still focusing on IB 3163
Differences between planned/actual trajectories shown using EUROCONTROL’s NEST analysis tool

## Slide 26: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14 (IB 3163)
    Key flight event times
Event | M1 (estimated) | M3 (actual)
Off-block time | 0810 | 0800
Take-off time | 0830 | 0825
Touch-down time | 1026 | 1024
On-block time | ? | ?
Notes: Traffic data
Example of EUROCONTROL summary data – still focusing on IB 3163
The key flight event times: departure, take-off, touch-down are known, but arrival at the gate is unknown

## Slide 27: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14 (IB 3163)
    Key flight event times
Event | M1 (estimated) | M3 (actual) | OOOI events
Off-block time | 0810 | 0800 | ‘Out of gate’
Take-off time | 0830 | 0825 | ‘Off the ground’
Touch-down time | 1026 | 1024 | ‘On the ground’
On-block time | ? | ? | ‘In the gate’
Notes: Traffic data
Example of EUROCONTROL summary data – still focusing on IB 3163
The key flight event times: departure, take-off, touch-down are known, but arrival at the gate is unknown
These are known as the ‘OOOI’ times – very useful, e.g. when calculating delay

## Slide 28: Traffic data
Per flight data
  EUROCONTROL data example LHR-MAD, 12SEP14 (IB 3163)
    Key flight event times
Event | M1 (estimated) | M3 (actual) | OOOI events
Off-block time | 0810 | 0800 | ‘Out of gate’
Taxi-out time | 20 mins | 25 mins | -
Take-off time | 0830 | 0825 | ‘Off the ground’
Touch-down time | 1026 | 1024 | ‘On the ground’
Taxi-in time | ? | ? | -
On-block time | ? | ? | ‘In the gate’
Notes: Traffic data
Example of EUROCONTROL summary data – still focusing on IB 3163
The key flight event times: departure, take-off, touch-down are known, but arrival at the gate is unknown
These are known as the ‘OOOI’ times – very useful, e.g. when calculating delay
Also reveal the taxi-times, if times are known

## Slide 29: Traffic data
National data
  National supervisory authorities (NSA)/civil aviation authorities
    UK CAA publishes monthly tables (airport movements, domestic/international routes)
    US FAA and BTS publish range of data/statistics, e.g. FAA’s Operational Network (OPSNET) – official source of NAS air traffic operations
  Airports/airport groups – many publish monthly summary tables, e.g.
    Aena airports (Spain)
    Aeroporti di Roma
    Aéroports de Paris
    Amsterdam Schiphol Airport
    Berlin airports
    Gatwick Airport
    Heathrow Airport
    Istanbul Ataturk Airport
    Luton Airport
    Luxembourg Airport
    Munich Airport
    … and so on
Notes: Traffic data
Examples of sources national data sources
NSAs/CAAs and airports publish various summaries
(BTS = Bureau of Transportation Statistics)
(NAS = National Airspace System)

## Slide 30: Traffic data
Recap of scope of traffic data by source
  Examples discussed only, by no means an exhaustive list
Source | Summary | Route | Flight
ICAO Data+ | yes | yes | no
ACI EUROPE | yes | no | no
Eurostat | yes | yes | no
EUROCONTROL | yes | yes | yes
Various national | yes | some | no
Notes: Traffic data – recap

## Slide 31: Passenger data

## Slide 32: Passenger data – introduction
What do we mean?
  Passengers on IFR/commercial flights
  Scheduled, charter
  Airlines – count pax carried
  Airports – terminal/transfer (count x2)
    – transit (same flight, count x1)
Data granularity
  Aggregated overview, coarse
  Per route
  Per direction, per airline, ticket details, etc.
Month (SEP10) / LHR
  6 221 219 pax
Month (SEP10) / LHR<>FRA
  125 258 scheduled pax
Month (SEP10) / LHR-FRA
  First: 816, Business: 10 583, Economy (full): 9830, Economy (discounted): 32 718 other: 6696
Examples follow
Notes: Passenger data
Interested in passengers on commercial flights (IFR), i.e. fare-paying pax onboard
Careful, as passengers are counted differently, e.g. airports count terminal/transfer passengers twice (once at origin airport and again at destination airport) whereas airline counts the same passengers once
Level of detail required? Aggregate data or detailed data per flight

## Slide 33: Passenger data
Summary data
  Simple totals are published by airlines/airports (though check comparing like-for-like)
    Monthly bulletins
    Annual financial reports
  However, focus here on availability of more detailed data …
Notes: Passenger data
Summary data published by airlines/airports; data found in financial reports can be very useful

## Slide 34: Passenger data
Summary data
  ICAO Data+ summaries by airlines, with various breakdowns e.g. domestic/ international, load factors
Month !!
Subscription
required
French airlines (2019 example)
ICAO Data+:
‘Air Carrier
Traffic’
Notes: Passenger data
Example of ICAO Data+ summary; note coverage can vary within dataset (see the number of months) – data covering full year for Transavia’s intl flights, but only half-year for dom flights

## Slide 35: Passenger data
Summary data
  ICAO Data+ summaries by airlines, with various breakdowns e.g. pax-km, load factors
Subscription
required
Lufthansa 2014-2019
ICAO Data+: ‘Air Carrier Finances’
2016 !!
2018 !!
Dataset downloaded in MAR21 - 2 year time lag
Notes: Passenger data
Example of ICAO Data+ summary per reporting airline

## Slide 36: Passenger data
Route data
  Eurostat offer a selection of datasets, pax by country, airport and per route
    ‘Pax on board’ – all passengers on board an aircraft during a flight stage
    ‘Pax carried’ – counted once only, not repeatedly on each individual stage of flight (excludes any double-counting)
Published
Eurostat: ‘avia_paoac’ table
Notes: Passenger data
Example of Eurostat summary (free access; very useful), e.g. per country
Passengers carried is a more useful statistic as prevents double-counting

## Slide 37: Passenger data
Route data
  Eurostat offer a bulk download; includes pax per route
Published
Eurostat: ‘avia_par’ table
Dataset downloaded in APR18 - 9 month time lag
Notes: Passenger data
Example of Eurostat summary (free access; very useful)
Bulk download facility available, so you can download a large amount of data in one go

## Slide 38: Passenger data
Itinerary data – introduction
  Passenger data through ticketing
  Traditional model of ticket sales
Book ticket
  MIDT
Issue ticket
Settle ticket
  BSP/ARC
Flight
Marketing Information Data Transfer (MIDT)
Bookings made in the major GDSs (e.g. Sabre, Amadeus)
Reservations – IATA/non-IATA agencies
Future travel data, available from a number of vendors…for a price
Billing and Settlement Plan (BSP) / Airline Reporting Corporation (ARC)
Ticket sales from the major GDSs & agencies (covering ≈400 airlines)
Actual travel data, available from IATA as their PaxIS product…for a price (alternative products exist)
  Online ticket sales made directly with airlines are not captured by MIDT or BSP/ARC
  Changes in progress, e.g. IATA ‘New Distribution Capability’ (not covered here)
Notes: Passenger data
Itinerary data captured through ticketing through global distribution systems (GDSs): itineraries from bookings (i.e. future data) or settled tickets (i.e. historic data)
Note that a growing proportion of ticket sales bypass GDSs due to direct sales with airlines

## Slide 39: Passenger data
Itinerary data
  IATA PaxIS (Passenger Intelligence Services) detailed passenger data based on ticket sales
    Monthly passenger itineraries since 2005 – global O/D coverage with a breakdown of seat class, fare paid, connecting airports
    Statistical estimates infill missing data – US market from ARC, non-BSP markets (LCC, charter and online airline ticket sales)
example routings to Adelaide
Purchase
required
Notes: Passenger data
Example of IATA PaxIS summary itinerary data – aggregated by month, but with a breakdown by connection and fare paid
Reported passengers and estimated passengers are provided – estimate to fill known gaps (to estimate 100% of the market)
Marketed airline displayed on ticket (dominate airline marketed airline operating longest leg)
E.g. first record shows BA ticketed passengers (7 estimated from 4 ticket sales) flying from Aberdeen to Adelaide, connecting at Heathrow and then Singapore, paying €592.30 per ticket (outbound fare)
PaxIS data is only commercially available

## Slide 40: Passenger data
Itinerary data
  US BTS agency DB1B (Airline Origin and Destination Survey) data based on a 10% sample of airline tickets
  Quarterly coverage since 1993 – US O/D coverage with a breakdown of seat class, fare paid
example itineraries to JFK
Published
Abilene
Albuquerque
Notes: Passenger data
Example of US Bureau of Transportation Statistics summary itinerary data available free, from a sample of tickets

## Slide 41: Passenger data
Survey data
  UK CAA Departing Passenger Survey detailed passenger data based on face-to-face interview at-gate (≈30 questions)
    O/D coverage with a breakdown of seat class, fare paid, demographics (UK focus)
    Responses scaled-up to represent dep. + arr. pax
    Bespoke questions possible…for a price
  Comparison of an anonymised ‘difficult’ airport pair:
Purchase
required
Notes: Passenger data
Example of UK CAA survey data which can provide detailed profiles of passengers
Table shows comparison of passenger numbers on a ‘difficult’ O/D pair (multiple operators, including charter flights) from different sources; note wide range of total passengers for the month (103k – 132k); PaxIS is missing charter passengers; CAA survey is overestimating scheduled passengers; whereas even the 2 airports’ totals don’t match (though suggest the actual total is approx. 115k)

## Slide 42: Other useful data

## Slide 43: Other useful data
A few examples of other useful data, and available sources
Aircraft fleet
  Commercially available from OAG and Cirium
  Online resources, e.g. airframes.org (registration required)
  EUROCONTROL PRISME Fleet (registration required)
    Extract (selected fields) for A20N (A320 NEO); Series: A320 251n
P-F ID | Serial No | Current Registration | Mode S | Mode S Type | Current Operator(s)
294106 | 7486 | 4R-ANA | 7705C1 | WIZ | Srilankan Airlines
294107 | 7489 | SE-DOX | 4A91F8 | WIZ | SAS - Scandinavian Airlines System
294110 | 7494 | PR-YRH | E49311 | WIZ | AZUL
294108 | 7499 | SE-DOY | 4A91F9 | WIZ | SAS - Scandinavian Airlines System
294117 | 7505 | PK-GTC | 8A064D | WIZ | Citilink Airways
294726 | 7508 | HS-BBZ | 88085A | WIZ | Thai AirAsia
294105 | 7514 | PR-YYI | E492D0 | WIZ | AZUL
Notes: Other useful data
Fleet data from commercial and free suppliers, plus EUROCONTROL
Example of EUROCONTROL PRISME Fleet data – details shown for a specific series of A320 NEO

## Slide 44: Other useful data
airframes.org fleet example – SriLankan Airlines
Registration | Manuf. | Model | Type | c/n | SELC | built | delivery | status
4R-ABL | Airbus | A320-232 | A320 | 2345 | JSBG | 2004 | 07/04/2011 | active
4R-ABM | Airbus | A320-214 | A320 | 4694 | FKCM | 2011 | 18/05/2011 | active
4R-ABN | Airbus | A320-214 | A320 | 4869 | FLAJ | 2011 | 25/10/2011 | active
4R-ABO | Airbus | A320-214 | A320 | 4915 | FLGM | 2011 | 29/11/2011 | active
4R-ABQ | Airbus | A321-231 | A321 | 3397 | ABHR | 2008 | 15/02/2014 | active
4R-ALA | Airbus | A330-243 | A332 | 303 | KQDF | 1999 | 26/10/1999 | active
4R-ALB | Airbus | A330-243 | A332 | 306 | KQDG | 1999 | 15/11/1999 | active
4R-ALC | Airbus | A330-243 | A332 | 311 | KQDH | 1999 | 10/12/1999 | active
4R-ALD | Airbus | A330-243 | A332 | 313 | KQDP | 1999 | 12/01/2000 | active
4R-ALH | Airbus | A330-243 | A332 | 627 | KQDE | 2004 | 08/12/2011 | active
4R-ALL | Airbus | A330-343 | A333 | 1564 | DRMQ | 2014 | 30/10/2014 | active
4R-ALM | Airbus | A330-343 | A333 | 1583 | HSFG | 2014 | 19/12/2014 | active
4R-ALN | Airbus | A330-343 | A333 | 1604 | CPHJ | 2015 | 26/03/2015 | active
4R-ALO | Airbus | A330-343 | A333 | 1650 | GKCH | 2015 | 15/08/2015 | active
4R-ALP | Airbus | A330-343 | A333 | 1669 | JSBM | 2015 | 10/11/2015 | active
4R-ALQ | Airbus | A330-343 | A333 | 1687 | ACBK | 2015 | 24/12/2015 | active
4R-ALR | Airbus | A330-343 | A333 | 1689 | FKAC | 2015 | 29/12/2015 | active
4R-ALS | Airbus | A330-243 | A332 | 1008 |  | 2009 | 2018-10 | active
4R-ANA | Airbus | A320-251N | A20N | 7486 | HSCQ | 2017 | 23/02/2017 | active
4R-ANB | Airbus | A320-251N | A20N | 7535 | EMBD | 2017 | 31/03/2017 | active
4R-ANC | Airbus | A320-251N | A20N | 7663 | EMCG | 2017 | 30/06/2017 | active
4R-AND | Airbus | A320-251N | A20N | 7697 | KQEG | 2017 | 27/10/2017 | active
4R-ANE | Airbus | A320-251N | A20N | 7891 | KQGJ | 2017 | 01/12/2017 | active
4R-ANF | Airbus | A321-251N | A21N | 8106 | JSBF | 2018 | 28/07/2018 | active
Notes: Other useful data
Fleet data cont.
Example of airframes.org fleet data – details for SriLankan Airlines

## Slide 45: Other useful data
Purchase
required
A few examples of other useful data, and available sources cont.
Schedules
  Commercially available from OAG and Cirium
MCTs (minimum connecting times)
  Commercially available from OAG and Cirium
  MCT – shortest time required for pax (+baggage) to connect between flights
    ‘Standard’ MCTs for connections: domestic to domestic; domestic to international; international to domestic; international to international
    ‘MCT exceptions’ specify longer/shorter times, e.g. different terminals, bilateral airline agreements
Notes: Other useful data
Schedules and minimum connecting times are available from commercial suppliers
Published schedule is often available from the airport, but only helps if this is the focus of your study
MCTs = shortest time allowed for passengers (+baggage) to connect between flights; times don’t change very often
MCTs include standard times and exceptions (examples on next slide)

## Slide 46: Other useful data
MCT example – Munich Airport
Terminal | Connection type | MCTs (minutes)
Within Terminal 1 | Domestic to domestic | 35
 | Domestic to international | 
 | International to domestic | 
 | International to international | 
Within Terminal 2 | Domestic to domestic | 30
 | Domestic to international | 
 | International to domestic | 
 | International to international | 
Between Terminals | All | 45
Terminal | Connection type | Inbound connecting flight | Outbound connecting flight | MCT (minutes)
Within Terminal 1 | Dom. to dom. | Air Berlin arr. | All (except specified dep.) | 50
Within Terminal 1 | Dom. to dom. | All (except specified arr.) | Air Berlin dep. | 50
Within Terminal 1 | Int. to int. | Air Berlin AB 7000 - AB 7499 | S7 Airlines S7 4898 | 50
Within Terminal 2 | Int. to dom. | Lufthansa LH 7440 - LH 7599 | Lufthansa | 45
Within Terminal 2 | Int. to int. | United Airlines UA 9435 - UA 9464 | United Airlines | 40
Between Terminals | All | All (except specified arr.) | S7 Airlines S7 4893, S7 4898 | 60
None specified | Int. to int. | United Airlines UA 8694 - UA 9299 | United Airlines UA 9435 - UA 9464 | 30
Standard MCTs
MCT exceptions
Notes: Other useful data
Example MCTs for Munich Airport
Exceptions can specify longer/shorter times, e.g. bilateral airline agreements

## Slide 47: Other useful data
Aircraft utilisation (hours/day), and
Passenger load factors
  ICAO Data+
  Airline monthly bulletins and annual financial reports
Cancellations – traditionally difficult to estimate, but data becoming available (airline and airport)
  FlightAware (global)
  FlightStats (global)
  EUROCONTROL CODA operational cancellation data (30 airports)
  UK CAA Table 4a Cancelled movements and Punctuality statistics (UK only)
  Airline reporting
  US BTS agency ‘On-Time Arrival Performance’ (US only)
Notes: Other useful data
Suppliers of other types of data
Cancellations traditionally very hard to estimate, but now a few published sources available

## Slide 48: Other useful data
Cancellation examples
Published
FlightStats last 30 days reporting (06MAR19)
EUROCONTROL CODA (Q2 2018) can reveal trends and effects of strikes/extreme weather
Notes: Other useful data
Examples of cancellation data; specific and aggregated data

## Slide 49: Other useful data
Cancellation examples
Ryanair daily reporting
BTS monthly reporting
Published
Notes: Other useful data
Examples of cancellation data; specific and aggregated data

## Slide 50: Other useful data
Cancellation data – note rolling availability of certain datasets:
  FlightStats cancellation reporting available for the last 30 days (unless purchased)
  Ryanair flight cancellations available for the last 60 days
09MAY19
ATC strike
Notes: Other useful data
Example of plotted cancellation data from Ryanair

## Slide 51: Examples

## Slide 52: Cost of delay data sources
Overview of the data sources used for cost of delay calculation
  Previous reports and forthcoming edition
Element | Data sources
fleet | ICAO / Cirium
fuel | various / ad hoc
crew | various / ad hoc
maintenance | ICAO / Cirium
passenger | various / ad hoc
curfews | Domino project / EUROCONTROL
reactionary | EUROCONTROL / Mercury model

## Slide 53: POEM project model data sources
Variable | Data source |  | Variable | Data source |  | Variable | Data source
EOBT [OOOI] | PRISME |  | Planned en-route time | PRISME |  | Regulation delay mins | PRISME
ETOT [OOOI] | Derive |  | Actual en-route time variation | PRISME & internal variable |  | Regulation Reason | CFMU (via PRISME)
ETO [OOOI] | Estimate |  | PTI | Internal variable |  | Regulation Type | CFMU (via PRISME)
EIBT [OOOI] | PRISME |  | Arrival capacity constraints | Internal variable |  | Regulation Location | CFMU (via PRISME)
SOBT | PRISME |  | Airborne arrival management | Internal variable |  | Filed NM | PRISME
SIBT | Estimate |  | ATO [OOOI] | Internal variable & derive |  | Regulated NM | PRISME
CTOT | Derive |  | Taxi-in | CODA & internal variable |  | Actual NM | PRISME
Type of aircraft | PRISME |  | Taxi-in delay | Internal variable |  | Filed taxi time | PRISME
A/c registration | PRISME |  | AIBT [OOOI] | PRISME & internal variable |  | Regulated taxi time | PRISME
Wait for crew & turnaround | External sources & internal variable |  | Crew hours | Internal variable |  | WTC | PRISME
A/c ready for boarding | Internal variable |  | A/c-crew pairings | Internal variable |  | Pax delay cost algorithm | UoW & internal variable
ACRT | Internal variable |  | Dynamic list of pax waiting for onward destination | Internal variable |  | Non-pax delay cost algorithm | UoW & internal variable
Wait for boarding | Internal variable (uses MCTs) |  | Dynamic list of inbound delayed flights with connecting pax | Internal variable |  | Dep airport LAT coords | PRISME or other source
A/c ready for pushback | Internal variable |  | MCTs for all airports | IATA & internal variable |  | Dep airport LONG coords | PRISME or other source
ART | Internal variable |  | Seat numbers for all a/c types | IATA & internal variable |  | Arr airport LAT coords | PRISME or other source
Network capacity restrictions | Internal variable |  | Load factors | Multiple external sources & internal variable |  | Arr airport LONG coords | PRISME or other source
ETOT (new) | Internal variable |  | Dep airport | PRISME |  | En-route fuel burn by a/c type | ANCAT 3 or BADA
AOBT [OOOI] | PRISME & internal variable |  | Arr airport | PRISME |  | MTOW by a/c type | PRU or BADA
Taxi-out | CODA, PRISME & internal variable |  | AO | PRISME |  | TAS | PRISME or BADA
Taxi-out delay | Internal variable |  | NAT flight Y/N | PRISME |  | AO type | Derive
ATOT [OOOI] | Internal variable & derive |  |  |  |  |  | 
Notes: Sources already mentioned are highlighted; original source of data required per variable

## Slide 54: Data cleaning and preparation

## Slide 55: Data cleaning and preparation
A few hints:
  Matching IATA/ICAO codes
    Codes can change over time, so apply correct ones for your study period, e.g. recent airport changes 31OCT18 ‘IST’ IATA code was reassigned from Istanbul Atatürk Airport (ICAO ‘LTBA’) to the new Istanbul Airport (ICAO ‘LTFM’); Atatürk Airport now ‘ISL’ 25OCT20 new Berlin Brandenburg Airport (IATA ‘BER’); absorbs Berlin Schönefeld Airport as T5 and its ICAO code ‘EDDB’
    IATA airline codes (in particular) are re-used; also ‘controlled’ duplicate codes used in different regions, e.g. ‘N9’ Novair (Sweden) and Shree Airlines (Nepal)
Notes: Data cleaning and preparation
It’s rare to acquire a dataset and then start using it straightaway – normally some cleaning and preparation tasks are required
Watch out when matching IATA/ICAO codes: codes can be reused elsewhere (airports/airlines); legitimate duplication of codes can exist (airlines); complications matching one-to-many/many-to-one codes (aircraft)
Be aware if your study period spans a significant airport code change

## Slide 56: Data cleaning and preparation
A few hints:
  Matching IATA/ICAO codes
    Difficulty distinguishing between pax/cargo aircraft within an airline fleet e.g. IATA airline code ‘LH’ applies to both Lufthansa (ICAO ‘DLH’) and Lufthansa Cargo (ICAO ‘GEC’)
    Occasional coding ambiguity, e.g. ICAO aircraft codes Airbus 310 ‘A310’, cf. IATA codes ‘310’, ‘312’, 313’ and ‘31F’, ‘31X’, ‘31Y’ (cargo) Embraer 190-100 and 190-200 were both ‘E190’ until MAR17 when distinguished as ‘E190’ and ‘E195’ (IATA ‘E90’ and ‘E95’)
    Occasional coding oddities e.g. the Franco-Swiss EuroAirport (ICAO ‘LFSB’) has two IATA codes ‘MLH’ Mulhouse/Basel (EuroAirport French) ‘BSL’ Basel/Mulhouse (EuroAirport Swiss)
Notes: Data cleaning and preparation
If interested in a subset of a fleet (e.g. Airbus 310-200 pax, IATA ‘312’), will be difficult if dataset uses ICAO coding (‘A310’) and you’re missing tail numbers
Does the dataset have both EuroAirport codes, in which case you’ll underestimate whatever you’re interested in (pax, cargo, movements)

## Slide 57: Data cleaning and preparation
A few hints:
  Use consistent times
    Schedules in local time cf. operations in UTC
  Check study period for unusual disruption
    SEP17: French ATC strike; Air Berlin & Ryanair cancellations; Thomas Cook strike
    SEP19: 4 airlines cease or suspend operations (Thomas Cook, Adria Airways, XL Airways France & Aigle Azur ); British Airways & Ryanair strikes
  Not a trivial task!
Notes: Data cleaning and preparation
Watch out for time differences; operational traffic in UTC
Watch out for time periods containing disruption

## Slide 58: Data cleaning and preparation
Check the data! Coding errors
Notes: Data cleaning and preparation
Watch out for errors; range checks useful
Example shows a miscoded aircraft based on its registration – on the rotation highlighted, the aircraft coding changes from a B753 (Medium wake turbulence category) to a B763 (Heavy wake turbulence category)

## Slide 59: Data cleaning and preparation
Check the data! Difficulty matching schedule data with traffic data
  Blue Air flights between Cluj and Bucharest
    3 scheduled; 2 flown
    Was 1 cancelled or 1 delayed until the next day?
    Is flight 3 on-time (1945) or late (0800,1530)?
    Etc.
Flights | Departure times | 
 | Scheduled | Actual
1 | 0800 | 
2 | 1530 | 
3 | 1945 | 1945
? |  | 2330
Notes: Data cleaning and preparation
Watch out for when matching schedule times to traffic data
Example shows that 3 flights were scheduled but only 2 were flown on the day; when assigning the schedule to the 2 flown, which times should be used? What is the delay? You will have to decide your data cleaning rules.

## Slide 60: Data cleaning and preparation
Check the data! Non-revenue flights
  Not all flights are what they seem
    Although military/general aviation can be identified (potentially for exclusion)
    Test/training flights, positioning flights, flights to/from maintenance bases are less obvious to detect, e.g.
ADEP-ADES | Date | Time | A/C type | Callsign | Company | Reg
EGLL-EGFF | 140912 | 1208 | B772 | BAW9173 | BAW | GZZZB
EGFF-EGLL | 140912 | 1830 | B77W | BAW9171 | BAW | GSTBB
Heathrow - Cardiff (British Airways Maintenance Base)
ADEP-ADES | Date | Time | A/C type | Callsign | Company | Reg
LCLK-LCLK | 140912 | 0310 | A320 | CYP069 | CYP | 5BDCH
LSZH-LSZH | 140912 | 0815 | A321 | QTR9901 | QTR | A7ADY
GMMN-GMMN | 140912 | 0940 | A321 | AFR394S | AFR | FGMZA
EDHI-EDHI | 140912 | 0935 | A320 | AIB275B | AIB | DAVVV
Circular flights
Notes: Data cleaning and preparation
Watch out for non-passenger traffic; need to identify flights with no passengers, so as not to overestimate passenger capacity (for example)
Example shows 2 flights between Heathrow and Cardiff; BA aircraft going to/returning from planned maintenance – this is not a BA passenger route
Example shows circular flights (O/D is the same airport); various reasons for these, e.g. pilot training, test flights, tourist flights, etc.

## Slide 61: Data cleaning and preparation
Check the data! Coding errors
Ikaria Airport coordinates from two datasets!?
Notes: Data cleaning and preparation
Watch out for errors
Example shows incorrect coordinates in an official dataset

## Slide 62
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com