## Slide 1: Introduction to ATM Future concepts in ATM
Luis Delgado
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2
ANS
AS
FIS
ATC
ASM
ATFM
ATS
AIP
NOTAM
CIRC
CNS
MET
S&R
AIS
ATM
ANS: Air Navigation Services
CNS: Communications, Navigation and Surveillance
ATM: Air Traffic Management
S&R: Search and Rescue
AIS: Air Information Services
MET: Meteorological Services
ASM: AirSpace Management
ATFM: Air Traffic Flow Management
ATS: Air Traffic Services
AIP: Aeronautical Information Publications
NOTAM: Notices to Airmen
CIRC: Circulars
AS: Alert Services
FIS: Flight Information Services
ATC: Air Traffic Control
Introduction

## Slide 3: Introduction
ATM Airspace Users involvement

## Slide 4: Introduction
ATFM Phases
Strategic Phase Matches long-term demand and needed ATC capacity
Pre-tactical Phase Balances flights next day with available ATC Capacity
Tactical Phase Manage current flights with existing ATC capacity

## Slide 5: Introduction
Traffic in a challenging environment
  Lack of capacity leads to inefficiencies (delay, cost, environmental…)
  Many factors (ANSPs, airports, airspace users, passengers, environment)
  Trade-offs
  Regulated environment (regulatory bodies, political environment)
  Airspace users need, and want to be, involved in decision making
Flight
Passenger

## Slide 6: Introduction
Traffic demand evolution
  ‘Most-likely’ scenario of the STATFOR forecast 
  14.4 million flights in Europe in 2035, 1.5 x 2012 level
  Between 3.4 million and 5.2 million fewer flights in 2030 compared to the 2010 long-term forecasts
Shift of focus:
From capacity increment
To performance enhancement and airspace user involvement
SESAR SJU, European ATM Master Plan Executive View Edition 2015

## Slide 7: Introduction
Predictability
[CTOT-5 min, CTOT + 10 min]

## Slide 8: Introduction
Predictability
Valenzuela, A., Franco, A., Rivas, D., García-Heras, J. and Soler, M., Effects of Reducing Wind-Induced Trajectory Uncertainty on Sector Demand, SESAR Innovation days 2017

## Slide 9: Introduction
ATM Airspace Users involvement
Airspace User 1
Network
Manager
Airspace User i
Airspace User N
Flight Plan 1
Ground delay 1
Flight Plan i
Ground delay i
Flight Plan N
Ground delay N

## Slide 10: Introduction
ATM Airspace Users involvement
?
Minimise delay
Maintain fairness (RBS)
Consider user preferences
Involve user in management
Congestion

## Slide 11: Introduction
ATM Airspace Users involvement
  Some CDM already used:
    Slot swapping – User Driven Prioritisation Process (UDPP)
    ATFM regulation messages
    A-CDM (Turn-around processes)
  New technological changes might help to improve the possibilities
Trajectory negotiation

## Slide 12: Introduction
Modernisation of CNS and ATM procedures
C: Voice communications
N: Not precise execution, nor prediction
S: Non-cooperative (ground-based)
ATM: Focus on Capacity management
C: Digital communications (data-link, SWIM)
N: 4D trajectory precision (also prediction)
S: Cooperative (aircraft send their position)
ATM: Trajectory Based Operations (TBO)

## Slide 13: User involvement on ATFM management – US example

## Slide 14
Ground Delay Program – Basic Algorithm
ATC specialist
monitors the demand and capacity

## Slide 15
Ground Delay Program – Basic Algorithm
ATC specialist
monitors the demand and capacity
Model the GDP using FSM
(Flight Schedule Monitor)
If capacity-demand imbalance

## Slide 16
Ground Delay Program – Basic Algorithm
Send advisory
to all airlines
before implementing
the GDP
If time
allows
ATC specialist
monitors the demand and capacity
Model the GDP using FSM
(Flight Schedule Monitor)
If capacity-demand imbalance

## Slide 17
Ground Delay Program – Basic Algorithm
Send advisory
to all airlines
before implementing
the GDP
If time
allows
ATC specialist
monitors the demand and capacity
Model the GDP using FSM
(Flight Schedule Monitor)
If capacity-demand imbalance
Airlines check the
impact of this proposed
GDP on their operations:
might opt to cancel some
flights

## Slide 18
Ground Delay Program – Basic Algorithm
Send advisory
to all airlines
before implementing
the GDP
If time
allows
ATC specialist
monitors the demand and capacity
Model the GDP using FSM
(Flight Schedule Monitor)
If capacity-demand imbalance
Airlines check the
impact of this proposed
GDP on their operations:
might opt to cancel some
flights
If needed
Implement the
GDP

## Slide 19
Ground Delay Program – Basic Algorithm
Implement the
GDP
Runs a RBS
algorithm
Apply the GDP
program
Issue CTA and
CTD
Airline gets CTA
and CTD

## Slide 20
Ground Delay Program – Basic Algorithm
Airline gets CTA
And CTD
New Slot Allocation
List
Cancel and
Substitution of flights
Compression
Airline gets CTA
and CTD

## Slide 21
Issue CTA and
CTD
If capacity-demand
imbalance
If time
allows
Ground Delay Program – Basic Algorithm
New Slot Allocation
List
Cancel and
Substitution of flights
Airline gets CTA
and CTD
ATC specialist
monitors the demand and capacity
Model the GDP using FSM
(Flight Schedule Monitor)
If needed
Implement the
GDP
Airlines check the
impact of this proposed
GDP on their operations:
might opt to cancel some
flights
Send advisory
to all airlines
before implementing
the GDP
Runs a RBS
algorithm
Airline gets CTA
and CTD
Apply the GDP
program
Compression
- GDP might be reviewed if conditions changes. Revisions may lead to substitutions, cancellations and compression.
- GDP ends when GDP Ends time is reached, or the GDP is cancelled.
[Manley, 2008]

## Slide 22
Ground Delay Program – Basic Algorithm
Slot | Flight | Delay
10h00-10h02 |  | 
10h03-10h04 |  | 
10h05-10h06 |  | 
10h07-10h08 |  | 
10h09-10h10 |  | 
10h11-10h12 |  | 
10h13-10h14 |  | 
10h15-10h16 |  | 
10h17-10h18 |  | 
10h19-10h20 |  | 
10h21-10h22 |  | 
10h23-10h24 |  | 
10h25-10h26 |  | 
10h27-10h28 |  | 
10h29-10h30 |  | 
GDP example:
AAR: 30 ac/hour
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6

## Slide 23
Ground Delay Program – Basic Algorithm
Slot | Flight | Delay
10h00-10h02 | A1_F1 | 0
10h03-10h04 |  | 
10h05-10h06 |  | 
10h07-10h08 |  | 
10h09-10h10 |  | 
10h11-10h12 |  | 
10h13-10h14 |  | 
10h15-10h16 |  | 
10h17-10h18 |  | 
10h19-10h20 |  | 
10h21-10h22 |  | 
10h23-10h24 |  | 
10h25-10h26 |  | 
10h27-10h28 |  | 
10h29-10h30 |  | 
GDP example:
AAR: 30 ac/hour
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6

## Slide 24
Ground Delay Program – Basic Algorithm
Slot | Flight | Delay
10h00-10h02 | A1_F1 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 |  | 
10h07-10h08 |  | 
10h09-10h10 |  | 
10h11-10h12 |  | 
10h13-10h14 |  | 
10h15-10h16 |  | 
10h17-10h18 |  | 
10h19-10h20 |  | 
10h21-10h22 |  | 
10h23-10h24 |  | 
10h25-10h26 |  | 
10h27-10h28 |  | 
10h29-10h30 |  | 
GDP example:
AAR: 30 ac/hour
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6

## Slide 25
Ground Delay Program – Basic Algorithm
Slot | Flight | Delay
10h00-10h02 | A1_F1 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F2 | 3
10h07-10h08 |  | 
10h09-10h10 |  | 
10h11-10h12 |  | 
10h13-10h14 |  | 
10h15-10h16 |  | 
10h17-10h18 |  | 
10h19-10h20 |  | 
10h21-10h22 |  | 
10h23-10h24 |  | 
10h25-10h26 |  | 
10h27-10h28 |  | 
10h29-10h30 |  | 
GDP example:
AAR: 30 ac/hour
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6

## Slide 26
Ground Delay Program – Basic Algorithm
GDP example:
AAR: 30 ac/hour
Slot | Flight | Delay
10h00-10h02 | A1_F1 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F2 | 3
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A1_F5 | 7
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6

## Slide 27
Slot | Flight | Delay
10h00-10h02 | A1_F1 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F2 | 3
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A1_F5 | 7
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7
Ground Delay Program – Basic Algorithm
Substitutions
Cancelations
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6

## Slide 28
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F1 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F2 | 3
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A1_F5 | 7
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 29
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 3
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A1_F5 | 7
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 30
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A1_F5 | 7
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 31
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A1_F5 | 7
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 32
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 33
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F2 | 8
10h13-10h14 | A2_F3 | 9
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 34
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A2_F2 | 10
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 35
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A2_F2 | 10
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 36
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | Cancel | 
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 37
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | Cancel | 
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 38
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | Cancel | 
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 39
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | Cancel | 
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 40
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | Cancel | 
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7

## Slide 41
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | Cancel | 
10h15-10h16 | A3_F2 | 9
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7
Compression

## Slide 42
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 |  | 
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7
Compression

## Slide 43
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 |  | 
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7
Compression

## Slide 44
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 |  | 
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 | A2_F4 | 11
10h29-10h30 | A1_F6 | 7
Compression

## Slide 45
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 | A2_F4 | 0
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 |  | 
10h29-10h30 | A1_F6 | 7
Compression

## Slide 46
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 | A2_F4 | 0
10h17-10h18 | A1_F4 | 7
10h19-10h20 | Cancel | 
10h21-10h22 | A4_F1 | 6
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 |  | 
10h29-10h30 | A1_F6 | 7
Compression

## Slide 47
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 | A2_F4 | 0
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A4_F1 | 4
10h21-10h22 |  | 
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 |  | 
10h29-10h30 | A1_F6 | 7
Compression

## Slide 48
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 | A2_F4 | 0
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A4_F1 | 4
10h21-10h22 |  | 
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 |  | 
10h29-10h30 | A1_F6 | 7
Compression

## Slide 49
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 | A2_F4 | 0
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A4_F1 | 4
10h21-10h22 |  | 
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 |  | 
10h29-10h30 | A1_F6 | 7
Compression

## Slide 50
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 | A2_F4 | 0
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A4_F1 | 4
10h21-10h22 | A1_F6 | 0
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 |  | 
10h29-10h30 |  | 
Compression

## Slide 51
Ground Delay Program – Basic Algorithm
Scheduled time | Flight
10h01 | A1_F1
10h02 | A2_F1
10h02 | A1_F2
10h02 | A3_F1
10h03 | A1_F3
10h03 | A2_F2
10h04 | A2_F3
10h06 | A3_F2
10h10 | A1_F4
10h12 | A1_F5
10h15 | A4_F1
10h15 | A3_F3
10h15 | A4_F2
10h16 | A2_F4
10h21 | A1_F6
Slot | Flight | Delay
10h00-10h02 | A1_F2 | 0
10h03-10h04 | A2_F1 | 1
10h05-10h06 | A1_F1 | 4
10h07-10h08 | A3_F1 | 5
10h09-10h10 | A1_F3 | 6
10h11-10h12 | A2_F3 | 7
10h13-10h14 | A3_F2 | 7
10h15-10h16 | A2_F4 | 0
10h17-10h18 | A1_F4 | 7
10h19-10h20 | A4_F1 | 4
10h21-10h22 | A1_F6 | 0
10h23-10h24 | A3_F3 | 8
10h25-10h26 | A4_F2 | 10
10h27-10h28 |  | 
10h29-10h30 |  | 

## Slide 52: SESAR Solutions

## Slide 53: SESAR operations
Trajectory oriented
European ATM Master Plan - Executive View. Ed. 2015

## Slide 54: SESAR operations
European ATM Master Plan - Executive View. Ed. 2015

## Slide 55: Trajectory Based Operations

## Slide 56: TBO
FAA 7233-4, Pre-Flight Pilot Checklist and International Flight Plan, July 15, 2015
Current Flight Plan

## Slide 57: TBO
Current Flight Plan Uncertainties
FMS
Better precession
(4D time window)

## Slide 58: TBO – Initial 4D flights (i4D)
Share and integrate data optimising aircraft trajectories in 4D
Controller workload can be optimised, conflicts between trajectories can be detected and solved automatically
Arrival planning aircraft can autonomously manage arrival obtaining fuel savings
2012 and 2014 first i4D flight trials
Time window
Time window
Time window
Time window
Time window
Time window
Time window
European ATM Master Plan - Executive View. Ed. 2015

## Slide 59: TBO – 4D Trajectories
NextGen defines 4DT as precise description of aircraft path in space and time. Centreline of path with WP with appropriate buffers to describe position uncertainty.
The required level of specificity of the 4DT depends on the flight-operating environment. Use of Controlled Time of Arrivals (CTAs)
CTAs represent time windows for aircraft to cross waypoints and they are used to regulate traffic flows entering congested spaces
Technology required to implement TBO
  Advanced FMS capabilities
  Data communications
  ADS-B
  Air Traffic Control Decision Support Tools
G. Enea , M. Porretta, A comparison of 4D-trajectory operations envisioned for NextGen and SESAR, some preliminary findings, 28th ICAS; 2012

## Slide 60: TBO – Trajectories management
TBO implies sharing of same information via SWIM and datalink between airborne and ground factors
Flight and flow centric operations will be possible at network level (eg. sector less operations)
Airspace configurations dynamically adjusted to demand
Controllers working on flows rather than individual flights
European ATM Master Plan - Executive View. Ed. 2015

## Slide 61: TBO – Trajectories management
European ATM Master Plan - Executive View. Ed. 2015

## Slide 62: TBO – Trajectories management
Collaborative NOP with increased integration of NOP an AOP information
  Exchange between the NM and operational stakeholders to cover all trajectory lifecycle
Calculated take-of time to target times (CTOT to TTA) for ATFM will be applied to selected flights in order to manage ATFCM at point of congestion rather than only at departure.
European ATM Master Plan - Executive View. Ed. 2015
Congested airspace
TTA

## Slide 63: TBO – Trajectories management
Stakeholders interaction
Based on: SESAR CONSORTIUM. 2006 (July). SESAR Definition Phase - Deliverable 3 – The ATM Target Concept Tech. rept. SESAR Consortium.
Airspace User 1
Network
Manager
Airspace User i
Airspace User N
Flight Plan 1
Ground delay 1
Flight Plan i
Ground delay i
Flight Plan N
Ground delay N

## Slide 64: TBO – Trajectories management
Based on: SESAR CONSORTIUM. 2006 (July). SESAR Definition Phase - Deliverable 1 - Air Transport Framework The Current Situation - The Market. Tech. rept. SESAR Consortium.

## Slide 65: TBO – Trajectories management
AU assume the compromise of flying the trajectory planned for the full flight with enough precision in the 4 dimensions (3D + time), and the ATM services agree to facilitate.

## Slide 66: TBO – Trajectories management
Flights operating as close as possible to optimum trajectory
Constraints with agreement on modifications on 4D trajectory
Time-based separations

## Slide 67: TBO – Time adherence
Separation needs to take time adherence into account
H. Hof, R. Flohr, O. Nunez, R. Garrity, ICAO working paper– Air Traffic Management Requirements and Performance Panel (ATMRPP) - 27th Working group meeting – Trajectory Based Operation (TBO) – Time adherence in TBO, 14 October 2014

## Slide 68: TBO – Time adherence
Arrivals
H. Hof, R. Flohr, O. Nunez, R. Garrity, ICAO working paper– Air Traffic Management Requirements and Performance Panel (ATMRPP) - 27th Working group meeting – Trajectory Based Operation (TBO) – Time adherence in TBO, 14 October 2014
Delay parameters related to arrival management

## Slide 69: TBO – Time adherence
H. Hof, R. Flohr, O. Nunez, R. Garrity, ICAO working paper– Air Traffic Management Requirements and Performance Panel (ATMRPP) - 27th Working group meeting – Trajectory Based Operation (TBO) – Time adherence in TBO, 14 October 2014
Evolution of variance in arrival time deviations
Arrivals

## Slide 70: TBO – Time adherence
H. Hof, R. Flohr, O. Nunez, R. Garrity, ICAO working paper– Air Traffic Management Requirements and Performance Panel (ATMRPP) - 27th Working group meeting – Trajectory Based Operation (TBO) – Time adherence in TBO, 14 October 2014
RTA tolerance level that serves complexity management
Time window required

## Slide 71: TBO – Time adherence
H. Hof, R. Flohr, O. Nunez, R. Garrity, ICAO working paper– Air Traffic Management Requirements and Performance Panel (ATMRPP) - 27th Working group meeting – Trajectory Based Operation (TBO) – Time adherence in TBO, 14 October 2014
RTA tolerance level that serves complexity management
Time window required

## Slide 72: TBO – Time adherence
H. Hof, R. Flohr, O. Nunez, R. Garrity, ICAO working paper– Air Traffic Management Requirements and Performance Panel (ATMRPP) - 27th Working group meeting – Trajectory Based Operation (TBO) – Time adherence in TBO, 14 October 2014
Flexibility
Predictability
Width of target window
Time window required

## Slide 73: TBO – Time adherence
H. Hof, R. Flohr, O. Nunez, R. Garrity, ICAO working paper– Air Traffic Management Requirements and Performance Panel (ATMRPP) - 27th Working group meeting – Trajectory Based Operation (TBO) – Time adherence in TBO, 14 October 2014
Time window required

## Slide 74: Uncertainties – trade-offs
Predictability trade-offs
A. Franco, D. Rivas, A. Valenzuela, Optimal Aircraft Path Planning in a Structured Airspace Using Ensemble Weather Forecasts -- -- 8th SESAR Innovation Days – Salzburg – 3rd – 7th December 2018

## Slide 75: Free routes

## Slide 76: Free routes
European ATM Master Plan - Executive View. Ed. 2015

## Slide 77: Free routes
Use of structure airspace with restrictions
  Longer routes than necessary (horizontal inefficiency)
  Higher fuel consumption
  Higher environmental impact
  Constrained airspace users’ preferences

## Slide 78: Free routes
Airspace within which aircraft operators may plan a route freely between a defined entry point and a defined exit point, with the possibility of deviating via intermediate navigation points without reference to the fixed route network.
Within this airspace, flights remain at all times subject to air traffic control and to any overriding airspace restrictions.
Entry point
Entry point
Exit point
Exit point
Exit point
Free routes ≠ Free flight
http://www.eurocontrol.int/articles/free-route-airspace

## Slide 79: Free routes
Shortest route not always most efficient
Free-route trajectory might be longer but user-preferred

## Slide 80: Free routes
Pre-defined direct (DCT) routes operated at specified times
User Preferred Routing (UPR), AU define route non-defined according to published route segments
Entry point
Entry point
Exit point
Exit point
Exit point
User Preferred Routing - Initial VALR (Step 1 V3), 2013

## Slide 81: Free routes – Benefits
Airspace users
  Save as much as 25,000 NM a day
  Flying distances reduced by 7.5 million NM, representing 45,000 tons of fuel
ANSPs
  Improved predictability (more stable trajectories)
  Better spread of conflicts
http://www.eurocontrol.int/articles/free-route-airspace

## Slide 82: Free routes – Difficulties
Less structured traffic
Higher spread of conflicts
More difficult interoperability between factors (i.e. civil and military coordination)
Potential reduction of capacity
Need of interstate coordination

## Slide 83: Free routes – Implementation
By the end of 2017, 51 ACCs some degree of Free Route Airspace operations
By the end of 2019 most European airspace is expected to have implemented FRA
By 2021/2022 all airspace having this type of operations
Cross-border implementation (implementation on incremental basis State  cross border)
  SAXFRA (Austria/Slovenia)
  SEENFRA (Romania/Hungary/Bulgaria)
  SEAFRA (Belgrade/Zagreb ACCs)
  MALTA/ITALY
  NEFRA (Estonia/Latvia/Finland/Sweden/Denmark/Norway)
Europe is first region in the world to have implemented full FRA concept
http://www.eurocontrol.int/articles/free-route-airspace

## Slide 84: Conclusions
Airline
Operating
Centre
Flight
Airport
Airspace
Management
Passenger
Airline
Operating
Centre
Airline
Operating
Centre
Airport
Airport
Airport
Airspace
Management
Airspace
Management
Flight
Flight
Flight
Flight
Passenger
Passenger
Passenger
Passenger

## Slide 85: Free routes – Implementation
http://www.eurocontrol.int/publications/free-route-airspace-fra-implementation-projections

## Slide 86: Free routes – Examples
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011

## Slide 87: Free routes – Examples
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011

## Slide 88: Free routes – Examples
BUMIL
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011

## Slide 89: Free routes – Examples
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011

## Slide 90: Free routes – Examples
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011

## Slide 91: Free routes – Examples
Tallin – London
274 NM vs.285 NM
GAIN 11 NM (20 km)
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011

## Slide 92: Free routes – Examples
Stansted – Rygge (Norway)
246 NM vs. 268 NM
GAIN 22 NM (41 km)
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011

## Slide 93: Free routes – Examples
A few concrete examples of the gains brought about by FRAM, As the crow flies, Free Route Airspace Maastricht presentation, 2011
Hamburg – Paris
229 NM vs. 244 NM
GAIN 15 NM
(28 km)

## Slide 94: Free routes – Examples
Cross-border cooperation
Free Route Airspace Maastricht and Karlsruhe (FRAMaK) Project
FRAMAK - Final Project Report (Demonstration Report) , 2014
http://www.sesarju.eu/newsroom/brochures-publications/framak-project-final-report

## Slide 95
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com